## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Module 2 ARRL General Class Chapter 2 – Procedures and Practices (2.1, 2.2) HF Operating Techniques, Emergency Operation

## Slide 4: HF Operating Techniques
Technician class operators focus skills for VHF and higher bands
  Although 10 meters (voice) and 80, 40, and 15 meters (CW) are HF options for technicians
General class operators have the advantage of using HF
  A General license opens up many more frequencies, modes, and activities

## Slide 5: Selecting a Frequency
Check FCC Part 97 for frequency & mode restrictions
  Refer to Band Plan in Module 1 (http://www.arrl.org/graphical-frequency-allocations)
On HF, perfectly clear channels are rare
Goal: Find a frequency that minimizes interference to adjacent stations (and, vice versa) – see recommended signal separation table …
RECOMMENDED SIGNAL SEPARATION
CW: 150-500 Hz
SSB: 2.5-3 kHz
RTTY: 250-500 Hz
PSK31: 150-500 Hz

## Slide 6: Selecting a Frequency (cont.)
Once frequency is found, check if other station is using it …
  Listen for 10-20 seconds ... then …
    Voice Mode: Is this frequency in use? This is [your call].
    CW/Digital Modes: QRL? DE [your call].
Frequency selection summary …
  Confirm frequency is authorized for your license privileges
  Follow the band plan under normal circumstances
  Listen to avoid interfering with ongoing communications

## Slide 7: Split / Dual Frequency Operation
When a rare or interesting station is on the air with many calling stations, it’s common to operate split …
  Set transceiver to listen on one frequency and transmit on another
  Allows for more orderly/effective operating
  Doesn’t work on all transceivers
  Referred to as a dual-VFO feature on a transceiver

## Slide 8: More Info … HF Operating Techniques
HF equipment is designed for continuous tuning. The control used for continuous tuning is called a VFO or Variable Frequency Oscillator
  The minimum frequency change is called step size or step rate
For short-range contacts, use 80 or 40 meters
  Using long-distance bands for short-range contacts needlessly occupies precious radio spectrum space (signal will be heard over much wider range than you’re using)
Longer range contacts, use 30 through 10 meters

## Slide 9
Band-by-Band Frequency Guide
General Class License Manual, Ninth Edition, Page 2-3

## Slide 10: PRACTICE QUESTIONS

## Slide 11: When choosing a transmitting frequency, what should you do to comply with good amateur practice?
Ensure that the frequency and mode selected are within your license class privileges
Follow generally accepted band plans agreed to by the Amateur Radio community
Monitor the frequency before transmitting
All these choices are correct
G1B08 (D) [97.101(a)] Page 2-4
11

## Slide 12: Which of the following is true concerning access to frequencies?
Nets always have priority
QSOs in progress always have priority
Except during emergencies, no amateur station has priority access to any frequency
Contest operations must always yield to non-contest use of frequencies
G2B01 (C) [97.101(b), (c)] Page 2-2
12

## Slide 13: What is good amateur practice if propagation changes during a contact and you notice interference from other stations on the frequency?
Tell the interfering stations to change frequency
Report the interference to your local Amateur Auxiliary Coordinator
Attempt to resolve the interference problem with the other stations in a mutually acceptable manner
Increase power to overcome interference
G2B03 (C) Page 2-4
13

## Slide 14: When selecting a CW transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies?
5 to 50 Hz
150 to 500 Hz
1 to 3 kHz
3 to 6 kHz
G2B04 (B) Page 2-2
14

## Slide 15: When selecting an SSB transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies?
5 to 50 Hz
150 to 500 Hz
Approximately 3 kHz
Approximately 6 kHz
G2B05 (C) Page 2-2
15

## Slide 16: What is a practical way to avoid harmful interference on an apparently clear frequency before calling CQ on CW or phone?
Send “QRL?” on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign
Listen for 2 minutes before calling CQ
Send the letter “V” in Morse code several times and listen for a response, or say “test” several times and listen for a response
Send “QSY” on CW or if using phone, announce “the frequency is in use,” then give your call sign and listen for a response
G2B06 (A) Page 2-2
16

## Slide 17: Which of the following complies with good amateur practice when choosing a frequency on which to initiate a call?
Check to see if the channel is assigned to another station
Identify your station by transmitting your call sign at least 3 times
Follow the voluntary band plan for the operating mode you intend to use
All these choices are correct
G2B07 (C) Page 2-2
17

## Slide 18: What does the Q signal “QRL?” mean?
“Will you keep the frequency clear?”
“Are you operating full break-in?” or “Can you operate full break-in?”
“Are you listening only for a specific station?”
“Are you busy?” or “Is this frequency in use?”
G2C04 (D) Page 2-2
18

## Slide 19: Which of the following are examples of the NATO Phonetic Alphabet?
Able, Baker, Charlie, Dog
Adam, Boy, Charles, David
America, Boston, Canada, Denmark
Alpha, Bravo, Charlie, Delta
G2D07 (D) Page 2-2
19

## Slide 20: What is normally meant by operating a transceiver in “split” mode?
The radio is operating at half power
The transceiver is operating from an external power source
The transceiver is set to different transmit and receive frequencies
The transmitter is emitting an SSB signal, as opposed to DSB operation
G4A03 (C) Page 2-4
20

## Slide 21: Which of the following is a common use for the dual-VFO feature on a transceiver?
To allow transmitting on two frequencies at once
To permit full duplex operation — that is, transmitting and receiving at the same time
To permit monitoring of two different frequencies
To facilitate computer interface
G4A12 (C) Page 2-4
21

## Slide 22: Making Contacts
Calling CQ is rare on VHF/UHF FM channels, but it is how many contacts are initiated on HF
To call CQ on phone/voice …
  “CQ CQ CQ, this is [your call repeated a few times with phonetics]”
  Pause for a response
  If no response, repeat your CQ
To call CQ on CW …
  “CQ CQ CQ DE [your call without phonetics]”

## Slide 23: Making Contacts, CQ Variations
CQ DX (DX means distant stations)
  If you hear CQ DX from a station on the US mainland, it means the person calling is looking for stations outside the lower 48 states
  On HF, it generally refers to any station outside the caller’s country
During CQ contests, you’ll generally hear …
  “CQ Contest”, “CQ test”, or “CQ from special event station”
CQ for stations from certain areas …
  “CQ North America” or “CQ California”

## Slide 24: Joining an Ongoing QSO (Contact)
Joining a QSO (also called breaking in) is common
On phone/voice, just say your call sign
On CW or digital modes, send BK (break) followed by your call sign
Same rules apply during contests and competitive events

## Slide 25: Logging Contacts
Although no longer required, most amateurs keep a log to verify contacts for awards and to record items of interest – see NOTE below
Typical log: time, date, frequency or band, mode of the contact (USB, PSK, etc.), call sign, signal reports, names, and equipment used
Can be useful in providing info requested by the FCC
NOTE: If you operate on 60 meters with any antenna other than a dipole, the FCC requires you to keep a record of the antenna gain calculations or manufacturer’s data (ensures you meet the 100 W ERP restrictions).

## Slide 26: Managing Interference
Interference is going to occur on HF …
  Frequencies aren’t channelized
  There are many amateurs using the frequencies
  Occurs due to crowding, propagation, personal choice, atmospheric conditions, and consumer electronics
Learning how to make contacts under these conditions is part of becoming a good operator

## Slide 27: Types of Interference
Harmful
  Defined by FCC 97.3(a)(23) as “interference which … seriously degrades, obstructs or repeatedly interrupts a radio communication service operating in accordance with the Radio Regulations”
    It’s not always illegal, but needs to be resolved to keep communicating
Malicious, deliberate or willful
  Specifically forbidden by FCC 97.101(d)

## Slide 28: Avoiding Interference
Learn what bands are crowded and when
Learn characteristics of each band (propagation & noise)
Learn how to use your equipment (understand strengths & weaknesses)
Check published calendars for major operating events

## Slide 29: Reacting to Interference
Be flexible … no one has a claim to any frequency
Have a back-up plan (especially for scheduled events)
  Do this in advance!
Keep a cool head … don’t allow harmful interference to turn into deliberate interference!

## Slide 30: PRACTICE QUESTIONS

## Slide 31: Which of the following is required by the FCC rules when operating in the 60-meter band?
If you are using an antenna other than a dipole, you must keep a record of the gain of your antenna
You must keep a record of the date, time, frequency, power level, and stations worked
You must keep a record of all third-party traffic
You must keep a record of the manufacturer of your equipment and the antenna used
G1C12 (A) [97.303(i)] Page 2-6
31

## Slide 32: What is the recommended way to break in to a phone contact?
Say “QRZ” several times, followed by your call sign
Say your call sign once
Say “Breaker Breaker”
Say “CQ” followed by the call sign of either station
G2A08 (B) Page 2-5
32

## Slide 33: Generally, who should respond to a station in the contiguous 48 states who calls “CQ DX”?
Any caller is welcome to respond
Only stations in Germany
Any stations outside the lower 48 states
Only contest stations
G2A11 (C) Page 2-5
33

## Slide 34: What is the voluntary band plan restriction for U.S. stations transmitting within the 48 contiguous states in the 50.1 to 50.125 MHz band segment?
Only contacts with stations not within the 48 contiguous states
Only contacts with other stations within the 48 contiguous states
Only digital contacts
Only SSTV contacts
G2B08 (A) Page 2-5
34

## Slide 35: Which of the following is a good way to indicate on a clear frequency in the HF phone bands that you are looking for a contact with any station?
Sign your call sign once, followed by the words “listening for a call” -- if no answer, change frequency and repeat
Say “QTC” followed by “this is” and your call sign -- if no answer, change frequency and repeat
Repeat “CQ” a few times, followed by “this is,” then your call sign a few times, then pause to listen, repeat as necessary
Transmit an unmodulated carried for approximately 10 seconds, followed by “this is” and your call sign, and pause to listen -- repeat as necessary
G2D05 (C) Page 2-5
35

## Slide 36: What is a reason why many amateurs keep a station log?
The ITU requires a log of all international contacts
The ITU requires a log of all international third-party traffic
The log provides evidence of operation needed to renew a license without retest
To help with a reply if the FCC requests information
G2D08 (D) Page 2-6
36

## Slide 37: Which of the following is required when participating in a contest on HF frequencies?
Submit a log to the contest sponsor
Send a QSL card to the stations worked, or QSL via Logbook of The World
Identify your station per normal FCC regulations
All these choices are correct
G2D09 (C) Page 2-5
37

## Slide 38: Modes
CW (continuous wave) … found in lower ranges for each HF band. However, CW can be transmitted anywhere on HF.
AM & SSB (single-side band)
  SSB is the most common voice mode or phone signal
  Has displaced AM as the preferred HF voice modulation method
  SSB signals use less spectrum space than AM (3 kHz vs. 6 kHz … this increases efficiency … results in SSB having a greater range than AM

## Slide 39: Modes (cont.)
USB vs. LSB (upper and lower side band)
  Good amateur practices is to use USB above 9 MHz (20 thru 10 meters) and LSB elsewhere except on 60 meters
    USB is used on VHF and UHF
FM is generally not used on HF because higher noise hurts intelligibility
  Exception: FM repeaters can be found on the higher frequencies of 10 meters (above 29 MHz) where cross-continent and DX contacts can be made when the band is open

## Slide 40: Modes (cont.)
Digital Voice …
  Relatively new on HF bands
  Operator’s voice converted to and from a digital stream via modem or sound card. Modem connects to a regular SSB transceiver.
  Fidelity comparable to regular SSB signals, but less affected by fading
  Most popular digital voice modes: FreeDV and protocol developed by G4GUO (Charles Brain)

## Slide 41: Modes (cont.)
Digital Modes …
  Packet radio common on VHF and UHF to exchange digital data, but also common on HF
  FT8: Most popular
  FT8, PSK63 and PSK31: Effective at low power levels … all widely used
  RTTY: Oldest, and still common (radioteletype)
  PACTOR or WINMOR: Used for semi-automatic and automatic messaging for small files

## Slide 42: Modes (cont.)
Image Modes
  Image mode transmissions on HF encode photos & graphics to tones
  These tones are reconstructed as an image on a display
  Image modes are allowed on same frequencies as voice, except for 60 meters
  Most common image mode: Slow-scan television (SSTV)
    Called slow because each image takes several seconds
  Fast-scan amateur television (ATV) allows full motion video
    Restricted to 432 MHz and higher frequency bands (due to wide bandwidth)

## Slide 43: Mode Comparison
More details in Chapters 5 & 6

## Slide 44: HF Receiving
On VHF, FM receivers have 3 basic controls …
  Frequency (channel), squelch, volume
SSC/CW receivers have additional controls to accommodate non-channelized, continuous-tuning operation (must be able to receive signals in the presence of noise and interference from adjacent channels) … for examples …
  Selectivity: Ability to discriminate between closely-spaces signals
  Sensitivity: Ability to detect a signal

## Slide 45: Signal Reporting
Usually exchanged between stations at beginning of a contact
Most common is RST
  Readability: Scale of 1 to 5 (5 = best)
  Strength: Scale of 1 to 9 (9 = best)
  Tone: Also 1 to 9 scale. Only used for CW and digital mode contacts.
    Indicates signal purity
    Values less than 9 indicate some kind of transmitter problem
  A C added after RST indicates an unstable signal or chirp

## Slide 46: PRACTICE QUESTIONS

## Slide 47: Which sideband is most commonly used for voice communications on frequencies of 14 MHz or higher?
Upper sideband
Lower sideband
Vestigial sideband
Double sideband
G2A01 (A) Page 2-9
47

## Slide 48: Which of the following modes is most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands?
Upper sideband
Lower sideband
Vestigial sideband
Double sideband
G2A02 (B) Page 2-9
48

## Slide 49: Which of the following is most commonly used for SSB voice communications in the VHF and UHF bands?
Upper sideband
Lower sideband
Vestigial sideband
Double sideband
G2A03 (A) Page 2-9
49

## Slide 50: Which mode is most commonly used for voice communications on the 17-meter and 12-meter bands?
Upper sideband
Lower sideband
Vestigial sideband
Double sideband
G2A04 (A) Page 2-9
50

## Slide 51: Which mode of voice communication is most commonly used on the HF amateur bands?
Frequency modulation
Double sideband
Single sideband
Phase modulation
G2A05 (C) Page 2-9
51

## Slide 52: Which of the following is an advantage when using single sideband, as compared to other analog voice modes on the HF amateur bands?
Very high fidelity voice modulation
Less subject to interference from atmospheric static crashes
Ease of tuning on receive and immunity to impulse noise
Less bandwidth used and greater power efficiency
G2A06 (D) Page 2-9
52

## Slide 53: Which of the following statements is true of the single sideband voice mode?
Only one sideband and the carrier are transmitted; the other sideband is suppressed
Only one sideband is transmitted; the other sideband and carrier are suppressed
SSB is the only voice mode that is authorized on the 20-meter, 15-meter, and 10-meter amateur bands
SSB is the only voice mode that is authorized on the 160-meter, 75-meter, and 40-meter amateur bands
G2A07 (B) Page 2-9
53

## Slide 54: Why do most amateur stations use lower sideband on the 160-meter, 75-meter, and 40-meter bands?
Lower sideband is more efficient than upper sideband at these frequencies
Lower sideband is the only sideband legal on these frequency bands
Because it is fully compatible with an AM detector
It is good amateur practice
G2A09 (D) Page 2-9
54

## Slide 55: HF Transmitting – PHONE
Putting transceiver into transmit mode is called keying the transmitter
  The PTT (push-to-talk) button works the same as on FM
Some HF operators use voice-operated transmit or VOX
  Allows hands-free operation

## Slide 56: HF Transmitting – CW
Prosign reference: http://www.radiotelegraphy.net/prosigns.htm

## Slide 57: CW Additional Information
FISTS: www.fists.org
CWOps: www.cwops.org
ARRL: www.arrl.org/cw-mode

## Slide 58: PRACTICE QUESTIONS

## Slide 59: Which of the following statements is true of voice VOX operation versus PTT operation?
The received signal is more natural sounding
It allows “hands free” operation
It occupies less bandwidth
It provides more power output
G2A10 (B) Page 2-12
59

## Slide 60: Which of the following describes full break-in telegraphy (QSK)?
Breaking stations send the Morse code prosign “BK”
Automatic keyers, instead of hand keys, are used to send Morse code
An operator must activate a manual send/receive switch before and after every transmission
Transmitting stations can receive between code characters and elements
G2C01 (D) Page 2-13
60

## Slide 61: What should you do if a CW station sends “QRS?”
Send slower
Change frequency
Increase your power
Repeat everything twice
G2C02 (A) Page 2-13
61

## Slide 62: What does it mean when a CW operator sends “KN” at the end of a transmission?
Listening for novice stations
Operating full break-in
Listening only for a specific station or stations
Closing station now
G2C03 (C) Page 2-13
62

## Slide 63: What is the best speed to use when answering a CQ in Morse code?
The fastest speed at which you are comfortable copying, but no slower than the CQ
The fastest speed at which you are comfortable copying, but no faster than the CQ
At the standard calling speed of 10 wpm
At the standard calling speed of 5 wpm
G2C05 (B) Page 2-13
63

## Slide 64: What does the term “zero beat” mean in CW operation?
Matching the speed of the transmitting station
Operating split to avoid interference on frequency
Sending without error
Matching the transmit frequency to the frequency of a received signal
G2C06 (D) Page 2-13
64

## Slide 65: What prosign is sent to indicate the end of a formal message when using CW?
SK
BK
AR
KN
G2C08 (C) Page 2-13
65

## Slide 66: What does the Q signal “QSL” mean?
Send slower
We have already confirmed by card
I acknowledge receipt
We have worked before
G2C09 (C) Page 2-13
66

## Slide 67: What does the Q signal “QRV” mean?
You are sending too fast
There is interference on the frequency
I am quitting for the day
I am ready to receive messages
G2C11 (D) Page 2-13
67

## Slide 68: What is the purpose of an electronic keyer?
Automatic transmit/receive switching
Automatic generation of strings of dots and dashes for CW operation
VOX operation
Computer interface for PSK and RTTY operation
G4A10 (B) Page 2-13
68

## Slide 69: Emergency Operation
Amateurs should be familiar with emergency rules and procedures
See Table 2.3 (General Class License Manual, Page 2-16/2-17)
  FCC 47 CFR § 97.401 Operating during a disaster
  FCC 47 CFR § 97.403 Safety of life and protection of property
  FCC 47 CFR § 97.405 Station in distress
  FCC 47 CFR § 97.407 Radio amateur civil emergency service

## Slide 70: ARES & RACES Amateur Radio two primary emergency response organizations
ARES = Amateur Radio Emergency Services (sponsored by ARRL)
  Mission: provide communications assistance to local and regional government and relief agencies
  http://www.arrl.org/ares
RACES (sponsored by FEMA)
  Mission: provide essential communications for State and local governments in time of emergency
  Only a licensed amateur may be the control operator of a RACES station

## Slide 71: Distress Calls
If you receive a call for help …
  Immediately suspend your existing contact
  Immediately acknowledge to the station calling for help
  Stand by to receive the location of the emergency and the name of the assistance required
  Relay the info to the proper authorities and stay on frequency

## Slide 72: Distress Calls (cont.)
If you’re the station making the distress call …
  On voice mode, say MAYDAY MAYDAY MAYDAY. On CW or digital send SOS SOS SOS followed by Any station come in please.
  Identify the transmission with your call sign
  State your location and the nature of the situation
  Describe the type of assistance required
FCC 47 CFR § 97.405 allows the distress station to use ANY means of communication available, even frequencies, mode, or power level outside your normal privileges

## Slide 73: PRACTICE QUESTIONS

## Slide 74: What is the first thing you should do if you are communicating with another amateur station and hear a station in distress break in?
Continue your communication because you were on the frequency first
Acknowledge the station in distress and determine what assistance may be needed
Change to a different frequency
Immediately cease all transmissions
G2B02 (B) Page 2-18
74

## Slide 75: Who may be the control operator of an amateur station transmitting in RACES to assist relief operations during a disaster?
Only a person holding an FCC-issued amateur operator license
Only a RACES net control operator
A person holding an FCC-issued amateur operator license or an appropriate government official
Any control operator when normal communication systems are operational
G2B09 (A) [97.407(a)] Page 2-17
75

## Slide 76: When is an amateur station allowed to use any means at its disposal to assist another station in distress?
Only when transmitting in RACES
At any time when transmitting in an organized net
At any time during an actual emergency
Only on authorized HF frequencies
G2B10 (C) [97.405(b)] Page 2-18
76

## Slide 77: What frequency should be used to send a distress call?
Whichever frequency has the best chance of communicating the distress message
Only frequencies authorized for RACES or ARES stations
Only frequencies that are within your operating privileges
Only frequencies used by police, fire, or emergency medical services
G2B11 (A) [97.405] Page 2-18
77

## Slide 78: END OF MODULE 2

## Slide 79
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.