## Slide 1
1

## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/
2

## Slide 3: Module 4a ARRL General Class Chapter 4 – Components & Circuits (4.1, 4.2, 4.3, 4.4) Power & Decibels, AC Power, Basic Components, Reactance, Impedance & Resonance
3

## Slide 4: Power and Decibels
Recall Ohm’s Law from your Technician training …
4

## Slide 5: Power and Decibels (cont.)
Similarly …
5

## Slide 6: Power and Decibels (cont.)
Substituting the Ohm’s Law equivalents for voltage and current allows power to be calculated using resistance …
6

## Slide 7: Power Calculation Examples
To find out how many watts of electrical power are used if 400 Vdc is supplied to an 800 Ω resistor …
7

## Slide 8: Power Calculation Examples (cont.)
To find out how many watts are being dissipated when a current of 7.0 mA flows through a 1.25 kΩ resistor …
8

## Slide 9: Calculating a Power or Voltage Ratio from dB
Power Ratio = log -1
dB
10
Voltage Ratio = log -1
dB
20
Inverse log notes …
Written as … log10-1
or … log-1
On scientific calculators …
LOG-1
ALOG
10X
INV then LOG
9

## Slide 10: Useful Power vs. dB Value to Remember
If you double the power (or cut it in half), there’s a 3 dB change …
dB = 10 log10
2
1
= 10 log10 (2) = 10 × (0.3) = 3 dB
10

## Slide 11: Converting dB to Percentage & Vice Versa
Application example: Suppose you are using an antenna feed line that has a loss of 1dB. You can calculate the amount of transmitter power that’s actually reaching your antenna and how much is lost in the feed line.
11

## Slide 12: Current, Voltage, and Power Review
12

## Slide 13: Resistance and Ohm’s Law Review
13

## Slide 14: Frequency Review
A complete sequence of ac current (alternating current) flowing, stopping, reversing, and stopping again is a cycle
The number of cycles per second is the current’s frequency (f), measured in hertz (Hz)
A harmonic is a frequency at some integer multiple (2, 3, 4, etc.) of a lowest or fundamental frequency
  The harmonic at twice the frequency is the second harmonic, at three times is the third harmonic (there is no first harmonic)
14

## Slide 15: Wavelength Review
Speed of light in space (c) is 300 million (3 × 108) meters per second … somewhat slower in wires and cables
Wavelength (λ) of radio wave is the distance it travels during one complete cycle
  λ = c / f
  f = c / λ
A radio wave can be referred to by frequency OR wavelength because the speed of light is constant
15

## Slide 16: PRACTICE QUESTIONS
16

## Slide 17: What dB change represents a factor of two increase or decrease in power?
Approximately 2 dB
Approximately 3 dB
Approximately 6 dB
Approximately 12 dB
G5B01 (B) Page 4-2
17

## Slide 18: How many watts of electrical power are used if 400 VDC is supplied to an 800 ohm load?
0.5 watts
200 watts
400 watts
3200 watts
G5B03 (B) Page 4-1
18

## Slide 19: How many watts of electrical power are used by a 12 VDC light bulb that draws 0.2 amperes?
2.4 watts
24 watts
6 watts
60 watts
G5B04 (A) Page 4-2
19

## Slide 20: How many watts are dissipated when a current of 7.0 milliamperes flows through a 1250 ohm resistance?
Approximately 61 milliwatts
Approximately 61 watts
Approximately 11 milliwatts
Approximately 11 watts
G5B05 (A) Page 4-2
20

## Slide 21: What percentage of power loss would result from a transmission line loss of 1 dB?
10.9 percent
12.2 percent
20.6 percent
25.9 percent
G5B10 (C) Page 4-3
21

## Slide 22: AC Power / RMS: Definition & Measurement
The power equation is very clear for dc power …
  P = E2 / R
However, what is the value of E for ac power?
  Not peak, not average … it’s RMS (root mean square or VRMS)
The RMS for a sine wave is 0.707 times the sine wave’s peak voltage
22

## Slide 23: Figure 4.2 Relationships between RMA, average, peak, and peak-to-peak ac voltage and current
23

## Slide 24: Waveform Formulas (Note: Do not use these for non-sine waves!)
It is particularly important to know the relationship between RMS and peak voltages to choose components that have sufficient voltage ratings. Capacitors are often connected across the ac power line to perform RF filtering. The capacitor must be rated to withstand the ac peak voltage.
Refer to Figure 4.2
24

## Slide 25: Waveform Calculation Examples
Example: A sine wave with a peak voltage of 17 V has what RMS value?
VRMS = 0.707 X VPK = 0.707 X 17 V = 12 V
Example: A sine wave with a peak-peak voltage of 100 V has what RMS value?
VRMS = 0.707 X
VP-P
2
= 0.707 X
100
2
= 35.4 V
25

## Slide 26: PEP: Definition and Measurement
PEP = Peak envelope power
PEP is the average power of one complete RF cycle at the peak of the signal’s envelope … a convenient way of measuring the max power of amplitude-modulated signals
However, this definition is confusing …
  See (following slide) definition from www.mdarc.org
26

## Slide 27: Clarification of Peak Envelope Power
RF signals such as AM and SSB have a constantly changing amplitude during transmission, like the image at the top of the page. For these signals, there will be points where the amplitude is at its greatest (see figure below). This is the "one RF cycle at the crest of the modulation envelope" in the definition.
Other signals, such as FM, PM (phase modulation) and CW, have a constant amplitude, so every RF cycle is its "peak" cycle.
Once that cycle is identified, we calculate the average power over its complete duration. That's the red area in figure on next slide.
27

## Slide 28: Clarification of Peak Envelope Power (cont.)
Once that cycle is identified, we calculate the average power over its complete duration. That's the red area in figure below.
Note that we calculate the power in both the positive voltage half-cycle and the negative voltage half-cycle. They don't cancel out because, as shown below, the PEV is squared, making both of them positive.
Start by measuring the amplitude of the peak, usually in volts. That is PEV in figure on previous slide
Then apply the following formula … (next slide) …
28

## Slide 29: PEP Calculations
Example: If PEV is 50V across a 50Ω load, the PEP power is …
Example: If a 50Ω load is dissipating 1200W PEP, the RMS voltage is …
29

## Slide 30: PEP Summary
PEP equals the average power IF an amplitude-modulated signal is NOT modulated
  An example of this is when modulation is removed from an AM signal (leaving only the steady carrier) or when a CW transmitter is keyed
An FM signal is a constant-power signal, so PEP is always equal to average power for FM signals. In other words, if an average-reading wattmeter connected to your transmitter reads 1060W when you close the key on CW, your output power will be …
1060W
30

## Slide 31: PRACTICE QUESTIONS
31

## Slide 32: What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output?
1.4 watts
100 watts
353.5 watts
400 watts
G5B06 (B) Page 4-7
32

## Slide 33: What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value?
The peak-to-peak value
The peak value
The RMS value
The reciprocal of the RMS value
G5B07 (C) Page 4-5
33

## Slide 34: What is the peak-to-peak voltage of a sine wave with an RMS voltage of 120.0 volts?
84.8 volts
169.7 volts
240.0 volts
339.4 volts
G5B08 (D) Page 4-6
34

## Slide 35: What is the RMS voltage of a sine wave with a value of 17 volts peak?
8.5 volts
12 volts
24 volts
34 volts
G5B09 (B) Page 4-6
35

## Slide 36: What is the ratio of peak envelope power to average power for an unmodulated carrier?
0.707
1.00
1.414
2.00
G5B11 (B) Page 4-7
36

## Slide 37: What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts?
173 volts
245 volts
346 volts
692 volts
G5B12 (B) Page 4-7
37

## Slide 38: What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts?
530 watts
1060 watts
1500 watts
2120 watts
G5B13 (B) Page 4-7
38

## Slide 39: What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output?
8.75 watts
625 watts
2500 watts
5000 watts
G5B14 (B) Page 4-7
39

## Slide 40: Basic Components
Refer to the following 5 slides … selected basic component samples from Figure 4.4 (page 4-8)
Three most basic components …
  Resistors: Designated with an R, resist flow of electricity, measured in ohms (Ω)
  Capacitors: Designated C, store electric energy, measured in farads (F)
  Inductors: Designated L, store magnetic energy, measured in henries (H)
40

## Slide 41: Common Schematic Symbols: Resistors
Fig. 4.4

## Slide 42: Common Schematic Symbols: Capacitors
Fig. 4.4

## Slide 43: Common Schematic Symbols: Inductors
Fig. 4.4

## Slide 44: Common Schematic Symbols: Tubes
Fig. 4.4

## Slide 45: Common Schematic Symbols: Wiring
Fig. 4.4

## Slide 46: Resistors and Resistance
Several common types
Available with nominal values from 1Ω or less to more than 1MΩ
  Nominal value printed with text or colored bands
  Most common units are ohms (Ω), kilo ohms (kΩ), and megohms (MΩ)
Precision tolerances range from 1% or less to 10%

## Slide 47: Converting Between Units
CONVERT FROM | CONVERT TO (a) | CONVERT TO (b)
Ohms | Kiloohms: Divide by 1000 | Megohms: Divide by 1,000,000
Kiloohms | Ohms: Multiply by 1000 | Megohms: Divide by 1000
Megohms | Ohms: Multiply by 1,000,000 | Kiloohms: Multiply by 1000
EXAMPLE: 150 Ω = 150 / 1000 = 0.15 KΩ and 150 Ω = 150 / 1,000,000 = 0.00015 MΩ
EXAMPLE: 4.7 kΩ = 4.7 X 1000 = 4700 kΩ and 4.7 kΩ = 4.7 / 1000 = .0047 MΩ
EXAMPLE: 2.2 MΩ = 2.2 X 1,000,000 = 2,200,000 Ω and 2.2 MΩ = 2.2 X 1000 = 2200 kΩ

## Slide 48: Inductors and Inductance
AIR-CORE
VARIABLE
MAGNETIC OR IRON CORE
Like resistors, several common types
Double lines indicate a solid magnetic core
Variable inductors often have solid cores. Use of double lines on schematics is optional
Miniature inductors (not shown) look similar to resistors

## Slide 49: Inductor Design
Inductance (ability to store magnetic energy) is directly proportional to the square of the number of turns and area enclosed by each turn
  Making an inductor LONGER without changing number of turns or diameter REDUCES inductance
Increasing the ability to store magnetic energy (called permeability) increases the inductance

## Slide 50: Inductor Design (cont.)
The type of core and winding affects inductance and vary according to the use/purpose of the inductor
Variable inductors are often used in low-power receiving and transmitting applications
  Adjusted by moving a magnetic core in and out of the inductor (threaded cores move when turned)
  For high-power inductors, adjustment is made by moving a sliding contact along the inductor

## Slide 51: Converting Between Units
CONVERT FROM | CONVERT TO (a) | CONVERT TO (b)
Nanohenries | Microhenries: Divide by 1000 | Millihenries: Divide by 1,000,000
Microhenries | Nanohenries: Multiply by 1000 | Millihenries: Divide by 1000
Millihenries | Nanohenries: Multiply by 1,000,000 | Microhenries: Multiply by 1000
EXAMPLE: 330 nH = 330 / 1000 = 0.33 µH and 330 nH = 330 / 1,000,000 = 0.00033 mH
EXAMPLE: 6.8 µH = 6.8 X 1000 = 6800 nH and 6.8 µH = 6.8 / 1000 = .0068 mH
EXAMPLE: 88 mH = 88 X 1,000,000 = 88,000,000 nH and 88 mH = 88 X 1000 = 8800 µH

## Slide 52: Inductor Coupling
Place 2 inductors close together with axes aligned
Magnetic field from one inductor can also pass through the second one, sharing some of its energy
This is called coupling
The ability of inductors to share or transfer magnetic energy is called mutual inductance

## Slide 53: Inductor Design (cont.)
In toroidal winding the core contains nearly all the inductor’s magnetic field
Since little of the field extends outside the core, toroids can be placed next to each other (in almost any orientation) with minimal mutual inductance
This property makes them useful in RF circuits
Composition of the core varies (ferrite, powdered iron, even exotic “rare earth” metals), making it possible to obtain wide range of inductance values in a relatively small package
The combination of materials (“mix”) in the core is selected so the inductor performs best over a specific range of frequencies

## Slide 54: PRACTICE QUESTIONS
54

## Slide 55: What is an advantage of using a ferrite core toroidal inductor?
Large values of inductance may be obtained
The magnetic properties of the core may be optimized for a specific range of frequencies
Most of the magnetic field is contained in the core
All these choices are correct
G6A08 (D) Page 4-12
55

## Slide 56: What determines the performance of a ferrite core at different frequencies?
Its conductivity
Its thickness
The composition, or “mix,” of materials used
The ratio of outer diameter to inner diameter
G6B01 (C) Page 4-12
56

## Slide 57: Capacitors and Capacitance
Capacitors have two conducting surfaces (electrodes) separated by a dielectric
Capacitance is the ability to store electric energy, measured in farads (F)
Blocks dc current flow
The simplest capacitor is a pair of metal plates separated by air

## Slide 58: Capacitors and Capacitance (cont.)
Tantalum and electrolytic capacitors are polarized, meaning the dc voltage may only be applied on one direction without damaging the electrolyte (check polarity markings for correct installation)
Capacitors have voltage ratings. Exceeding this rating can result in arcing between conducting surfaces (usually destroys all but air-dielectric capacitors)

## Slide 59: Capacitors and Capacitance (cont.)
Capacitor types:
  Ceramic – RF filtering, bypassing at high frequencies, low cost
  Plastic film – audio circuits & lower radio frequencies
  Silvered-mica – highly stable, low loss, used in RF circuits
  Electrolytic and tantalum – power supply filter circuits
  Air and vacuum dielectric – transmitting and RF circuits

## Slide 60: Capacitors and Capacitance (cont.)
Capacitor uses:
  Blocking – pass ac signals while blocking dc signals
  Bypass – provide low impedance path for ac signals around higher-impedance circuit
  Filter – smooth out voltage pulses of rectified ac to an even dc voltage
  Suppressor – absorb energy of voltage transients or spikes
  Tuning – vary frequency of resonant circuits or adjust impedance matching circuits

## Slide 61: Aluminum and Tantalum Electrolytic Capacitors
Designed to optimize their energy storage capabilities
Voltage must be applied with the correct polarity
Creates large capacitances in comparatively small volumes
Aluminum: Uses metal foil for conducting surfaces and dielectric is an insulating layer on the foil created by a wet paste or gel
Tantalum: Similar to aluminum in that a porous mass of tantalum is immersed in an electrolyte

## Slide 62: PRACTICE QUESTIONS

## Slide 63: What is the value in nanofarads (nF) of a 22,000 picofarad (pF) capacitor?
0.22
2.2
22
220
G5C17 (C) Page 4-13
63

## Slide 64: What is the value in microfarads of a 4700 nanofarad (nF) capacitor?
47
0.47
47,000
4.7
G5C18 (D) Page 4-13
64

## Slide 65: Which of the following is an advantage of an electrolytic capacitor?
Tight tolerance
Much less leakage than any other type
High capacitance for a given volume
Inexpensive RF capacitor
G6A04 (C) Page 4-12
65

## Slide 66: Which of the following is an advantage of ceramic capacitors as compared to other types of capacitors?
Tight tolerance
High stability
High capacitance for given volume
Comparatively low cost
G6A14 (D) Page 4-13
66

## Slide 67: Transformers
Transformers transfer ac power between 2 or more inductors (called windings) sharing a common core
The winding TO which power is applied is the primary
The winding FROM which power is supplied is the secondary
When voltage is applied to primary, mutual inductance causes voltage to appear across secondary
Transformers work in “both directions”

## Slide 68: Transformers (cont.)
Transformers change power from one combination of ac voltage and current to another by using windings with different numbers of turns
  The transformation occurs because all windings share the same magnetic field (wound on the same core)
A significant change between secondary & primary usually requires a change in wire size between windings
  In step-up transformers, the primary carries higher current and is wound with larger diameter wire than the secondary

## Slide 69: Transformer “Math”
The ratio of number turns in the primary winding (NP) to the number of turns in the secondary (NS) determines how current and voltage are changed
Since most circuits are concerned with voltage, most transformer equations relate transformer input (primary) voltage (EP) to output (secondary) voltage (ES)
ES
EP
NS
NP
=
NS
NP
ES
=
EP
×
OR

## Slide 70: Transformer “Math” Examples
What is the voltage across a 500-turn secondary winding if 120V ac is applied across the 2250-turn primary winding?
NS
NP

## Slide 71: Transformer “Math” Examples (cont.)
What would be the secondary-to-primary turns ratio to change 115V ac to 500V ac?
… is the same as …
=
=
ES
EP
NS
NP
=
NS
NP
=
ES
EP
NS
NP
=
ES
EP

## Slide 72: PRACTICE QUESTIONS

## Slide 73: What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding?
Capacitive coupling
Displacement current coupling
Mutual inductance
Mutual capacitance
G5C01 (C) Page 4-13
73

## Slide 74: What happens if a signal is applied to the secondary winding of a 4:1 voltage step-down transformer instead of the primary winding?
The output voltage is multiplied by 4
The output voltage is divided by 4
Additional resistance must be added in series with the primary to prevent overload
Additional resistance must be added in parallel with the secondary to prevent overload
G5C02 (A) Page 4-14
74

## Slide 75: What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC?
2370 volts
540 volts
26.7 volts
5.9 volts
G5C06 (C) Page 4-14
75

## Slide 76: Why is the conductor of the primary winding of many voltage step-up transformers larger in diameter than the conductor of the secondary winding?
To improve the coupling between the primary and secondary
To accommodate the higher current of the primary
To prevent parasitic oscillations due to resistive losses in the primary
To ensure that the volume of the primary winding is equal to the volume of the secondary winding
G5C16 (B) Page 4-14
76

## Slide 77: Components in Series and Parallel Circuits

## Slide 78: Components in Series and Parallel Circuits
In series circuits, the current is the same in all components and voltages are summed (Kirchoff’s Voltage Law).
  Voltages add in a series circuit
In parallel circuits, voltage across all components is the same and the sum of currents into and out of circuit junctions must be equal (Kirchoff’s Current Law).
  Currents add in a parallel circuit
Components connected in series or parallel can be replaced with a single equivalent component

## Slide 79: Calculating Series & Parallel Equivalent Values
COMPONENT | IN SERIES
RESISTOR | ADD VALUES, R1 + R2 + R3 + …
INDUCTOR | ADD VALUES, L1 + L2 + L3 + …
CAPACITOR | RECIPROCAL OF RECIPROCALS, 1/(1/C1 + 1/C2 + 1/C3 + …)
COMPONENT | IN PARALLEL
RESISTOR | RECIPROCAL OF RECIPROCALS, 1/(1/R1 + 1/R2 + 1/R3 + …)
INDUCTOR | RECIPROCAL OF RECIPROCALS, 1/(1/L1 + 1/L2 + 1/L3 + …)
CAPACITOR | ADD VALUES, C1 + C2 + C3 + …
Refer to Figure 4.10

## Slide 80: Effect on Total Value of Adding Components in Series and Parallel
COMPONENT | ADDING IN SERIES | ADDING IN PARALLEL
RESISTOR | INCREASE | DECREASE
INDUCTOR | INCREASE | DECREASE
CAPACITOR | DECREASE | INCREASE
Refer to Figure 4.10

## Slide 81
Figure 4.10: This drawing illustrates how components in series and parallel can be combined into a single equivalent component value.

## Slide 82: Examples: Calculating Series & Parallel Equivalent Values
Three 100 Ω resistors …
In Series …
In Parallel …
Three 100 µF capacitors …
In Series …
In Parallel …

## Slide 83: Calculating Series & Parallel Equivalent Values (cont.)
With only two components, the reciprocal of reciprocals calculation is greatly simplified …
Inductance of a 20 mH and 50 mH inductor …
In series …
In parallel …

## Slide 84: PRACTICE QUESTIONS

## Slide 85: How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit?
It equals the average of each branch current
It decreases as more parallel branches are added to the circuit
It equals the sum of the currents through each branch
It is the sum of the reciprocal of each individual voltage drop
G5B02 (C) Page 4-15
85

## Slide 86: Which of the following components increases the total resistance of a resistor?
A parallel resistor
A series resistor
A series capacitor
A parallel capacitor
G5C03 (B) Page 4-15
86

## Slide 87: What is the total resistance of three 100 ohm resistors in parallel?
0.30 ohms
0.33 ohms
33.3 ohms
300 ohms
G5C04 (C) Page 4-17
87

## Slide 88: If three equal value resistors in series produce 450 ohms, what is the value of each resistor?
1500 ohms
90 ohms
150 ohms
175 ohms
G5C05 (C) Page 4-18
88

## Slide 89: What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel?
576.9 nanofarads
1733 picofarads
3583 picofarads
10.750 nanofarads
G5C08 (D) Page 4-18
89

## Slide 90: What is the capacitance of three 100 microfarad capacitors connected in series?
0.30 microfarads
0.33 microfarads
33.3 microfarads
300 microfarads
G5C09 (C) Page 4-17
90

## Slide 91: What is the inductance of three 10 millihenry inductors connected in parallel?
0.30 henries
3.3 henries
3.3 millihenries
30 millihenries
G5C10 (C) Page 4-17
91

## Slide 92: What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor?
0.07 millihenries
14.3 millihenries
70 millihenries
1000 millihenries
G5C11 (C) Page 4-17
92

## Slide 93: What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor?
0.07 millihenries
14.3 millihenries
70 millihenries
1000 millihenries
G5C12 (B) Page 4-17
93

## Slide 94: Which of the following components should be added to a capacitor to increase the capacitance?
An inductor in series
A resistor in series
A capacitor in parallel
A capacitor in series
G5C13 (C) Page 4-15
94

## Slide 95: Which of the following components should be added to an inductor to increase the inductance?
A capacitor in series
A resistor in parallel
An inductor in parallel
An inductor in series
G5C14 (D) Page 4-15
95

## Slide 96: What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor connected in parallel?
5.9 ohms
0.17 ohms
10000 ohms
80 ohms
G5C15 (A) Page 4-18
96

## Slide 97: Reactance
Reactance: Resistance to the flow of ac current caused by capacitance or inductance. Denoted by X. Measured in ohms (Ω), like resistance.
Capacitive reactance: Opposition to ac current flow from the stored energy in a capacitor. Denoted by XC.
Capacitors behave differently with ac and dc current. With dc, when voltage is initially applied, capacitor looks like a short circuit. After charging, it looks like an open circuit. This is how it blocks dc signals. AC behavior depends upon voltage frequency.

## Slide 98: Capacitive Reactance
As the frequency of the applied signal increases, XC decreases, and vice versa

## Slide 99: Reactance (cont.)
Inductive reactance is the opposition to ac current flow from the stored energy in a inductor and is denoted by XL
Behavior with frequency is described by:

## Slide 100: Inductive Reactance
As the frequency of the applied signal increases, XL increases, and vice versa

## Slide 101: Parasitic Inductance
Parasitic: an unwanted characteristic resulting from the component’s physical construction. Examples:
  The coils in wire-wound resistors (coils create parasitic inductance)
  Wire leads of components
  In inductors, each pair of turns creates parasitic capacitance in series with the inductance
Often significant enough to disrupt circuit’s operation or affect tuning in radios

## Slide 102: PRACTICE QUESTIONS

## Slide 103: What is reactance?
Opposition to the flow of direct current caused by resistance
Opposition to the flow of alternating current caused by capacitance or inductance
A property of ideal resistors in AC circuits
A large spark produced at switch contacts when an inductor is de-energized
G5A02 (B) Page 4-19
103

## Slide 104: Which of the following causes opposition to the flow of alternating current in an inductor?
Conductance
Reluctance
Admittance
Reactance
G5A03 (D) Page 4-19
104

## Slide 105: Which of the following causes opposition to the flow of alternating current in a capacitor?
Conductance
Reluctance
Admittance
Reactance
G5A04 (C) Page 4-19
105

## Slide 106: How does an inductor react to AC?
As the frequency of the applied AC increases, the reactance decreases
As the amplitude of the applied AC increases, the reactance increases
As the amplitude of the applied AC increases, the reactance decreases
As the frequency of the applied AC increases, the reactance increases
G5A05 (D) Page 4-20
106

## Slide 107: How does a capacitor react to AC?
As the frequency of the applied AC increases, the reactance decreases
As the frequency of the applied AC increases, the reactance increases
As the amplitude of the applied AC increases, the reactance increases
As the amplitude of the applied AC increases, the reactance decreases
G5A06 (A) Page 4-19
107

## Slide 108: What unit is used to measure reactance?
Farad
Ohm
Ampere
Siemens
G5A09 (B) Page 4-19
108

## Slide 109: Which of the following is a reason not to use wire-wound resistors in an RF circuit?
The resistor’s tolerance value would not be adequate for such a circuit
The resistor’s inductance could make circuit performance unpredictable
The resistor could overheat
The resistor’s internal capacitance would detune the circuit
G6A06 (B) Page 4-21
109

## Slide 110: Impedance
Impedance is the opposition to current flow in an ac circuit caused by resistance, reactance, or any combination of the two. Denoted by Z. Measured in ohms.
Like resistance, it’s the ratio of voltage to current (Fig. 4.13).
Figure 4.13

## Slide 111: Resonance
Resonance is the condition in which there is a match between the frequency at which a circuit or antenna naturally responds to the frequency of an applied signal
Occurs when capacitive and inductive reactance are equal
In a resonant series circuit, reactance of L and C cancel, making a short circuit, leaving only the resistance (R) as the circuit’s impedance
Used in filters & tuned circuits to pass or reject specific frequencies

## Slide 112: Resonant Series Circuit
In a resonant series circuit, the reactance of L and the reactance of C cancel, making a short circuit. This leaves only the resistance (R) as the circuit’s impedance.

## Slide 113: Self-Resonance
Resonance can occur when a component’s expected reactance equals the reactance of it’s parasitic reactance (called self-resonance
Results in a component that appears to be a short or open circuit at the self-resonant frequency
Above this frequency, the component’s reactance switches type, making an inductor capacitive and a capacitor inductive!

## Slide 114: Impedance Transformation
A transformer can change the combination of voltage and current while transferring energy
The transformer also changes impedance between the primary and secondary circuits (by changing the ratio of voltage and current between the primary and secondary circuits)
The turns ratio controls the transformation in the same way as the ratio of gear teeth in a mechanical transmission

## Slide 115: Impedance Transformation Examples
or
What is the primary impedance if a 200 Ω load is connected to the secondary of a transformer with a 5:1 secondary-to-primary turns ratio?
NP
NS
=
ZP = ZS
NP
NS
ZP = ZS
NP
NS

## Slide 116: Impedance Transformation Examples (cont.)
What turns ratio is required to change a 600 Ω impedance to a 4 Ω impedance?

## Slide 117: Impedance Matching
An energy source’s ability to deliver power to a load is limited by its internal impedance
Amateur transmitting equipment is designed so that the internal impedance of its output circuits is 50 Ω
If the difference between the antenna system impedance and transmitter’s out impedance is great enough, the transmitter may reduce output power to avoid damage (solution is an impedance-matching circuit)

## Slide 118: Impedance Matching (cont.)
Most impedance-matching circuits are LC circuits (inductors and capacitors) … see figure below:
Impedance matching can also be performed by special lengths and connections of transmission lines.

## Slide 119: PRACTICE QUESTIONS

## Slide 120: What is impedance?
The electric charge stored by a capacitor
The inverse of resistance
The opposition to the flow of current in an AC circuit
The force of repulsion between two similar electric fields
G5A01 (C) Page 4-21
120

## Slide 121: What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive?
The source delivers minimum power to the load
The electrical load is shorted
No current can flow through the circuit
The source can deliver maximum power to the load
G5A07 (D) Page 4-22
121

## Slide 122: What is one reason to use an impedance matching transformer?
To minimize transmitter power output
To maximize the transfer of power
To reduce power supply ripple
To minimize radiation resistance
G5A08 (B) Page 4-23
122

## Slide 123: Which of the following devices can be used for impedance matching at radio frequencies?
A transformer
A Pi-network
A length of transmission line
All these choices are correct
G5A10 (D) Page 4-23
123

## Slide 124: Which of the following describes one method of impedance matching between two AC circuits?
Insert an LC network between the two circuits
Reduce the power output of the first circuit
Increase the power output of the first circuit
Insert a circulator between the two circuits
G5A11 (A) Page 4-23
124

## Slide 125: What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance?
12.2 to 1
24.4 to 1
150 to 1
300 to 1
G5C07 (A) Page 4-22
125

## Slide 126: What happens when an inductor is operated above its self-resonant frequency?
Its reactance increases
Harmonics are generated
It becomes capacitive
Catastrophic failure is likely
G6A11 (C) Page 4-22
126

## Slide 127: END OF MODULE 4a

## Slide 128
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.