## Slide 1
1

## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/
2

## Slide 3: Module 4b ARRL General Class Chapter 4 – Components and Circuits (4.5, 4.6, 4.7 ) Active Components, Practical Circuits, Basic Test Equipment

## Slide 4: Semiconductor Components
The most common active components are made of semiconductors
Most are made of silicon and germanium
Electrical properties can be controlled by addition of small amounts of dopants (impurities) such as indium and phosphorus
If the impurity creates an excess of electrons, the result is an N-type material. The opposite is P-type.
Where N-type and P-type are in contact is a PN junction

## Slide 5: Diodes & Rectifiers
A semiconductor junction diode uses a PN junction to block current flow in one direction
Wire leads are attached to each layer
Current flows when positive voltage is applied from P-type to N-type material (forward bias)

## Slide 6: Diodes & Rectifiers (cont.)
Voltage applied in opposite direction is reverse bias
  Pulls electrons away from junction so no current flows
Voltage required to force electrons across junction is the junction threshold voltage (VF)
  For silicon diodes, VF ≅ 0.7 V
  For germanium diodes, VF ≅ 0.3 V

## Slide 7: Types of Diodes
Light Emitting
Laser
Avalanche
Zener
Schottky
Photodiode
PN junction
Transient Voltage Suppression
Gold Doped
Constant Current
Peltier
Silicon Controlled Rectifier
PIN
Varactor

## Slide 8: Diode Ratings
Peak inverse voltage (PIV): Maximum reverse voltage before breakdown occurs (allowing current to flow in reverse direction)
Average forward current (IF): Exceeding diode’s rating will destroy the diode’s internal structure
Junction capacitance (CJ): When reverse biased, layers of P- and N-type material act like capacitor plates. The larger the CJ the longer it takes to switch to conducting forward current.

## Slide 9: Bipolar Transistors
Adding a 3rd layer of semiconducting material creates a device that can amplify signals called the transistor
Figure here is a bipolar junction transistor (BJT)
Unlike the diode, it requires power to function
It has 3 electrodes
  Collector (C)
  Base (B)
  Emitter (E)
Controlled by current flow between base and emitter

## Slide 10: Bipolar Transistors (cont.)
Very little base-emitter current is required for collector-emitter current to flow
The control of a large current by a smaller current is amplification
Ratio of collector-emitter current to base-emitter current is current gain
  Current gain for dc signals is ß
  Current gain for ac signals is hfe

## Slide 11: Field Effect Transistors (FET)
3 electrodes: Drain (D), Source (S), and Gate (G)
Instead of controlling drain-source current with gate-source current, the voltage between gate and source is used
Instead of current gain, FET has transconductance (gm) which is the ratio of source-drain current to gate voltage
MOSFETs (metal-oxide semiconductor FET) use oxide layer to insulate the gate

## Slide 12: Additional Transistor Notes
High amplification makes them ideal for use as switches (both voltage and current)
With enough voltage, transistors can be driven into saturation where further increases in input result in NO change in output
High enough input signals can reduce output current to zero called cutoff
Saturation and cutoff conditions are excellent representation of digital ON/OFF signals in logic circuits

## Slide 13: PRACTICE QUESTIONS

## Slide 14: What is the approximate junction threshold voltage of a germanium diode?
0.1 volt
0.3 volts
0.7 volts
1.0 volts
G6A03 (B) Page 4-24
14

## Slide 15: What is the approximate junction threshold voltage of a conventional silicon diode?
0.1 volt
0.3 volts
0.7 volts
1.0 volts
G6A05 (C) Page 4-24
15

## Slide 16: What are the stable operating points for a bipolar transistor used as a switch in a logic circuit?
Its saturation and cutoff regions
Its active region (between the cutoff and saturation regions)
Its peak and valley current points
Its enhancement and depletion modes
G6A07 (A) Page 4-25
16

## Slide 17: Which of the following describes the construction of a MOSFET?
The gate is formed by a back-biased junction
The gate is separated from the channel with a thin insulating layer
The source is separated from the drain by a thin insulating layer
The source is formed by depositing metal on silicon
G6A09 (B) Page 4-25
17

## Slide 18: Vacuum Tubes
Have at least 3 electrodes called elements
3 basic parts:
  A source of electrons
  Electrode to collect electrons
  Intervening electrodes that control electrons traveling from source to collector
Compared to transistors, most like the FET
Operate at high (hazardous) voltages (2000-3000 V). Exercise caution!

## Slide 19: Tube Terminology
Filament or heater – heats the cathode, causing it to emit electrons
Cathode – source of electrons
Control grid – grid closest to cathode, used to regulate electron travel between cathode and plate
Screen grid – electrode that reduces grid-to-plate capacitance
Suppressor grid – prevents electrons from traveling from plate to control or screen grid
Plate – collects electrons which is called plate current

## Slide 20: PRACTICE QUESTIONS

## Slide 21: Which element of a triode vacuum tube is used to regulate the flow of electrons between cathode and plate?
Control grid
Heater
Screen grid
Trigger electrode
G6A10 (A) Page 4-26
21

## Slide 22: What is the primary purpose of a screen grid in a vacuum tube?
To reduce grid-to-plate capacitance
To increase efficiency
To increase the control grid resistance
To decrease plate resistance
G6A12 (A) Page 4-26
22

## Slide 23: Analog Integrated Circuits (IC’s)
Operate over a continuous range of voltages and currents
Used for amplification, filtering, measurement, voltage regulation, and power control
Most common analog IC’s are the operational amplifier and linear voltage regulator
  Op amps are used for dc and audio circuits … inexpensive source of gain
  Linear voltage regulators maintain power supply output at constant voltage over a wide range of currents

## Slide 24: Figure 4.22
The popular 741 op-amp symbol and dual in-line package (DIP) connections are shown at (A). A common 3-terminal voltage regulator, the 7800-series, is shown in the TO-220 package at (B).

## Slide 25: Digital Integrated Circuits
Digital IC’s operate with discrete values of voltage and current representing the binary numbers system values 0 and 1 (representing OFF and ON)
Used for performing computations or controlling functions
The most popular logic family in use is CMOS (complementary metal-oxide semiconductors) technology (known for high speed and low power consumption)

## Slide 26: Table 4.4: Logic Family Characteristics
FAMILY NAME | MAX OPERATION FREQUENCY | POWER CONSUMPTION | POWER SUPPLY
TTL | 100 MHz | High | 5 V
CMOS | 1 GHz | Low | 3-5 V
CMOS (CD4000) | 1 MHz | Very Low | 3-15 V

## Slide 27: Digital Logic Basics
The basic building block of digital circuits are called gates that perform inversion (changing 1 to 0 and vice versa) and the OR and AND functions
The most common gates in use are the inverter, NAND and NOR
More complex functions (e.g., microprocessors, signal processors, etc.) are constructed from combinations of these functions
Circuits that use gates to combine binary inputs to generate a binary output or combination of binary outputs are called combinational logic
See Figure 4.23 for details

## Slide 28: Figure 4.23: Schematic symbols for the basic digital logic functions with the logic equations and truth tables that describe their operation.

## Slide 29: Figure 4.23: Schematic symbols for the basic digital logic functions with the logic equations and truth tables that describe their operation (cont.).

## Slide 30: Figure 4.23: Schematic symbols for the basic digital logic functions with the logic equations and truth tables that describe their operation (cont.).

## Slide 31: Digital Logic Basics (cont.)
Sequential logic circuits combine binary signals in a way that depends on time and on the sequence of inputs to the circuits
Basic building block of sequential logic is the flip-flop
  Responds to clock signal that causes it outputs to change based on input
  The 2 outputs (Q and Q-bar) are always in opposite states
  Connecting flip-flops together so that one flip-flop’s output feeds the next one’s input creates 2 important circuits; counters and shift registers

## Slide 32: Counter Logic
The outputs of the chain of flip-flops make up a binary number or state representing the number of clock signals that have occurred
Each flip-flop stores one bit of the total count
Highest number a counter can represent is 2N (N = number of flip-flops that make up the counter)
A 3-bit counter (3 flip-flops) can count 23 (= 8) states, 4-bit (24) can count 16 states, 5-bit (25) counts 32 states, etc.

## Slide 33: Shift Registers
Slightly different arrangement of the flip-flop array than in counters
Stores a sequence of 1s and 0s from its input as the flip-flop outputs
Each clock signal causes the value at the shift register’s input to pass or shift to the next flip-flop in the string
Some shift registers circuits can be configured to shift up and down (or forward/backward)
A simple form of digital memory

## Slide 34: RF Integrated Circuits
Designed for functions such as …
  Low-level high-gain amplifiers, mixers, modulators/demodulators, filters
Greatly reduce number of discrete devices require to build radio circuits
Monolithic microwave integrated circuits (MMIC) are special types of RF IC’s that work through microwave frequencies
  Perform several functions
  Enables construction of low-cost cell phones, GPS receivers, etc.

## Slide 35: PRACTICE QUESTIONS

## Slide 36: What is meant by the term MMIC?
Multi-Megabyte Integrated Circuit
Monolithic Microwave Integrated Circuit
Military Manufactured Integrated Circuit
Mode Modulated Integrated Circuit
G6B02 (B) Page 4-30
36

## Slide 37: Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits?
Low power consumption
High power handling capability
Better suited for RF amplification
Better suited for power supply regulation
G6B03 (A) Page 4-28
37

## Slide 38: What kind of device is an integrated circuit operational amplifier?
Digital
MMIC
Programmable Logic
Analog
G6B06 (D) Page 4-27
38

## Slide 39: Which of the following describes the function of a two-input AND gate?
Output is high when either or both inputs are low
Output is high only when both inputs are high
Output is low when either or both inputs are high
Output is low only when both inputs are high
G7B03 (B) Page 4-28
39

## Slide 40: Which of the following describes the function of a two input NOR gate?
Output is high when either or both inputs are low
Output is high only when both inputs are high
Output is low when either or both inputs are high
Output is low only when both inputs are high
G7B04 (C) Page 4-28
40

## Slide 41: How many states does a 3-bit binary counter have?
3
6
8
16
G7B05 (C) Page 4-28
41

## Slide 42: What is a shift register?
A clocked array of circuits that passes data in steps along the array
An array of operational amplifiers used for tri-state arithmetic operations
A digital mixer
An analog mixer
G7B06 (A) Page 4-28
42

## Slide 43: Microprocessors & Related Components: Memory
Microprocessors are capable of performing millions of computing instructions per second
Programs must be stored in memory devices so the microprocessor can read these instructions
  Volatile memory loses data when power is removed
  Nonvolatile memory stores data permanently, even without power
  Random-access memory (RAM) can be read from or written to
  Read-only memory (ROM) stores data permanently and cannot be changed

## Slide 44: Data Interfaces
Microprocessors communicate through data interfaces
  Two types: Serial & Parallel
  Serial transfers one bit of data in each transfer operation
  Parallel transfers multiple bits in each operation
One BYTE
One BIT

## Slide 45: Visual Interfaces
Amateur equipment uses two types of devices to present information visually
  Indicators & displays
Indicators: Presents ON/OFF information visually by the presence or absence of color or light
  Common indicators: Incandescent light bulbs & light-emitting diodes (LEDs)
Displays: Presents text or graphics information in visual form

## Slide 46: LEDs
Have largely replaced incandescent light bulbs in amateur equipment
  Last longer, can be turned on/off more quickly, use less power, generate less heat
Available in many colors
Made from special types of semiconductor material that emit light when the PN junction is forward biased

## Slide 47: Liquid Crystal Displays (LCD)
Most common type of display
Created by sandwiching liquid crystal material between glass panels
A pattern of electrodes is printed in a thin film on the front panel with a single electrode covering the rear panel
Voltage applied to front panel causes the crystals to twist in a configuration that blocks light
LCDs require ambient or back lighting (light source behind the crystal layer) since the crystal layer does not generate light on its own

## Slide 48: PRACTICE QUESTIONS

## Slide 49: What is meant by the term ROM?
Resistor Operated Memory
Read Only Memory
Random Operational Memory
Resistant to Overload Memory
G6B04 (B) Page 4-30
49

## Slide 50: What is meant when memory is characterized as non-volatile?
It is resistant to radiation damage
It is resistant to high temperatures
The stored information is maintained even if power is removed
The stored information cannot be changed once written
G6B05 (C) Page 4-30
50

## Slide 51: How is an LED biased when emitting light?
Beyond cutoff
At the Zener voltage
Reverse biased
Forward biased
G6B08 (D) Page 4-31
51

## Slide 52: Which of the following is a characteristic of a liquid crystal display?
It utilizes ambient or back lighting
It offers a wide dynamic range
It consumes relatively high power
It has relatively short lifetime
G6B09 (A) Page 4-31
52

## Slide 53: Practical Circuits: Rectifiers
Amateur radio electronic equipment requires dc power, so a power supply is required to run it from household ac power
  Most amateur equipment uses dc power at 13.8 V (chosen to be compatible with vehicle power systems)
Power supplies have 3 basic parts …
  Input transformer, rectifier, and filter-regulator output circuit

## Slide 54: Rectifier Circuits
Figure 4.24: Basic Rectifier Circuits (half-wave & full wave)
Half-Wave Rectifier. Converts only one-half of the input waveform (180°). This creates a series of pulses of current in the load at the same frequency as the input voltage.
Full-Wave Rectifier. Converts entire input waveform (360°). This is really 2 half-wave rectifiers operating on alternate half cycles. Requires that the transformer be center-tapped to provide a return path for current flowing to the load.

## Slide 55: Rectifiers (cont.)
The advantage of the full-wave rectifier is that output is produced during the entire 360° of the wave cycle (more efficient)
The output from full-wave rectifiers is a series of pulses at TWICE the frequency of the input voltage

## Slide 56: Full-Wave Bridge (Fig 4.25)
Another type of full-wave rectifier. This circuit adds 2 diodes (total of 4), but eliminates the need for a center-tapped winding.

## Slide 57: Power Supply Filter Circuits
Rectifiers output pulses of dc current don’t provide a stable voltage for direct use by electronic circuits
The variation in output voltage is called ripple
Pulses must be smoothed out by a filter network … consists of capacitors or capacitors AND inductors
Most common way to reduce ripple is a filter capacitor or capacitor-input filter
Older high-voltage circuits may use choke inductors

## Slide 58: Power Supply Safety
Fuses in the primary are used to protect against short circuits or excessive current loads
Bleeder resistors discharge stored energy when the supply is turned off
Working on power supplies – wait for the bleeder resistor to discharge energy, even if it is unplugged

## Slide 59: Switchmode or Switching Supplies
Another type of power supply filter, called linear filters
AC input is first rectified and filtered
Transistor switch pulses at high-frequency (20 kHz or more) to transfer energy to a filter capacitor (smoothes out ripple)
High frequency enables power supply to quickly change to current demands and means that small, lightweight inductors & capacitors can be used to filter the output

## Slide 60: PRACTICE QUESTIONS

## Slide 61: What useful feature does a power supply bleeder resistor provide?
It acts as a fuse for excess voltage
It ensures that the filter capacitors are discharged when power is removed
It removes shock hazards from the induction coils
It eliminates ground loop current
G7A01 (B) Page 4-33
61

## Slide 62: Which of the following components are used in a power supply filter network?
Diodes
Transformers and transducers
Quartz crystals
Capacitors and inductors
G7A02 (D) Page 4-33
62

## Slide 63: Which type of rectifier circuit uses two diodes and a center-tapped transformer?
Full-wave
Full-wave bridge
Half-wave
Synchronous
G7A03 (A) Page 4-32
63

## Slide 64: What is an advantage of a half-wave rectifier in a power supply?
Only one diode is required
The ripple frequency is twice that of a full-wave rectifier
More current can be drawn from the half-wave rectifier
The output voltage is two times the peak output voltage of the transformer
G7A04 (A) Page 4-32
64

## Slide 65: What portion of the AC cycle is converted to DC by a half-wave rectifier?
90 degrees
180 degrees
270 degrees
360 degrees
G7A05 (B) Page 4-32
65

## Slide 66: What portion of the AC cycle is converted to DC by a full-wave rectifier?
90 degrees
180 degrees
270 degrees
360 degrees
G7A06 (D) Page 4-32
66

## Slide 67: What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
A series of DC pulses at twice the frequency of the AC input
A series of DC pulses at the same frequency as the AC input
A sine wave at half the frequency of the AC input
A steady DC voltage
G7A07 (A) Page 4-32
67

## Slide 68: Which of the following is an advantage of a switchmode power supply as compared to a linear power supply?
Faster switching time makes higher output voltage possible
Fewer circuit components are required
High-frequency operation allows the use of smaller components
All these choices are correct
G7A08 (C) Page 4-33
68

## Slide 69: Batteries & Chargers
Two battery types: primary and secondary
Primary
  Disposable, discarded after discharging
  Battery chemistry: carbon-zinc, alkaline, silver-nickel
  Preferable to secondary batteries for emergency operation because ac power may not be available for charging
Secondary
  Can be recharged/reused many times
  Battery chemistry: nickel-cadmium (NiCd), nickel-metal hydride (NiMH), lithium-ion (Li-ion), lead-acid

## Slide 70: Table 4.8: Battery Types & Characteristics
BATTERY STYLE | CHEMISTRY | TYPE | FULL-CHARGE (V) | ENERGY RATING (mAh)
AAA | Alkaline | Disposable | 1.5 | 1100
AA | Alkaline | Disposable | 1.5 | 2600-3200
AA | Carbon-Zinc | Disposable | 1.5 | 600
AA | Nickel-Cadmium (NiCd) | Rechargeable | 1.2 | 700
AA | Nickel-Metal Hydride (NiMH) | Rechargeable | 1.2 | 1500-2200
AA | Lithium | Disposable | 1.7 | 2100-2400
C | Alkaline | Disposable | 1.5 | 7500
D | Alkaline | Disposable | 1.5 | 14,000
9 V | Alkaline | Disposable | 9 | 580
9 V | Nickel-Cadmium (NiCd) | Rechargeable | 9 | 110
9 V | Nickel-Metal Hydride (NiMH) | Rechargeable | 9 | 150
Coin Cells | Lithium | Disposable | 3-3.3 | 25-1000

## Slide 71: Storage Batteries (Larger Secondary Batteries)
Used for emergency or portable power to replace power supplies operating from ac power
Battery chemistry: lead-acid, liquid electrolyte, gel electrolyte (gel-cells)
Rated as “12 V” batteries, but are actually 13.8 V
Lead-acid batteries can produce useful power down to 10.5 V
Discharging below minimum voltage will reduce battery life

## Slide 72: Batteries (cont.)
Limiting amount of current drawn keeps battery cool and extends life
Some battery types (NiCds) are designed to have low internal resistance to supply high discharge currents
Batteries slowly lose charge when not in use. This is called self-discharge (minimize by keeping battery cool & dry, but avoid freezing as the expanding water can crack the case or damage electrodes).

## Slide 73: Alternative Power
Solar Power: photovoltaic conversion of sunlight to electricity
  Solar panels/cells are special type of diode … silicon PN-junctions
In solar cells, photons are absorbed by electrons that then have enough energy to travel across the PN junction and create dc current flow
  The forward voltage created (≈ 5V) is measured as the open-circuit voltage
Wind/solar power systems require substantial energy storage
In solar systems, battery connection is made through a series-connected diode to prevent battery from discharging back through the panel during periods of low illumination when voltage is reduced

## Slide 74: PRACTICE QUESTIONS

## Slide 75: What is the name of the process by which sunlight is changed directly into electricity?
Photovoltaic conversion
Photon emission
Photosynthesis
Photon decomposition
G4E08 (A) Page 4-36
75

## Slide 76: What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
0.02 VDC
0.5 VDC
0.2 VDC
1.38 VDC
G4E09 (B) Page 4-36
76

## Slide 77: What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel?
The diode serves to regulate the charging voltage to prevent overcharge
The diode prevents self-discharge of the battery through the panel during times of low or no illumination
The diode limits the current flowing from the panel to a safe value
The diode greatly increases the efficiency during times of high illumination
G4E10 (B) Page 4-37
77

## Slide 78: Which of the following is a disadvantage of using wind as the primary source of power for an emergency station?
The conversion efficiency from mechanical energy to electrical energy is less than 2 percent
The voltage and current ratings of such systems are not compatible with amateur equipment
A large energy storage system is needed to supply power when the wind is not blowing
All these choices are correct
G4E11 (C) Page 4-37
78

## Slide 79: What is the minimum allowable discharge voltage for maximum life of a standard 12 volt lead-acid battery?
6 volts
8.5 volts
10.5 volts
12 volts
G6A01 (C) Page 4-36
79

## Slide 80: What is an advantage of the low internal resistance of nickel-cadmium batteries?
Long life
High discharge current
High voltage
Rapid recharge
G6A02 (B) Page 4-36
80

## Slide 81: Connector Terminology
Pins: contacts that extend out of the connector body (male)
Sockets: hollow, recessed contacts (female)
Keyed connectors: specially shaped (bodies or inserts) to prevent damage from connecting incorrectly
Plugs: connectors installed on ends of cables
Jacks/receptables: connectors installed on equipment
Adapters: make connections between 2 different connector styles
Splitters: divide signals between 2 connectors

## Slide 82: Power Connectors
Fig 4.28: Connectors used on amateur equipment
Fig 4.29: Terminals that are crimped to ends of wires.

## Slide 83: Power Connectors (cont.)
Anderson Powerpole connectors have become the standard used by ARES
  Anderson connectors are “sexless” … by standardizing on a single style, equipment can be easily shared and replaced
Note that these (see previous figure) are crimp terminals … special crimping tools are used for attaching the wire to the terminal (avoid using pliers or other tools for making these connections)

## Slide 84: Audio Connectors
Come in ¼-inch, ⅛-inch (miniature), and subminiature varieties
Contact at end of plug is the tip
Connector at base of plug is the sleeve
3rd contact (if applicable) between tip and sleeve is the ring (called TRS or tip-ring-sleeve)
Phono plugs/jacks (also called RCA connectors) are used for audio, video and low-level RF signals
Fig. 30: Samples of audio connectors.

## Slide 85: RF Connectors
Fig. 4.31: Each type of RF connector is specially made to carry RF signals and preserve the shielding of coaxial cable. Adapters are available to connect one style of connector to another.

## Slide 86: RF Connectors (cont.)
Radio signals require special connectors for use at RF frequencies
Connectors must have about the same impedance as the feed line (or some of the signal will be reflected by the connector)
Most common connector is the UHF family in Fig. 4.31 (UHF does not refer to frequency)
UHF connectors are typically used up to 150 MHz and can handle legal-limit transmitter power at HF

## Slide 87: RF Connectors (cont.)
UHF connector drawbacks: lack of weather proofing, inconsistent performance above 150 MHz, limited power handling at higher frequencies
Type N series connectors address these drawbacks
  Can be used to 10 GHz
SMA connectors are small threaded connectors designed for miniature coax and are rated to 18 GHz. Handheld transceivers often use SMA connectors to attach antennas.

## Slide 88: Data Connectors
Digital data is exchanged between computers and radio equipment more that ever before in amateur radio
D-type connectors are used for RS-232 (COM port) interfaces
The model number of a D-type connector specifies the number of circuits and a P or S depending upon whether the connector uses pins (male) or sockets (female). For example, D-type 9-pin connectors referred to as DB-9 or DE-9 are used for COM ports on PCs.
The D refers to its shape …

## Slide 89: PRACTICE QUESTIONS

## Slide 90: Which of the following connectors would be a good choice for a serial data port?
PL-259
Type N
Type SMA
DE-9
G2E12 (D) Page 4-40
90

## Slide 91: Which of the following describes a type N connector?
A moisture-resistant RF connector useful to 10 GHz
A small bayonet connector used for data circuits
A threaded connector used for hydraulic systems
An audio connector used in surround-sound installations
G6B07 (A) Page 4-40
91

## Slide 92: What is a type SMA connector?
A large bayonet connector usable at power levels more than 1 KW
A small threaded connector suitable for signals up to several GHz
A connector designed for serial multiple access signals
A type of push-on connector intended for high-voltage applications
G6B11 (B) Page 4-40
92

## Slide 93: Which of these connector types is commonly used for audio signals in Amateur Radio stations?
PL-259
BNC
RCA Phono
Type N
G6B12 (C) Page 4-38
93

## Slide 94: Which of these connector types is commonly used for RF connections at frequencies up to 150 MHz?
Octal
RJ-11
PL-259
DB-25
G6B13 (C) Page 4-39
94

## Slide 95: Basic Test Equipment: Analog & Digital Meters
A volt-ohm-meter (a.k.a. VOM or multimeter) is the simplest and very versatile piece of test equipment. There are two types: analog and digital.
Functions: measures voltage, measures current, measures resistance, checks continuity, tests diodes, tests transistors, frequency counter, measures capacitance, measures inductance, and interfaces to PCs to record readings

## Slide 96: Analog & Digital Meters (cont.)
Digital multimeters (DDM) offer greater precision than analog meters
For finding a peak or minimum reading (for example, when adjusting or tuning a circuit). Experienced hams often prefer analog meters since it’s easier to just watch the analog meter needle move than the display on a digital meter.
Meters should affect the circuit being measured to the smallest degree possible. When measuring voltage, meters should have a high input impedance so that it places the minimum load on the circuit.

## Slide 97: Oscilloscope (or Scope)
Provides a visual display of voltage against time
Display is updated thousands or millions of times per second to give a real-time view of the signal’s characteristics (allows for measurement of fast-changing waveforms that can’t be measured by other meters).
Signals are connected to the scope through horizontal and vertical channel amplifiers. Amplifier gain is variable to adjust vertical sensitivity of the scope’s display.

## Slide 98: Monitoring Oscilloscope
Used for monitoring transmitted signals by connecting the attenuated RF output of the transmitter to the vertical channel of the scope
  This assists in adjusting keying waveforms, microphone gain, and speech processing
  When adjusting keying waveforms, the operator can clearly see the effects of any adjustments or conditions that might cause distortion or key clicks on the transmitted signal

## Slide 99: Impedance & Resonance Measurements
An antenna analyzer contains a CW signal generator, frequency counter, SWR bridge, and impedance meter
  Connects to the antenna feed line to measure SWR without having to transmit a signal at high power
  Measures feed line velocity factor, electrical length, and characteristic impedance, and other parameters
  Because they use small signals, accuracy can be affected by strong signals from nearby transmitters

## Slide 100: Field Strength & RF Power Meters
Other useful tests include antenna efficiency and radiation pattern which is measured with a field strength meter
Field strength meters are often used for comparing relative levels of RF output during antenna and transmitter adjustments
Radiation pattern is measured by placing field strength meter in one location and rotating the antenna. Or, the meter can be carried to different locations to determine radiation pattern of a fixed antenna.

## Slide 101: Field Strength & RF Power Meters (cont.)
Directional wattmeters measure both forward and reflected power (PF and PR) in the line
Standing wave ratio (SWR) can be calculated from forward and reflected power measurements:

## Slide 102: PRACTICE QUESTIONS

## Slide 103: What item of test equipment contains horizontal and vertical channel amplifiers?
An ohmmeter
A signal generator
An ammeter
An oscilloscope
G4B01 (D) Page 4-42
103

## Slide 104: Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
An oscilloscope uses less power
Complex impedances can be easily measured
Input impedance is much lower
Complex waveforms can be measured
G4B02 (D) Page 4-42
104

## Slide 105: Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter?
An oscilloscope
A field strength meter
A sidetone monitor
A wavemeter
G4B03 (A) Page 4-42
105

## Slide 106: What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
The local oscillator of the transmitter
An external RF oscillator
The transmitter balanced mixer output
The attenuated RF output of the transmitter
G4B04 (D) Page 4-42
106

## Slide 107: Why is high input impedance desirable for a voltmeter?
It improves the frequency response
It decreases battery consumption in the meter
It improves the resolution of the readings
It decreases the loading on circuits being measured
G4B05 (D) Page 4-41
107

## Slide 108: What is an advantage of a digital voltmeter as compared to an analog voltmeter?
Better for measuring computer circuits
Better for RF measurements
Better precision for most uses
Faster response
G4B06 (C) Page 4-41
108

## Slide 109: Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments?
A field strength meter
An antenna noise bridge
A multimeter
A Q meter
G4B08 (A) Page 4-43
109

## Slide 110: Which of the following can be determined with a field strength meter?
The radiation resistance of an antenna
The radiation pattern of an antenna
The presence and amount of phase distortion of a transmitter
The presence and amount of amplitude distortion of a transmitter
G4B09 (B) Page 4-43
110

## Slide 111: Which of the following can be determined with a directional wattmeter?
Standing wave ratio
Antenna front-to-back ratio
RF interference
Radio wave propagation
G4B10 (A) Page 4-43
111

## Slide 112: Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
Receiver
Transmitter
Antenna and feed line
All these choices are correct
G4B11 (C) Page 4-42
112

## Slide 113: What problem can occur when making measurements on an antenna system with an antenna analyzer?
Permanent damage to the analyzer may occur if it is operated into a high SWR
Strong signals from nearby transmitters can affect the accuracy of measurements
The analyzer can be damaged if measurements outside the ham bands are attempted
Connecting the analyzer to an antenna can cause it to absorb harmonics
G4B12 (B) Page 4-43
113

## Slide 114: What is a use for an antenna analyzer other than measuring the SWR of an antenna system?
Measuring the front-to-back ratio of an antenna
Measuring the turns ratio of a power transformer
Determining the impedance of coaxial cable
Determining the gain of a directional antenna
G4B13 (C) Page 4-43
114

## Slide 115: What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with digital readout?
When testing logic circuits
When high precision is desired
When measuring the frequency of an oscillator
When adjusting tuned circuits
G4B14 (D) Page 4-41
115

## Slide 116: END OF MODULE 4b

## Slide 117
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.