## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Module 5a ARRL General Class Chapter 5 – Radio Signals & Equipment (5.1, 5.2, 5.3) Basic Modes & Bandwidth, Radio’s Building Blocks, Transmitters

## Slide 4: Basic Modes & Bandwidth: Amplitude Modulated Modes
Varying the power or amplitude of a signal to add speech or data is called amplitude modulation (AM)
This info contained in the signal’s envelope – the max values of the instantaneous power for each cycle
The process of recovering speech or music from the AM envelope is called detection
AM signals are composed of a carrier and two sidebands (upper and lower … USB and LSB)

## Slide 5: Amplitude Modulated Modes (cont.)
AM signal sidebands are steady and unchanging (as long as the tone is transmitted)
Upper sideband is higher in frequency than the carrier; lower sideband is lower in frequency than carrier
AM signal with one sideband removed is a single sideband (SSB)
SSB transmissions have more range than AM because all the SSB’s power is contained in a single sideband. The SSB’s smaller bandwidth makes it possible to fit more signals in a fixed frequency range.

## Slide 6: Frequency & Phase Modulated Modes
Modes that vary the frequency of a signal to add speech or data info are called frequency modulation (FM)
Frequency is varied in proportion to the instantaneous amplitude of the modulating signal
Phase modulation (PM) is created by varying the signal’s phase angle

## Slide 7: Bandwidth Definition
Figure 5.1: The FCC defines bandwidth as “the width of a frequency band outside of which the mean [average] power of the transmitted signal is attenuated at least 26 dB below the mean power.”

## Slide 8: Bandwidth Definition (cont.)
The difference in frequency between the lowest and highest component of a composite signal is the signal’s bandwidth
  See Fig 5.1 for the FCC definition
The FCC limits signal bandwidth so that many stations and types of signals can share the limited amount of spectrum space (see Table 5.1)

## Slide 9: Table 5.1: Amateur Signal Bandwidths Most Common Amateur Signals
Type of Signal | Typical Bandwidth
AM voice | 6 kHz
Amateur television | 6 MHz
SSB voice | 2 to 3 kHz
Digital using SSB | 50 to 3000 Hz (0.05 – 3 kHz)
CW | 100 to 300 Hz (0.1 – 0.3 kHz)
FM voice | 5 to 16 kHz

## Slide 10: PRACTICE QUESTIONS

## Slide 11: What is the name of the process that changes the phase angle of an RF signal to convey information?
Phase convolution
Phase modulation
Phase transformation
Phase inversion
G8A02 (B) Page 5-2
11

## Slide 12: What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
Frequency convolution
Frequency transformation
Frequency conversion
Frequency modulation
G8A03 (D) Page 5-2
12

## Slide 13: What type of modulation varies the instantaneous power level of the RF signal?
Frequency shift keying
Phase modulation
Frequency modulation
Amplitude modulation
G8A05 (D) Page 5-1
13

## Slide 14: Which of the following phone emissions uses the narrowest bandwidth?
Single sideband
Double sideband
Phase modulation
Frequency modulation
G8A07 (A) Page 5-2
14

## Slide 15: Radio’s Building Blocks
Nearly all radios are made up of a few fundamental types of circuits
There’s a variety of ways circuits are built, but basic functions are the same
Radio circuits that perform signal generating and processing functions can also be performed on digital data by software in a radio that uses digital signal processing (DSP). Generally referred to as software-defined radio (SDR).

## Slide 16: Filters
Used to attenuate (reduce in strength) or pass signals
Classified by their response (how they act on signals)
Range of signals passes is the passband
Range of signals attenuated is the stopband (attenuation is also referred to as rejection)

## Slide 17: Figure 5.2 – Generic filter response curves showing how filters of different types affect signals. A larger filter response means less attenuation of the signal cutoff frequencies are shown as fCO.

## Slide 18: Figure 5.2 – Generic filter response curves showing how filters of different types affect signals. A larger filter response means less attenuation of the signal cutoff frequencies are shown as fCO.

## Slide 19: Filters (cont.)
Low-pass filters (Fig 5.2A) pass all frequencies below the cutoff frequency with little or no attenuation. The cutoff frequency (fCO) is the frequency at which the output signal power is reduced to one-half that of the input signal.
High-pass filter (Fig 5.2B) is the opposite; signals are passed above the cutoff frequency and attenuated below.

## Slide 20: Filters (cont.)
Band-pass filters have upper and lower cutoff frequencies. Signals between these are passed … outside are attenuated.
  Frequency range between upper and lower cutoff is the filter’s bandwidth
  Opposite of band-pass is band-stop. Attenuates signals between cutoff frequencies. If stopband is very narrow, that is a notch filter.
Even though filters pass a range of frequencies, they may attenuate signals in the passband. This is called insertion loss.
Outside passband, attenuation may vary, but maximum attenuation is the filter’s ultimate rejection.

## Slide 21: Oscillators
Fig 5.3: An oscillator consists of an amplifier with feedback from the output to input. The product of gain and feedback ratio must be greater than 1 at the frequency of oscillation.

## Slide 22: Oscillators (cont.)
An oscillator consists of an amplifier that increases signal amplitude (gain) and a feedback circuit to route some of the amplifier’s output signal back to its input
Oscillator circuits must include a filter so that feedback is present at only the intended frequency
The oscillator output frequency can be fixed or variable

## Slide 23: Oscillators (cont.)
LC oscillator’s feedback circuits consist of an inductor (L) and capacitor (C) connected (in parallel or series) to form a resonant circuit
  Often called a tank circuit because of their ability to store energy
  The resonant frequency of the LC circuit (determined by the L and C values) is the frequency of the oscillator
The output frequency of a variable-frequency oscillator (VFO) can be adjusted by changing the L or C. VFOs are used to tune a radio to different frequencies.

## Slide 24: Oscillators (cont.)
Two other widely used VFO circuits are …
  Phase-locked loop (PLL)
  Direct digital synthesizer (DDS)
    Controllable by software
    Comparable stability to crystal oscillators
    Used as the high-stability VFO in most current transceivers

## Slide 25: Mixers
Mixers change signals to another frequency
A mixer circuit combines signals with two frequencies, f1 and f2, and produces signals with the sum and difference frequencies at its output (heterodyning)
Example …
  f1 = 14.050 MHz
  f2 = 3.35 MHz
  There will be output signals at 17.4 (f1+f2) and 10.7 (f1-f2) MHz
Fig 5.4: The mixer combines signals of different frequencies, producing signals at the sum and difference frequency.

## Slide 26: Multipliers (see Fig 5.5 in text)
Similar to a mixer
Creates a harmonic of an input frequency
Multipliers are often used when a stable VHF or UHF signal is required that cannot be generated directly at VHF/UHF
A low-frequency oscillator supplies the multiplier input, and the output is tuned to the desired harmonic of the input signal

## Slide 27: Modulators
These circuits add info to a carrier signal by varying the carrier’s amplitude, frequency, or phase
Can be used for AM, FM, or SSB

## Slide 28: Amplitude Modulation
Figure 5.6: The spectrum of 3 types of AM signals. Full AM has both sidebands and the carrier. The carrier is represented by the vertical line in the middle, and the sidebands contain speech or data signals that have been used to modulate the carrier. DSB removes the carrier, but has the same bandwidth as AM. SSB removes one sideband and have the lowest bandwidth of the 3.

## Slide 29: Amplitude Modulation (cont.)
DSB can be produced by a balanced modulator – special mixer where f1 is the carrier and f2 is the modulator
SSB is generated by removing the unwanted sideband and carrier with a filter (filter method) or by combining signals with certain phase relationships (phasing method)
Using only one sideband uses transmitted output power more effectively

## Slide 30: Frequency & Phase Modulation: Figure 5.7
(A) FREQUENCY MODULATION

## Slide 31: Frequency & Phase Modulation: Figure 5.7
(B) PHASE MODULATION

## Slide 32: Frequency & Phase Modulation (cont.)
Frequency modulation (FM) – the signal frequency varies in proportion to modulating signal’s amplitude – called deviation
Phase modulation (PM) – deviation varies with both amplitude and frequency of the modulating signal
  PM is produced by a reactance modulator connected to a tuned RF amplifier following the oscillator
When modulation is applied, the phase of the carrier will be changed, but the average frequency will NOT change

## Slide 33: Quadrature Modulation
Also called I/Q modulation because of the I & Q signals that create the modulated output signal
Used primarily to transmit digital data, but different combinations of I & Q signals can create signals with any form of modulation
The RF output of the combiner consists of a pair of modulated signals that have carrier signals 90° different in phase
Fig 5.8: Block diagram of an I/Q modulator. I and Q are input signals that can be analog signals or streams of digital data.

## Slide 34: PRACTICE QUESTIONS

## Slide 35: Which of the following are basic components of a sine wave oscillator?
An amplifier and a divider
A frequency multiplier and a mixer
A circulator and a filter operating in a feed-forward loop
A filter and an amplifier operating in a feedback loop
G7B07 (D) Page 5-4
35

## Slide 36: What determines the frequency of an LC oscillator?
The number of stages in the counter
The number of stages in the divider
The inductance and capacitance in the tank circuit
The time delay of the lag circuit
G7B09 (C) Page 5-4
36

## Slide 37: Which of the following is an advantage of a direct digital synthesizer (DDS)?
Wide tuning range and no need for band switching
Relatively high-power output
Relatively low power consumption
Variable frequency with the stability of a crystal oscillator
G7C05 (D) Page 5-5
37

## Slide 38: What is the phase difference between the I and Q signals that software-defined radio (SDR) equipment uses for modulation and demodulation?
Zero
90 degrees
180 degrees
45 degrees
G7C09 (B) Page 5-7
38

## Slide 39: What is an advantage of using I and Q signals in software-defined radios (SDRs)?
The need for high resolution analog-to-digital converters is eliminated
All types of modulation can be created with appropriate processing.
Minimum detectible signal level is reduced
Converting the signal from digital to analog creates mixing products
G7C10 (B) Page 5-7
39

## Slide 40: What is meant by the term “software-defined radio” (SDR)?
A radio in which most major signal processing functions are performed by software
A radio that provides computer interface for automatic logging of band and frequency
A radio that uses crystal filters designed using software
A computer model that can simulate performance of a radio to aid in the design process
G7C11 (A) Page 5-3
40

## Slide 41: What is the frequency above which a low-pass filter’s output power is less than half the input power?
Notch frequency
Neper frequency
Cutoff frequency
Rolloff frequency
G7C12 (C) Page 5-4
41

## Slide 42: What term specifies a filter’s maximum ability to reject signals outside its passband?
Notch depth
Rolloff
Insertion loss
Ultimate rejection
G7C13 (D) Page 5-4
42

## Slide 43: The bandwidth of a band-pass filter is measured between what two frequencies?
Upper and lower half-power
Cutoff and rolloff
Pole and zero
Image and harmonic
G7C14 (A) Page 5-4
43

## Slide 44: What term specifies a filter’s attenuation inside its passband?
Insertion loss
Return loss
Q
Ultimate rejection
G7C15 (A) Page 5-4
44

## Slide 45: Which of the following is a typical application for a Direct Digital Synthesizer?
A high-stability variable frequency oscillator in a transceiver
A digital voltmeter
A digital mode interface between a computer and a transceiver
A high-sensitivity radio direction finder
G7C16 (A) Page 5-5
45

## Slide 46: What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
Multiplex modulation
Phase modulation
Amplitude modulation
Pulse modulation
G8A04 (B) Page 5-7
46

## Slide 47: What is another term for the mixing of two RF signals?
Heterodyning
Synthesizing
Cancellation
Phase inverting
G8B03 (A) Page 5-5
47

## Slide 48: What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
Mixer
Reactance modulator
Pre-emphasis network
Multiplier
G8B04 (D) Page 5-5
48

## Slide 49: What combination of a mixer’s Local Oscillator (LO) and RF input frequencies is found in the output?
The ratio
The average
The sum and difference
The arithmetic product
G8B11 (C) Page 5-5
49

## Slide 50: Transmitters: CW Transmitters
Fig 5.9: The simplest transmitter consists of the oscillator and amplifier and a means of turning the output signal on and off – the key (or keyer). A single crystal oscillator can be replaced with a variable-frequency oscillator to allow the transmitter to be tuned to different frequencies.

## Slide 51: CW Transmitters (cont.)
Fig 5.10: By changing the frequency of the local oscillator (LO), the VFO’s output can be shifted from band to band, creating a multiband transmitter. The mixer input always covers the same frequency range.

## Slide 52: SSB Phone Transmitters
Fig 5.11: Substituting the circuits to create an SSB signal for the VFO creates a multiband SSB transmitter.
How to change the CW transmitter to SSB phone …

## Slide 53: SSB Phone Transmitters (cont.)
Voice signals from a mic are processed by a speech amplifier and input to the balanced modulator
The variable frequency oscillator is the other input to the balanced modulator
The output is a DSB signal, so a filter is used to removed the undesired sideband, producing a SSB
Distortion anywhere in the transmit chain will generate unwanted spurious signals (harmonics, mixing products, splatter, etc.)
Refer to Figure 5.11 …..

## Slide 54: FM Transmitters
Fig 5.12: The carrier and modulation are generated at relatively low frequencies in an FM transmitter.
The modulated signal is then multiplied to the desired output frequency. The amount of signal deviation is also multiplied.

## Slide 55: FM Transmitters (cont.)
Modulation and frequency changing are performed differently in FM transmitters (see Figure 12)
It is much more practical to generate the signal at low frequency and multiply it to reach the desired band
In a 2 meter FM transmitter, the modulated oscillator frequency is approximately 12 MHz, and multipliers select the 12th harmonic for transmission. For an output on 146.52 MHz, the oscillator must produce a 146.52 / 12 = 12.21 MHz signal.

## Slide 56: FM Transmitters (cont.)
The frequency deviation is also multiplied. For example, if the 146.52 MHz signal is to have the standard deviation of 5 MHz, the maximum oscillator deviation would be 5 / 12 MHz = 0.416.7 MHz or 416.7 Hz.
Carson’s Rule provides a good approximation of an FM signal’s bandwidth.
BW = 2 × (peak deviation + highest modulating frequency)
Example: If an FM phone signal’s peak deviation is limited to 5 kHz and the highest modulating frequency is 3 kHz, then:
BW = 2 × (5 + 3) = 16 kHz

## Slide 57: Signal Quality
Overmodulation – AM Modes
  An AM or SSB signal that varies excessively in response to the modulating signal
  Distorts transmitted audio
  Causes: Speaking too loudly, mic gain too high, audio gain too high

## Slide 58: Fig. 5.13 – Modulation
The figure shows the modulation envelope of an AM signal, the waveform created by connecting the peaks of the modulated signal – modulation envelope of an SSB signal is similar
Properly modulated signal at (A)
Overmodulation at (B) … distorted signal causes interference on nearby frequencies

## Slide 59: Overmodulation – AM (cont.)
Refer to Fig 5.13B
  Example of cutoff … transmitter output is turned off instead of following the modulated signal
    Flattopping occurs when transmitter output reaches a maximum limit and cannot increase further, even though the modulating signal is increasing
    If output signal is completely cut off between peaks, the result is carrier cutoff
    Both types of overmodulation cause interference by generating spurious signals beyond normal signal bandwidth (called splatter or buckshot)

## Slide 60: Overmodulation – AM (cont.)
ALC (automatic level control) circuits in the transmitter help prevent this … reduces output power during voice peaks
  Controlled by properly setting transmit audio or microphone gain
  Should be adjusted to activate only on voice peaks
Two-tone test monitors transmitter linearity … keeps signal clean
  Only needs to be performed occasionally to note appropriate gain settings and level adjustments

## Slide 61: Controlling Sideband Frequency
Most radios display carrier frequency of the SSB signal
  Actual signal lies entirely above (USB) or below (LSB) this frequency
Each SSB occupies 3 kHz, so you will need to stay far enough from edge of frequency privilege to avoid illegal transmission
For General license holders, using LSB on 40 m, you should operate with carrier frequency at least 3 kHz above the edge of the band segment – 7.178 MHz – thus occupying 7.175 to 7.178 MHz (see Fig 5.14).

## Slide 62: Fig 5.14
When sidebands extend from the carrier toward a band edge or a band segment edge, operate with a displayed carrier frequency no closer than 3 kHz to the edge frequency and be sure your signal is “clean.”

## Slide 63: Key Clicks
Sharp transient clicking sounds heard on adjacent frequencies as a transmitter turns on and off too rapidly during CW transmissions or if transmitter turn on/off erratically.
Fig. 5.15: CW waveforms can be inspected using a monitoring oscilloscope.

## Slide 64: PRACTICE QUESTIONS

## Slide 65: What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver?
The RF clipping level
Transmit audio or microphone gain
Antenna inductance or capacitance
Attenuator level
G2A12 (B) Page 5-11
65

## Slide 66: What signals are used to conduct a two-tone test?
Two audio signals of the same frequency shifted 90 degrees
Two non-harmonically related audio signals
Two swept frequency tones
Two audio frequency range square wave signals of equal amplitude
G4B07 (B) Page 5-11
66

## Slide 67: What type of transmitter performance does a two-tone test analyze?
Linearity
Percentage of suppression of carrier and undesired sideband for SSB
Percentage of frequency modulation
Percentage of carrier phase shift
G4B15 (A) Page 5-11
67

## Slide 68: What is the purpose of a speech processor as used in a modern transceiver?
Increase the intelligibility of transmitted phone signals during poor conditions
Increase transmitter bass response for more natural-sounding SSB signals
Prevent distortion of voice signals
Decrease high-frequency voice output to prevent out-of-band operation
G4D01 (A) Page 5-12
68

## Slide 69: Which of the following describes how a speech processor affects a transmitted single sideband phone signal?
It increases peak power
It increases average power
It reduces harmonic distortion
It reduces intermodulation distortion
G4D02 (B) Page 5-12
69

## Slide 70: Which of the following can be the result of an incorrectly adjusted speech processor?
Distorted speech
Splatter
Excessive background pickup
All these choices are correct
G4D03 (D) Page 5-12
70

## Slide 71: What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
7.178 to 7.181 MHz
7.178 to 7.184 MHz
7.175 to 7.178 MHz
7.1765 to 7.1795 MHz
G4D08 (C) Page 5-12
71

## Slide 72: What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
14.347 to 14.647 MHz
14.347 to 14.350 MHz
14.344 to 14.347 MHz
14.3455 to 14.3485 MHz
G4D09 (B) Page 5-12
72

## Slide 73: How close to the lower edge of the phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
At least 3 kHz above the edge of the segment
At least 3 kHz below the edge of the segment
At least 1 kHz below the edge of the segment
At least 1 kHz above the edge of the segment
G4D10 (A) Page 5-12
73

## Slide 74: How close to the upper edge of the phone segment should your displayed carrier frequency be when using 3 kHz wide USB?
At least 3 kHz above the edge of the band
At least 3 kHz below the edge of the band
At least 1 kHz above the edge of the segment
At least 1 kHz below the edge of the segment
G4D11 (B) Page 5-12
74

## Slide 75: Which of the following describes a linear amplifier?
Any RF power amplifier used in conjunction with an amateur transceiver
An amplifier in which the output preserves the input waveform
A Class C high efficiency amplifier
An amplifier used as a frequency multiplier
G7B10 (B) Page 5-9
75

## Slide 76: Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters?
Carrier oscillator
Filter
IF amplifier
RF amplifier
G7C01 (B) Page 5-9
76

## Slide 77: Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters?
Discriminator
Detector
IF amplifier
Balanced modulator
G7C02 (D) Page 5-9
77

## Slide 78: Which of the following is an effect of overmodulation?
Insufficient audio
Insufficient bandwidth
Frequency drift
Excessive bandwidth
G8A08 (D) Page 5-11
78

## Slide 79: What is meant by the term “flat-topping,” when referring to a single sideband phone transmission?
Signal distortion caused by insufficient collector current
The transmitter’s automatic level control (ALC) is properly adjusted
Signal distortion caused by excessive drive
The transmitter’s carrier is properly suppressed
G8A10 (C) Page 5-10
79

## Slide 80: What is the modulation envelope of an AM signal?
The waveform created by connecting the peak values of the modulated signal
The carrier frequency that contains the signal
Spurious signals that envelop nearby frequencies
The bandwidth of the modulated signal
G8A11 (A) Page 5-10
80

## Slide 81: What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
3 kHz
5 kHz
8 kHz
16 kHz
G8B06 (D) Page 5-10
81

## Slide 82: What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
101.75 Hz
416.7 Hz
5 kHz
60 kHz
G8B07 (B) Page 5-10
82

## Slide 83: Amplifiers
Radio operators (HF) sometimes use amplifiers to boost signals when conditions are poor, to accommodate difficult propagation paths, etc.
On HF, high-power amplifiers often use vacuum tube circuits that require operator adjustment
The efficiency of an amplifier is defined as the RF output power divided by the dc input power
Also called linears

## Slide 84: Four Common Amplifier Classes
Class A – The most linear, lowest signal distortion, least efficient
Class B – Known as push-pull, pair of amplifying devices each active during complementary halves of the signal’s cycle, good linearity, good efficiency
Class AB – Midway between A and B, linearity not as good as A, but efficiency is improved
Class C – Highest efficiency, only suitable for CW and FM (due to poor linearity)

## Slide 85: Amplifiers (cont.)
Some linear amplifiers can be operated in either Class AB for SSB operation or in Class C for CW
Transceivers often include a delay in the keying circuit timing so that the changeover relay is completely switched before transceiver is allowed to supply any RF output
  Prevents hot-switching in which amplifier is already supplying RF
  Can destroy the relay or other external devices

## Slide 86: Tuning Vacuum Tube Amplifiers
Set BAND switch to desired frequency
Apply drive power to amplifier while adjusting TUNE control to obtain minimum plate current (dip)
Adjust LOAD to obtain peak output power
Continue adjusting until max output power is obtained
Avoid exceeding max plate current
Input power to amplifier may also be adjusted during this process

## Slide 87: Amplifiers (cont.)
Tubes can be destroyed by applying too much drive
Modern amplifiers have protective circuits
Be sure to operate amplifier according to manufacturer specifications
Similar cautions apply to solid-state amplifiers with power transistors that can be destroyed with excessive drive power
Some amplifiers generate automatic leveling control (ALC) signals that can be connected to the transmitter to limit excess drive. Check both the amplifier and transceiver manuals to be sure signals are compatible and so you know how to use the ALC meter readings.

## Slide 88: Neutralization
HF amplifiers can self-oscillate because of positive feedback in an amplifier tube
Self-oscillation creates spurious output signals and may damage the tube or amplifier components
The technique of preventing self-oscillation is called neutralization
  Done by creating negative feedback (small variable capacitor between amplifier’s output and input circuits)

## Slide 89: PRACTICE QUESTIONS

## Slide 90: What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control?
A pronounced peak
A pronounced dip
No change will be observed
A slow, rhythmic oscillation
G4A04 (B) Page 5-15
90

## Slide 91: What is a reason to use Automatic Level Control (ALC) with an RF power amplifier?
To balance the transmitter audio frequency response
To reduce harmonic radiation
To reduce distortion due to excessive drive
To increase overall efficiency
G4A05 (C) Page 5-15
91

## Slide 92: What condition can lead to permanent damage to a solid-state RF power amplifier?
Insufficient drive power
Low input SWR
Shorting the input signal to ground
Excessive drive power
G4A07 (D) Page 5-15
92

## Slide 93: What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier?
Minimum SWR on the antenna
Minimum plate current without exceeding maximum allowable grid current
Highest plate voltage while minimizing grid current
Maximum power output without exceeding maximum allowable plate current
G4A08 (D) Page 5-15
93

## Slide 94: Why is a time delay sometimes included in a transmitter keying circuit?
To prevent stations from interfering with one another
To allow the transmitter power regulators to charge properly
To allow time for transmit-receive changeover operations to complete properly before RF output is allowed
To allow time for a warning signal to be sent to other stations
G4A09 (C) Page 5-14
94

## Slide 95: What is the reason for neutralizing the final amplifier stage of a transmitter?
To limit the modulation index
To eliminate self-oscillations
To cut off the final amplifier during standby periods
To keep the carrier on frequency
G7B01 (B) Page 5-15
95

## Slide 96: Which of these classes of amplifiers has the highest efficiency?
Class A
Class B
Class AB
Class C
G7B02 (D) Page 5-14
96

## Slide 97: How is the efficiency of an RF power amplifier determined?
Divide the DC input power by the DC output power
Divide the RF output power by the DC input power
Multiply the RF input power by the reciprocal of the RF output power
Add the RF input power to the DC output power
G7B08 (B) Page 5-14
97

## Slide 98: For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal?
SSB
FM
AM
All these choices are correct
G7B11 (B) Page 5-14
98

## Slide 99: END OF MODULE 5a

## Slide 100
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.