## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Module 5b ARRL General Class Chapter 5 – Radio Signals & Equipment (5.4, 5.5) Receivers, HF Station Installation

## Slide 4: Superheterodyne Receivers
Most receivers use by today’s amateurs are superheterodyne
Received signals are incredibly weak – on the order of nano or picowatts
  Received signals are first strengthened by the RF amplifier, then applied to the RF input of a mixer
  The local oscillator (LO) is adjusted so that the desired signal creates a mixing product at the intermediate frequency (IF)
  A detector or demodulator stage follows the IF to recover the modulating information

## Slide 5: Superheterodyne Receivers (cont.)
The simplest possible superhet consists of a mixer connected to the antenna, an oscillator to act as the LO, and a detector that operates directly on the resulting IF signal
  See Figure 5.16

## Slide 6: Fig. 5.16
A superheterodyne receiver converts signals to audio in two steps. The front end converts the frequency of a signal to the intermediate frequency (IF) where most of the gain of the receiver is provided. A second mixer – the product detector – converts the signal to audio frequencies.

## Slide 7: Superheterodyne Receivers (cont.)
Once amplified to a more usable level, SSB and CW signals are demodulated by a product detector, a special type of mixer
If an AM signal is being received, a product detector or envelope detector recovers the modulating signal
Output of the detector is an audio signal amplified by an audio frequency (AF) amplifier and input to a speaker, headphones, or sound card

## Slide 8: Fig 5.17: Once the FM signal is converted to the IF, hi-gain amplifiers called limiters change the signal to a square wave that only varies in frequency (not amplitude). A discriminator converts the frequency variations to audio.

## Slide 9: Superheterodyne Receivers (cont.)
The RF amplifier and mixer are the receivers front end
  Processes weak signals at their original frequencies
  A preselector is often used to reject out-of-band signals
  A preamplifier (preamp) is used if additional sensitivity is needed (weak signals)

## Slide 10: FM Receivers (Fig. 5.17)
Similar to AM/SSB/CW superhets
  The linear IF amplifier is replaced by a limiter
    Limiter amplifies the received signal until all amplitude modulated info (noise) is removed and only a square wave of the varying frequency remains
    Audio information is recovered by a discriminator or quadrature detector that replaces the product detector
Superhets have some weaknesses, like all radio designs
  Because there are mixing products at both the sum and difference frequencies, undesired signals can create their own mixing products at the IF … see next slide for examples (refer to Fig 5.4)

## Slide 11: Superhet Mixer Weakness Example (see Fig 5.4)
In a mixer, with an RF Input or Input Frequency (f1) and Local Oscillator (f2), remember there are mixing products at …
f1 ± f2 meaning f1 + f2 AND f1 – f2
With IF = 455 kHZ (0.455 MHz) and LO = 13.800 MHZ, you will have signals at …
f1 ± f2 = 13.800 + 0.455 and 13.800 – 0.455 or 14.255 and 13.345 MHz
The signals at 14.255 and 13.345 will create their OWN mixing products. The first will be at 14.225 – 13.800 (LO) = 455 kHz. The second will be at 13.800 (LO) – 13.345 = 455 kHz.
Assuming the receiver is set at 14.255 MHz, the undesired signal at 13.345 MHz is an image response.

## Slide 12: FM Receivers (cont.)
Another flaw is caused by the LO and other oscillator circuits. Leakage of signals into the signal path can cause steady signals to appear (called birdies).
Figs 5.16 and 5.17 show single-conversion receivers, with only one mixer converting the signal from RF to IF
  The IF stages provide most of the gain and selectivity
  Filtering is applied at each IF (allows filter bandwidth selection for desired signal) … this gives the best received signal quality with the lowest unwanted noise and interference, maximizing the signal-to-noise ratio (SNR)

## Slide 13: Digital Signal Processing (DSP)
The general term for converting signals from analog to digital is digital signal processing
Fig 5.18 (below): DSP systems use an analog-to-digital converter (ADC) to change the signal to digital data. A special type of microprocessor then performs the mathematical operations on the data to accomplish filtering, noise reduction, or other functions. A digital-to-analog converter (DAC) changes the processed data back to analog form for output as audio.

## Slide 14: Digital Signal Processing (cont.)
Two advantages over analog circuitry
  Performance & flexibility
DSP offers selectable preprogrammed filters and allow the operator to adjust the filter bandwidth and shape and even to define new filters
Expensive functions in analog circuits can be implemented in DSP as a program without additional hardware

## Slide 15: Managing Receiver Gain (RF Gain)
When looking for weak signals, set RF gain to maximum (for highest receiver sensitivity)
Lower RF gain volume to reduce background noise
Automatic gain control (AGC) circuits vary gain of the RF and IF amplifiers so output volume stays constant for both weak and strong signals
  AGC circuit changes the voltage that controls the IF amp gain. This voltage is read by the S-meter (measures signal strength).

## Slide 16: RF Gain and AGC (cont.)
S-meters are calibrated in S-units
  One S-unit equals up to 6dB (fourfold) change in signal strength
S-9 (a strong signal) is located at the midpoint of the display
  Larger values to the right (20, 40, 60)
  These correspond to “dB above S-9”
Reading of “S-9 + 20 dB” is a signal 20 dB (100 times) stronger than an S-9 signal

## Slide 17: Receiver Linearity
If the received signal is distorted, spurious signals will appear just as if a transmitting station were emitting them
The most common form of receiver nonlinearity is overload (also called front-end overload) or gain compression
Solution to overload is to filter out the offending signal or reduce receiver gain (attenuator circuit). Proper use of attenuator and RF gain controls can dramatically reduce received noise distortion caused by strong signals.

## Slide 18: Rejecting Interference and Noise
IF filters narrow the receiver’s passband (removes unwanted signals)
Notch filters remove signals in a very narrow band of frequencies (such as a signal tone from an interfering carrier)
Passband or IF shift adjust receiver’s passband above or below the displayed carrier frequency (avoids interference on adjacent frequencies)
Reverse sideband controls allow switching between receiving CW signals above carrier frequency (USB) and below it (LSB). Avoids interference by placing the signals on the “other side” of the carrier where filtering rejects them.

## Slide 19: Rejecting Interference and Noise (cont.)
Noise blankers sense short, sharp pulses in the IF signals and reduce the gain of the IF and audio amplifiers during the pulse … called blanking
  If noise blankers are adjustable, it can be set to blank the receiver at different noise levels
Noise reduction is performed by the DSP.
  Removes hiss and noise from the audio that is not part of the desired speech, data, or CW
  Increasing the noise reduction level may cause some of the desired signal to be removed (causes distortion) … use the least noise reduction require to minimize this

## Slide 20: PRACTICE QUESTIONS

## Slide 21: What is the purpose of the “notch filter” found on many HF transceivers?
To restrict the transmitter voice bandwidth
To reduce interference from carriers in the receiver passband
To eliminate receiver interference from impulse noise sources
To enhance the reception of a specific frequency on a crowded band
G4A01 (B) Page 5-20
21

## Slide 22: What is one advantage of selecting the opposite, or “reverse,” sideband when receiving CW signals on a typical HF transceiver?
Interference from impulse noise will be eliminated
More stations can be accommodated within a given signal passband
It may be possible to reduce or eliminate interference from other signals
Accidental out-of-band operation can be prevented
G4A02 (C) Page 5-20
22

## Slide 23: Which of the following is a use for the IF shift control on a receiver?
To avoid interference from stations very close to the receive frequency
To change frequency rapidly
To permit listening on a different frequency from that on which you are transmitting
To tune in stations that are slightly off frequency without changing your transmit frequency
G4A11 (A) Page 5-20
23

## Slide 24: What is one reason to use the attenuator function that is present on many HF transceivers?
To reduce signal overload due to strong incoming signals
To reduce the transmitter power when driving a linear amplifier
To reduce power consumption when operating from batteries
To slow down received CW signals for better copy
G4A13 (A) Page 5-19
24

## Slide 25: How does a noise blanker work?
By temporarily increasing received bandwidth
By redirecting noise pulses into a filter capacitor
By reducing receiver gain during a noise pulse
By clipping noise peaks
G4A16 (C) Page 5-20
25

## Slide 26: What happens as the noise reduction control level in a receiver is increased?
Received signals may become distorted
Received frequency may become unstable
CW signals may become severely attenuated
Received frequency may shift several kHz
G4A17 (A) Page 5-20
26

## Slide 27: Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter?
A wide range of filter bandwidths and shapes can be created
Fewer digital components are required
Mixing products are greatly reduced
The DSP filter is much more effective at VHF frequencies
G4C12 (A) Page 5-18
27

## Slide 28: What does an S meter measure?
Conductance
Impedance
Received signal strength
Transmitter power output
G4D04 (C) Page 5-19
28

## Slide 29: How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
It is 10 times less powerful
It is 20 times less powerful
It is 20 times more powerful
It is 100 times more powerful
G4D05 (D) Page 5-19
29

## Slide 30: Where is an S meter found?
In a receiver
In an SWR bridge
In a transmitter
In a conductance bridge
G4D06 (A) Page 5-19
30

## Slide 31: How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
Approximately 1.5 times
Approximately 2 times
Approximately 4 times
Approximately 8 times
G4D07 (C) Page 5-19
31

## Slide 32: What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver?
Balanced modulator
IF amplifier
Mixer
Detector
G7C03 (C) Page 5-16
32

## Slide 33: What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers?
RF oscillator
IF filter
Balanced modulator
Product detector
G7C04 (D) Page 5-17
33

## Slide 34: What is the simplest combination of stages that implement a superheterodyne receiver?
RF amplifier, detector, audio amplifier
RF amplifier, mixer, IF discriminator
HF oscillator, mixer, detector
HF oscillator, prescaler, audio amplifier
G7C07 (C) Page 5-16
34

## Slide 35: What circuit is used in analog FM receivers to convert IF output signals to audio?
Product detector
Phase inverter
Mixer
Discriminator
G7C08 (D) Page 5-18
35

## Slide 36: Which mixer input is varied or tuned to convert signals of different frequencies to an intermediate frequency (IF)?
Image frequency
Local oscillator
RF input
Beat frequency oscillator
G8B01 (B) Page 5-16
36

## Slide 37: If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, what type of interference will a 13.345 MHz signal produce in the receiver?
Quadrature noise
Image response
Mixer interference
Intermediate interference
G8B02 (B) Page 5-18
37

## Slide 38: Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
It is required by FCC rules
It minimizes power consumption in the receiver
It improves impedance matching of the antenna
It results in the best signal-to-noise ratio
G8B09 (D) Page 5-18
38

## Slide 39: HF Installation
HF operating, with loner wavelengths and higher field strengths, makes grounding and interference control much more important
The General Exam focuses on three related areas …
  Mobile installations
  RF grounding
  RF interference

## Slide 40: Mobile Installations – Power Connections
Mobile radios that can output 100 W require solid power connections capable of supplying 20 A or more
  Solid state radios perform unpredictably with input voltage drops below the specified minimum power supply voltage
Best power connection is direct to battery, heavy gauge wire, with both leads fused
  Do NOT use cigarette lighter socket … usually rated for on a few amperes, and insufficient to supply a 100 W HF radio

## Slide 41: Mobile Installations – Antenna Connections
A limitation of mobile installations is that electrically short (smaller in terms of wavelength) antennas are less efficient that full-sized ones
  Particularly true on lower frequency bands
Tips to improve antenna performance
  Use most efficient antenna you can
  Make sure your ground connections to vehicle are solid
  Mount antenna where it is clear of metal surfaces

## Slide 42: Mobile Interference
Different interference sources than home stations
  Ignition noise (spark plugs firing) … n/a in diesel engines
  Alternator whine
  Vehicle’s accessories
  On-board control computers
  Electric motors in fuel pumps, windows, and battery charging systems
  Winch motors in 4X4 vehicles & trucks

## Slide 43: Grounding & Bonding
AC grounding prevents hazardous voltages from appearing on equipment chassis, creating a shock hazard
To manage RF, bond equipment enclosures together (see Fig 5.19) … Bonding means to connect two points together to minimize voltage differences between them
During digital operation, unwanted RF currents can cause distortion, erratic operation of computer interfaces, activate transmitter improperly, and garble digital protocols

## Slide 44: Grounding & Bonding (cont.)
Bonding basics …
  Connect all metal equipment enclosures directly together or to a common RF bonding bus
  Keep connections, straps, and wires SHORT
  Use short, heavy conductors (#12 or #14 AWG) or strap
  If strong RF is present, use a piece of wide flashing or screen under the equipment, connected to the bonding bus
If ground connection is resonant at an odd number of ¼ wavelengths, it will generate high impedance, enabling RF voltages to exist on enclosures and cables

## Slide 45: Grounding & Bonding (cont.)
Ground loops are created by a continuous current path around a series of equipment connections
Loop acts as a single-turn inductor … picks up voltages from magnetic fields (from transformers, ac wiring, etc.)
Result is a “hum” in transmitted signals or that interferes with control or data signals
Ground loops can be avoided by connecting all ground conductors to the RF bonding bus

## Slide 46: RF Interference (RFI): Causes & Solutions
RFI | CAUSE | SOLUTION
Fundamental Overload | Radio/TV receivers unable to reject strong signals … causes distortion or inability to receive desired signal | Prevent signal by using filters in signal path
Common-mode & Direct pickup | From electronic equipment with internal electronics … picked up on outside of cable shields and conductors of unshielded connections | Block current with RF chokes
Harmonics | Spurious emissions from an amateur station may be received by radio or TV equipment | Use a low-pass filter at the transmitter
Intermodulation | Poor contacts between conductors picking up RF signals can create a nonlinear connection that acts as a mixer and mixing products from the signals | Find/repair the poor contact or block the RF signals
Arcing | A spark or sustained arc creates radio crackling or buzz over wide frequency range, (from power-line hardware) | May require power company to make repairs; filter specific equip.

## Slide 47: Common RFI Symptoms
RFI is quite varied
Some more common types are …
  CW, FM, or data: Interference consists of ON/OFF buzzes, humming, clicks or thumps when the interfering signal is transmitted
  AM phone: Equipment experiencing overload or direct detection will often emit a replica of the speaker’s voice
  SSB voice: Similar to AM phone, but voice will be distorted or garbled

## Slide 48: Suppressing RFI
Filters are effective and easy to install
Block RF by placing an impedance in its path
  Form conductor carrying RF current into an RF choke by winding it around or through a ferrite core
Ferrite beads placed on cables to prevent RF common-mode from flowing on outside of cables/shields
Interference to audio equipment and sensor connections can be eliminated by using a small (100 pF to 1 nF) bypass capacitor across balanced connections

## Slide 49: Fig 5.19

## Slide 50: PRACTICE QUESTIONS

## Slide 51: Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver?
The VOX circuit does not un-key the transmitter
The transmitter signal is distorted
Frequent connection timeouts
All these choices are correct
G4A15 (D) Page 5-22
51

## Slide 52: Which of the following might be useful in reducing RF interference to audio frequency devices?
Bypass inductor
Bypass capacitor
Forward-biased diode
Reverse-biased diode
G4C01 (B) Page 5-24
52

## Slide 53: Which of the following could be a cause of interference covering a wide range of frequencies?
Not using a balun or line isolator to feed balanced antennas
Lack of rectification of the transmitter’s signal in power conductors
Arcing at a poor electrical connection
Using a balun to feed an unbalanced antenna
G4C02 (C) Page 5-24
53

## Slide 54: What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter?
A steady hum whenever the transmitter is on the air
On-and-off humming or clicking
Distorted speech
Clearly audible speech
G4C03 (C) Page 5-24
54

## Slide 55: What is the effect on an audio device when there is interference from a nearby CW transmitter?
On-and-off humming or clicking
A CW signal at a nearly pure audio frequency
A chirpy CW signal
Severely distorted audio
G4C04 (A) Page 5-24
55

## Slide 56: What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod?
Flat braid rather than round wire has been used for the ground wire
Insulated wire has been used for the ground wire
The ground rod is resonant
The ground wire has high impedance on that frequency
G4C05 (D) Page 5-23
56

## Slide 57: What effect can be caused by a resonant ground connection?
Overheating of ground straps
Corrosion of the ground rod
High RF voltages on the enclosures of station equipment
A ground loop
G4C06 (C) Page 5-23
57

## Slide 58: Which of the following would reduce RF interference caused by common-mode current on an audio cable?
Placing a ferrite choke around the cable
Adding series capacitors to the conductors
Adding shunt inductors to the conductors
Adding an additional insulating jacket to the cable
G4C08 (A) Page 5-24
58

## Slide 59: How can a ground loop be avoided?
Connect all ground conductors in series
Connect the AC neutral conductor to the ground wire
Avoid using lock washers and star washers when making ground connections
Connect all ground conductors to a single point
G4C09 (D) Page 5-23
59

## Slide 60: What could be a symptom of a ground loop somewhere in your station?
You receive reports of “hum” on your station’s transmitted signal
The SWR reading for one or more antennas is suddenly very high
An item of station equipment starts to draw excessive amounts of current
You receive reports of harmonic interference from your station
G4C10 (A) Page 5-23
60

## Slide 61: What technique helps to minimize RF “hot spots” in an amateur station?
Building all equipment in a metal enclosure
Using surge suppressor power outlets
Bonding all equipment enclosures together
Low-pass filters on all feed lines
G4C11 (C) Page 5-22
61

## Slide 62: Why must the metal enclosure of every item of station equipment be grounded?
It prevents a blown fuse in the event of an internal short circuit
It prevents signal overload
It ensures that the neutral wire is grounded
It ensures that hazardous voltages cannot appear on the chassis
G4C13 (D) Page 5-22
62

## Slide 63: Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation?
To the battery using heavy-gauge wire
To the alternator or generator using heavy-gauge wire
To the battery using resistor wire
To the alternator or generator using resistor wire
G4E03 (A) Page 5-21
63

## Slide 64: Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle’s auxiliary power socket?
The socket is not wired with an RF-shielded power cable
The socket’s wiring may be inadequate for the current drawn by the transceiver
The DC polarity of the socket is reversed from the polarity of modern HF transceivers
Drawing more than 50 watts from this socket could cause the engine to overheat
G4E04 (B) Page 5-21
64

## Slide 65: Which of the following most limits an HF mobile installation?
“Picket fencing”
The wire gauge of the DC power line to the transceiver
Efficiency of the electrically short antenna
FCC rules limiting mobile output power on the 75-meter band
G4E05 (C) Page 5-21
65

## Slide 66: Which of the following may cause receive interference in a radio installed in a vehicle?
The battery charging system
The fuel delivery system
The vehicle control computer
All these choices are correct
G4E07 (D) Page 5-22
66

## Slide 67: How does a ferrite bead or core reduce common-mode RF current on the shield of a coaxial cable?
By creating an impedance in the current’s path
It converts common-mode current to differential mode
By creating an out-of-phase current to cancel the common-mode current
Ferrites expel magnetic fields
G6B10 (A) Page 5-24
67

## Slide 68: What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted?
Substantially higher
About the same
Substantially lower
Twice the transmission line impedance
G7C06 (B) Page 5-23
68

## Slide 69: What process combines two signals in a non-linear circuit or connection to produce unwanted spurious outputs?
Intermodulation
Heterodyning
Detection
Rolloff
G8B12 (A) Page 5-24
69

## Slide 70: END OF MODULE 5b

## Slide 71
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.