## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Module 6 ARRL General Class Chapter 6 – Digital Modes (6.1, 6.2, 6.3, 6.4) Basics of Digital Modes, Character-Based Modes, Packet-Based Modes & Systems, Receiving & Transmitting Digital Modes

## Slide 4: Basics of Digital Modes: Where to Find Digital Activity
Communications are digital modes if info is exchanged as individual characters encoded as digital bits … Morse Code (CW), radioteletype, PSK31, FT8, D-STAR, DMR, slow-scan TV, etc.
Digital modes restricted to CW/data segments of each HF band
  Found near top of CW segment
  Example: On 20 meters, most PSK signals are near 14.070 MHz. RTTY and other digital modes are found above that between 14.070 and 14.112 MHz. Also see Table 6.1.

## Slide 5: Digital Modes Overview
Data rates and bandwidths specified by FCC rules
Digital codes not specified by the FCC must be public
Radioteletype (RTTY) – originally used mechanical teleprinters but migrated to computer sound cards
PSK31 – good weak signal mode using low transmitter power and very narrow bandwidth (computer sound card)
PACTOR – stands for PACket Teletype Over Radio
WINMOR – stands for WINdows Messaging Over Radio
Packet Radio – common on the VHF and UHF bands (1200 & 9600 baud)

## Slide 6: Table 6.1: Digital Signal Band Plan (HF Bands)
Band (meters) | Frequency Range (MHz) | Notes
160 | 1.800 – 1.810 | FT8 is on 1.840 MHz
80 | 3.570 – 3.600 | 
60 | 5332, 5348, 5358.5, 5373, 5405 kHz | Channel center frequencies
40 | 7.070 – 7.125 | RTTY DX calling frequency 7.040
30 | 10.130 – 10.150 | 
20 | 14.070 – 14.0995 and 14.1005 – 14.112 | PSK31 calling frequency 14.070
17 | 18.100 – 18.110 | 
15 | 21.070 – 21.110 | 
12 | 24.920 – 24.930 | 
10 | 28.070 – 28.189 | 

## Slide 7: Definitions
Air link: the part of the comm system that involves radio transmission and reception of signals
Bit: the fundamental unit of data; a 0 or 1 representing all or part of a binary number
Bit rate: number of digital bits/second sent from one system to another
Baud(s): number of symbols/second sent from one system to another
Duty cycle: ratio of time that transmitter is on to total time plus off time
Protocol: rules that control the method used to exchange data between systems
Mode: combination of a protocol with a modulation method

## Slide 8: Frequency Shift Keying (FSK)
Individual bits of data encoded as tones
  As data are transmitted, different tone frequencies are used
The frequencies in a two-tone FSK signal are called mark and space
  Space represents 0, mark represents 1
In “direct” FSK, the frequency of the transmitter’s VFO is controlled by a digital data signal from the computer
Audio FSK (AFSK) – audio tones modulate an SSB or FM transmitter through the mic input
Multiple FSK – more than 2 tones are used to create more codes
VFO = variable frequency oscillator

## Slide 9: Phase Shift Keying (PSK)
Most common type of phase shift is to invert one of the tone waveforms (shifting phase 180°)
Rapid changes in phase can be heard from human ear as a raspy noise of buzz – the signature of PSK signals on the air received by a CW or SSB receivers (sort of like the sound on an old computer modem)

## Slide 10: PRACTICE QUESTIONS

## Slide 11: What segment of the 20-meter band is most often used for digital transmissions (avoiding the DX propagation beacons)?
14.000 - 14.050 MHz
14.070 - 14.112 MHz
14.150 - 14.225 MHz
14.275 - 14.350 MHz
G2E04 (B) Page 6-2
11

## Slide 12: What segment of the 80-meter band is most commonly used for digital transmissions?
3570 — 3600 kHz
3500 — 3525 kHz
3700 — 3750 kHz
3775 — 3825 kHz
G2E07 (A) Page 6-2
12

## Slide 13: In what segment of the 20-meter band are most PSK31 operations commonly found?
At the bottom of the slow-scan TV segment, near 14.230 MHz
At the top of the SSB phone segment, near 14.325 MHz
In the middle of the CW segment, near 14.100 MHz
Below the RTTY segment, near 14.070 MHz
G2E08 (D) Page 6-2
13

## Slide 14: How is an FSK signal generated?
By keying an FM transmitter with a sub-audible tone
By changing an oscillator’s frequency directly with a digital control signal
By using a transceiver’s computer data interface protocol to change frequencies
By reconfiguring the CW keying input to act as a tone generator
G8A01 (B) Page 6-4
14

## Slide 15: How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
Dot and dash
On and off
High and low
Mark and space
G8C11 (D) Page 6-4
15

## Slide 16: Character-Based Modes
Simplest use of digital communications is a mode in which individual characters are entered by an operator, then transmitted to another station where they are read by another operator (CW, for example)
Speeds are low, but convenient to use and require little additional equipment other than sound card or modem
Sometimes referred to as keyboard-to-keyboard or chat
Transmit a stream of characters without additional data

## Slide 17: RTTY: Oldest form of ham radio digital communications
Fig 6.1: The Baudot timing sequence for the bit pattern that encodes the letter “D”. The start bit is sent first. Start and stop bits are required to allow the receiving and transmitting systems to synchronize. Mark and space are represented as audio tones in the transmitted signal. Baudot is origin of term baud.

## Slide 18: Radioteletype (RTTY)
RTTY uses Baudot code which represents each text character as a sequence of 5 bits
  5 bits only allow for 32 different characters … not enough for entire English alphabet, numerals, and punctuation
  2 special codes (LTRS & FIGS) are use to switch between 2 character sets (doubling number of available characters)
The difference between the mark and space tones (see Fig 6.1) is called the signal’s shift
You should always answer an RTTY station at same speed and shift it’s using

## Slide 19: PSK31 (Phase Key Shifting)
Most popular PSK mode (also called 31 Baud)
Uses a sound card to generate RTTY signals
“31” is the symbol rate of the protocol (actually 31.25 baud)
Designed for keyboard-to-keyboard communication (typing rates up to 50 wpm)
QPSK31 (quadrature PSK31) sends TWO audio tones, so there are now four possible phase shift combinations

## Slide 20: PSK31 (cont.)
Since PSK has two tones, you have to select the right sideband (USB or LSB) to decode the data … sideband sensitive
QPSK31 / PSK31 have about the same bandwidth (2.5 kHz)
PSK uses a variable length character code called Varicode that assigns shorter codes to common characters and longer codes for uncommon characters (like Morse code)
  Capital letters & punctuation take longer to send
  If you’re used to RTTY (no lower case), turn off CAPS LOCK!

## Slide 21: Packet-Based Modes & Systems
Packet-based or structured modes are derived from early teletype-over-radio modes and computer-to-computer network protocols
Hams have adapted these protocols, creating packet radio, PACTOR, WINMOR, and other communication systems
Some packet modes (JT65 & FT8) require precisely-defined transmission periods … utility software is available to keep your computer synchronized to within 1 second of standard time

## Slide 22: Packet Basics
Packet refers to the transmission of data in structured groups (called frames)
Figure 6.2: Packet communication systems package data with control and routing information and add error detection information. Each package of header, data, and trailer is called a frame. Different packet protocols use different sets of information and methods of creating the frame.

## Slide 23: Packet Basics (cont.) … see Fig 6.2
Header – Contains bit patterns that allow receiver to synch with the packet’s structure, control, and routing information, and for some protocols, error detection/correction information.
Data – Data to be exchanged between the systems. Usually ASCII characters. Usually compressed for efficiency.
Trailer – Additional info used for error detection.
  Forward error correction (FEC) goes beyond simply detecting errors. By including redundant encoded info with the data, it’s possible for receiver to CORRECT certain types of data errors.

## Slide 24: Automatic Repeat reQuest (ARQ) Systems
If mismatch is detected, receiving system responds with NAK (not acknowledged) and protocol requests retransmission.
Transmitting system will continue to send packet until received without errors or retransmission limit is exceeded.
ARQ used in modes: PACTOR, packet radio, WINMOR, etc.
ARQ protocols were designed for wired network connections, and the transmission can only be received from one receiving station during the connection. This means you can’t break in to an ongoing contact between two stations using an ARQ mode.

## Slide 25: ARQ (cont.)
So that a station can advertise its presence, ARQ protocols provide a broadcast mode to transmit without another station having established a contact
A MON mode is also provided so that other stations can listen to the conversation without error correction
Using the MON (monitoring) mode allows you to determine if a frequency is occupied by 2 stations having an ARQ mode contact

## Slide 26: Packet Radio
Used almost exclusively on VHF and UF bands
Based on computer network protocol X.25
  One of the oldest packet-switching communication protocols
  X.25 protocol popular during the late 1970s and 1980s in the computer industry
Packets are exchanged using VHF FM voice transceivers at 1200 or 9600 baud
Does not work well with HF because data are easily disrupted by noise and fading (even at 300 baud allowed on HF)

## Slide 27: PACTOR and WINMOR
RTTY protocol was not designed to manage transmission errors
Teletype Over Radio (TOR) systems were developed to address this (AMTOR, G-TOR, etc.)
These original TOR protocols are reliable, but slow
PACTOR (Packet-based TOR) and WINMOR (Windows TOR) addresses reliability AND speed … and extends TOR capability
PACTOR 1 uses FSK modulation; PACTOR 1 thru 4 use advanced PSK modulation (PACTOR 4 not yet legal for US amateurs)

## Slide 28: WINLINK
Enables transferring of email messages & digital files on HF bands
Winlink isn’t a mode … it’s a communication system
Uses the internet to connect its email servers with gateway and mailbox stations around the world on HF, VHF and UHF
  Winlink stations do not connect directly with the internet, but provide an effective means for stations out of local internet connection range
  Even without internet connectivity, Winlink Express can act as standalone mailbox stations or communicate directly with each other

## Slide 29: FT8 & WSPR (WS = Weak Signal)
Supported by the WSJT software suite (and JT65, MSK144, etc.)
  https://physics.princeton.edu/pulsar/k1jt/
Uses precisely-timed sequences of transmit/receive, 8-tone FSK modulation and error decoding/correction to enable successful decoding at very low signal-to-noise ratios (SNR)
FT8 exchanges 75-bit messages … there is a limited amount of info that can be exchanged with this size limit (call signs, grid locators, signal reports)
WSPR uses HF propagation paths at very low SNR … does not support 2-way QSOs
Low power WSPR transmitters generate coded packets; stations that receive these report success on www.wsprnet.org

## Slide 30: PRACTICE QUESTIONS

## Slide 31: How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations?
Unplug the data connector temporarily and see if the channel-busy indication is turned off
Put the modem or controller in a mode which allows monitoring communications without a connection
Transmit UI packets several times and wait to see if there is a response from another PACTOR station
Send the message, ”Is this frequency in use?”
G2E02 (B) Page 6-7
31

## Slide 32: How do you join a contact between two stations using the PACTOR protocol?
Send broadcast packets containing your call sign while in MONITOR mode
Transmit a steady carrier until the PACTOR protocol times out and disconnects
Joining an existing contact is not possible, PACTOR connections are limited to two stations
Send a NAK response continuously so that the sending station must stand by
G2E09 (C) Page 6-7
32

## Slide 33: Which of the following is characteristic of the FT8 mode of the WSJT-X family?
It is a keyboard-to-keyboard chat mode
Each transmission takes exactly 60 seconds
It is limited to use on VHF
Typical exchanges are limited to call signs, grid locators, and signal reports
G2E11 (D) Page 6-9
33

## Slide 34: Which communication system sometimes uses the internet to transfer messages?
Winlink
RTTY
ARES
SKYWARN
G2E13 (A) Page 6-8
34

## Slide 35: Which of the following is a requirement when using the FT8 digital mode?
A special hardware modem
Computer time accurate within approximately 1 second
Receiver attenuator set to -12 dB
A vertically polarized antenna
G2E15 (B) Page 6-6
35

## Slide 36: What type of modulation is used by the FT8 digital mode?
8-tone frequency shift keying
Vestigial sideband
Amplitude compressed AM
Direct sequence spread spectrum
G8A09 (A) Page 6-9
36

## Slide 37: Which of the following narrow-band digital modes can receive signals with very low signal-to-noise ratios?
MSK144
FT8
AMTOR
MFSK32
G8A12 (B) Page 6-9
37

## Slide 38: Which digital mode is used as a low-power beacon for assessing HF propagation?
WSPR
Olivia
PSK31
SSB-SC
G8C02 (A) Page 6-9
38

## Slide 39: What part of a packet radio frame contains the routing and handling information?
Directory
Preamble
Header
Footer
G8C03 (C) Page 6-7
39

## Slide 40: In the PACTOR protocol, what is meant by a NAK response to a transmitted packet?
The receiver is requesting the packet be retransmitted
The receiver is reporting the packet was received without error
The receiver is busy decoding the packet
The entire file has been received correctly
G8C05 (A) Page 6-7
40

## Slide 41: How does the receiving station respond to an ARQ data mode packet containing errors?
It terminates the contact
It requests the packet be retransmitted
It sends the packet back to the transmitting station
It requests a change in transmitting protocol
G8C07 (B) Page 6-7
41

## Slide 42: How does forward error correction (FEC) allow the receiver to correct errors in received data packets?
By controlling transmitter output power for optimum signal strength
By using the Varicode character set
By transmitting redundant information with the data
By using a parity bit with each character
G8C10 (C) Page 6-7
42

## Slide 43: Receiving & Transmitting Digital Modes
Most digital modes on HF are transmitted as USB signals
  Exception … RTTY uses LSB
Your modem or software must be configured to correct baud rate and receiving tone frequency to receive data, even if the signal is strong and seems to be tuned correctly
Since PSK31 uses a single tone, either USB or LSB will work!

## Slide 44: Bandwidth of Digital Modes
Like other amateur signals, digital mode bandwidth is defined by the FCC … §97.3(a)(8)
  Bandwidth of signal changes with the symbol rate
  As symbol rate increases, so does the bandwidth needed for the signal needed to transmit them … see Table 6.2 for details
Most common method of generating / transmitting these modes is to connect to audio output from computer sound card to microphone of an SSB transceiver

## Slide 45: Table 6.2
MODE | BANDWIDTH (Hz)
PSK31 | 50
FT8 | 50
RTTY | 200
MFSK16 | 300
JT65 | 350
DominoEX | 524
Olivia | 1000
WINMOR | 1600
MT63 | 2000
PACTOR-III | 2300
PACTOR-4 | 2300
Bandwidth Comparison of Digital Modes
Bandwidths are approximate for the highest commonly used symbol rate and are not specifications
Be careful when operating near the edge of a data signal band. Using LSB for an FSK mode, the sidebands will be below the displayed carrier frequency of you radio.

## Slide 46: Transmitter Duty Cycle
Most amateur transmitters are not designed to operate at full power for an extended period of time
  CW only operates at full power 40-50% of the time
  SSB only operates at full power 20-25% of the time
  FM modes operate at full power the entire transmission time!
Extended transmissions may be enough to exceed a transmitter’s average power rating
  Reduce transmit power to prevent overheating

## Slide 47: Digital Mode Signal Quality
Digital modes are just as capable of generating interference as phone and CW
For digital modes that use an SSB transmitter to transmit audio frequency shift keying (AFSK), the most common problem is supplying too much or too little audio from the computer to the radio’s microphone input
On waterfall displays, the vertical lines represent spurious emissions … cause by overmodulation of the transmitter

## Slide 48: ALC and Digital Modes (automatic level control)
Used for preventing excessive drive to amplifier inputs
ALC circuits reduce gain when power levels get too high
  However, it comes at a price. The signal compression can result in distortion.
For digital signals, distortion caused by ALC makes the signal harder to decode and creates spurious emissions, similar to overmodulation
So, when in digital mode, disable your ALC!

## Slide 49: PRACTICE QUESTIONS

## Slide 50: Which mode is normally used when sending RTTY signals via AFSK with an SSB transmitter?
USB
DSB
CW
LSB
G2E01 (D) Page 6-9
50

## Slide 51: What is the standard sideband used to generate a JT65, JT9, or FT8 digital signal when using AFSK in any amateur band?
LSB
USB
DSB
SSB
G2E05 (B) Page 6-9
51

## Slide 52: What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
The mark and space frequencies may be reversed
You may have selected the wrong baud rate
You may be listening on the wrong sideband
All these choices are correct
G2E14 (D) Page 6-9
52

## Slide 53: What is likely to happen if a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode?
ALC will invert the modulation of the AFSK mode
Improper action of ALC distorts the signal and can cause spurious emissions
When using digital modes, too much ALC activity can cause the transmitter to overheat
All these choices are correct
G4A14 (B) Page 6-11
53

## Slide 54: What is the approximate bandwidth of a PACTOR-III signal at maximum data rate?
31.5 Hz
500 Hz
1800 Hz
2300 Hz
G8B05 (D) Page 6-10
54

## Slide 55: Why is it important to know the duty cycle of the mode you are using when transmitting?
To aid in tuning your transmitter
Some modes have high duty cycles that could exceed the transmitter’s average power rating
To allow time for the other station to break in during a transmission
The attenuator will have to be adjusted accordingly
G8B08 (B) Page 6-10
55

## Slide 56: What is the relationship between transmitted symbol rate and bandwidth?
Symbol rate and bandwidth are not related
Higher symbol rates require wider bandwidth
Lower symbol rates require wider bandwidth
Bandwidth is always half the symbol rate
G8B10 (B) Page 6-10
56

## Slide 57: What is indicated on a waterfall display by one or more vertical lines on either side of a digital signal?
Long path propagation
Backscatter propagation
Insufficient modulation
Overmodulation
G8C13 (D) Page 6-11
57

## Slide 58: Digital Operating Procedures Initiating & Terminating Digital Contacts
Sample CQ from a digital mode (RTTY, PSK31, etc.) …
  CQ CQ CQ DE KØILP KØILP KØILP K
Sample/typical response …
  KØILP KØILP KØILP DE KX4IU KX4IU KX4IU K
Modes such as PACTOR and WINMOR … the software or modem will have a specific disconnect message … BYE or D

## Slide 59: Connecting to Gateway and Mailbox Stations
The exact connection method depends upon equipment and mode, but begin by sending a CONNECT message
If signal is received without errors, a training sequence of packets may be exchanged to determine protocol to use
Because these stations respond without a human control operator present, FCC classifies them as automatically-controlled digital stations … restricted to certain band segments (Table 6.3)
Stations under FCC rules must operate under local or remote control (with control operator in charge of all transmissions)

## Slide 60: Table 6.3
BAND (Meters) | FREQUENCY RANGE (MHz)
160 | Not permitted
80 | 3.585 – 3.600
60 | Not permitted
40 | 7.100 – 7.105
30 | 10.140 – 10.150
20 | 14.095 – 14.0995 & 14.1005 – 14.112
17 | 18.105 – 18.110
15 | 21.090 – 21.100
12 | 24.925 – 24.930
10 | 28.120 – 28.189
6 | 50.1 – 54.0
Automatic Control Band Segments for RTTY & Data

## Slide 61: During the Contact (Operating Displays) – See Fig 6.3 in text
A waterfall display displays the presence of signals as a series of lines representing a scan across the frequency range.
Signal strength is represented as brightness, intensity, or color.
As new lines are captured, older lines are moved down or to one side, giving the impression of a waterfall.

## Slide 62: Waterfall Display – tuning aids for RTTY signals
The left side is a spectrum of the filtered received audio. The vertical lines are at the mark and space frequencies, and help tune in the signal so the peaks are on the lines (indicating the right tone frequencies.
The crossed-ellipses on the right are used for fine tuning … ellipses at right angles and the same size indicate correct tuning.

## Slide 63: Third-Party Traffic in Digital Modes
All FCC rules about 3rd party messages apply to digital transmissions
  Includes info in email, digital images, or web pages transmitted via amateur radio
Commercial messages may not be transmitted via amateur radio
  Includes advertisements and info pertaining to your business

## Slide 64: Interfering Signals in Digital Modes
“Hidden transmitter” problems occur in all modes
  If you’re in a skip zone for one of the stations involved in a contact or that is trying to connect to the same digital station, you won’t hear the hidden transmitter, but the receiving station might hear both of you (it’s hidden to YOU)
  The resulting interference is unintentional but prevents both you and the hidden transmitter from completing a contact
Packet modes (PACTOR, WINMOR) don’t recover from reception difficulties as well as keyboard-to-keyboard modes (RTTY, PSK31), resulting in … failure to connect, frequent retries, transmission delays, timeouts, and dropped connections

## Slide 65: PRACTICE QUESTIONS

## Slide 66: Which of the following is a way to establish contact with a digital messaging system gateway station?
Send an email to the system control operator
Send QRL in Morse code
Respond when the station broadcasts its SSID
Transmit a connect message on the station’s published frequency
G2E10 (D) Page 6-12
66

## Slide 67: Under what circumstances are messages that are sent via digital modes exempt from Part 97 third-party rules that apply to other modes of communication?
Under no circumstances
When messages are encrypted
When messages are not encrypted
When under automatic control
G1E09 (A) [97.115] Page 6-14
67

## Slide 68: What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission?
Frequent retries or timeouts
Long pauses in message transmission
Failure to establish a connection between stations
All these choices are correct
G2E03 (D) Page 6-14
68

## Slide 69: Which of the following is a way to establish contact with a digital messaging system gateway station?
Send an email to the system control operator
Send QRL in Morse code
Respond when the station broadcasts its SSID
Transmit a connect message on the station’s published frequency
G2E10 (D) Page 6-12
69

## Slide 70: What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR?
The checksum overflows
The connection is dropped
Packets will be routed incorrectly
Encoding reverts to the default character set
G8C06 (B) Page 6-14
70

## Slide 71: Which of the following describes a waterfall display?
Frequency is horizontal, signal strength is vertical, time is intensity
Frequency is vertical, signal strength is intensity, time is horizontal
Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity
G8C14 (C) Page 6-13
71

## Slide 72: END OF MODULE 6

## Slide 73
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.