## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Module 7 ARRL General Class Chapter 7 – Antennas (7.1, 7.2, 7.3, 7.4, 7.5) Dipoles, Ground-planes, Yagi Antennas, Loop Antennas, Specialized Antennas, Feed Lines

## Slide 4: Dipoles
The most fundamental antenna
Straight conductor that is 1⁄2 wavelength (λ/2) long with feed point in the middle
Radiates strongest broadside to its axis in a plane containing the antenna’s conductor
Weakest radiation is off the ends (see Fig 7.1)
Shape of azimuth pattern for a dipole in free space is a figure 8

## Slide 5: Fig 7.1
Part A shows the radiation pattern in the plane of a dipole located in free space. The dipole element is located on the line from 270 to 90 degrees in this figure. Part B shows the three-dimensional radiation pattern in all directions around the dipole.

## Slide 6: Dipoles (cont.)
Dipole is often used as reference antenna for gain measurements
  Gain measured in dBd
  Isotropic antenna as the reference, gain is given in dBi
    Isotropic antenna: radiates equally in all directions
  Convert dBd to dBi by adding 2.15 dB
  Convert dBi to dBd by subtracting 2.15 dB
Current in half-wave dipole is highest in middle, Ø at ends; voltage along dipole is highest at ends and lowest in middle (Fig 7.2)

## Slide 7: Fig 7.2
The half-wave dipole at A has its maximum current in the middle and maximum voltage at each end. Feed point impedance is lowest in the middle. At odd harmonics of the fundamental frequency, the dipole’s feed point impedance is low at the midpoint once again as shown at B.

## Slide 8: Dipoles (cont.)
Impedance increases as feed point is moved away from the center; several thousand ohms at the ends
Example: End-fed half-wave (EFHW) antenna … popular for portable operating (lightweight and easy to install)
  EFHW is just a half-wave dipole fed at one end
Calculating free-space length …
  In free space, 1⁄2 wavelength in feet equals 492 divided by frequency in MHz

## Slide 9: Example: What is the approximate length in feet of a 1/2-wave dipole resonant at 3.550 MHz?
= = 139 ft

## Slide 10: Example: What is the approximate length in feet of a 1⁄2-wave dipole for 14.250 MHz?
= = 34.5 ft

## Slide 11: Dipoles (cont.)
Center-fed dipoles are easiest to use on the band for which they are resonant
The feed point impedance is a good match for 50 or 75-Ω coax and for coax on odd multiples of the fundamental frequency
A dipole doesn’t need to be straight to be effective
  Dipole can be supported in the center where the feed line can be conveniently attached
  This configuration is called an inverted V

## Slide 12: Ground Plane Verticals
The ground-plane antenna is one-half of a dipole with the missing portion made up by an electrical mirror, called the ground plane
  Made from sheet metal or a screen of radial wires
  Basic ground-plane is 1⁄4-wavelength (λ/4) long with feed point at the junction of antenna and ground plane
For HF ground-plane antennas at ground level, radial wires are laid on surface of ground or buried within a few inches of surface

## Slide 13: Ground Plane Verticals (cont.)
Ground-planes are called verticals because that’s the usual way of constructing and installing them
Ground-plane radiates best broadside to its axis
If installed vertically, the ground-plane antenna’s pattern is omnidirectional, uniform in all azimuth angles or directions
  Useful for VHF and UHF mobile/portable communications where signals may come from any direction

## Slide 14: Fig 7.3
The ground plane, whether made of solid metal or radial wires, creates an electrical mirror image of the 1⁄4-wavelength antenna. This creates the electrical equivalent of a dipole antenna.
The feed point impedance at the base of the ideal ground-plane is 35 Ω, half of a complete dipole’s impedance, because only half of the antenna is physically there and able to radiate energy.

## Slide 15: Fig 7.4
The feed point impedance of a ground-plane antenna with radials perpendicular to the antenna is approximately 35 Ω, resulting in a 1.4:1 SWR with 50-Ω coaxial cable. Drooping or sloping the radials gradually raises the feed point impedance until, with the radials drooped so far as to become the other half of a dipole, feed point impedance becomes 72 Ω. A 50-Ω feed point is reached with radials drooping approximately 45 degrees.

## Slide 16: Ground Planes (cont.)
A droop angle between 30 and 45 degrees as shown in Fig 7.4 results in the feed point impedance increasing to approx. 50 Ω (matches coaxial cable)
As with the dipole, it is not useful to provide a one-size-fits-all formula for length of a ground-plane antenna
Since the ground-plane is one-half the size of a dipole, start with one-half the free-space length (246 / f in MHz) and be prepared to trim the antenna’s length

## Slide 17: Example: What is the approximate length in feet of a 1⁄4-wave ground-plane antenna resonant at 28.5 MHz?

## Slide 18: Mobile HF Antennas
Mobile HF antennas are often some form of ground-plane
  Most popular is the vertically-oriented whip
A full-sized λ/4 mobile whip is not feasible on bands below 28 and 24 MHz (too long)
Loading techniques are used to increase their electrical length
  Loading coils: A coil added at base or somewhere along the length
  Capacitance hats: Spokes or a wheel-shaped structure is added near the top of the antenna
  Linear loading: Part of the antenna is folded back on itself

## Slide 19: Mobile HF Antennas (cont.)
Another common feature on mobile whips is corona ball at the tip
  Does add a small amount of loading capacitance, but primary function is to eliminate high-voltage discharges from the sharp tip of the antenna while transmitting
A loaded antenna is not as efficient as a full-sized straight whip and will have a small operating bandwidth without retuning
The screwdriver antenna design — a whip with an adjustable loading coil at the base — has gained popularity for HF mobile operation as a good compromise between performance and convenience

## Slide 20: Effects of Ground
A dipole’s feed point impedance and radiation pattern are both affected by its physical height above ground
Feed point impedance is affected because the electrical image is electrically reversed from the actual dipole
As the image and antenna get closer together, the actual antenna begins to be “shorted out” by the image
Below 1⁄4 wavelength in height, dipole’s feed point impedance steadily decreases until it is close to Ø at ground level

## Slide 21: Fig 7.5
The feed point impedance of a horizontal
dipole over perfect ground varies dramatically with height. At ground level, the antenna is effectively “shorted out” by its electrical image. As the antenna is raised, the impedance gradually approaches the 72-Ω feed point impedance of a dipole in free space.
Above 1⁄4 λ, the impedance varies as suggested by Figure 7.5, eventually reaching a stable value at a height of several wavelengths.

## Slide 22: Effects of Ground (cont.)
Height above ground also affects radiation patterns because of reflection of the antenna’s radiated energy by the ground
The direct and reflected signals take different amounts of time to travel to the receiving antenna so they can add together, cancel each other, or any combination in between
Fig 7.6 shows what happens when a dipole is raised in steps from a very low height to more than one wavelength above ground

## Slide 23: Fig 7.6
As a low dipole starting at 1⁄8 wavelength above ground is
raised, the effects of its electrical ground image cause the elevation pattern to flatten out. At multiples of 1/2 wavelength in height, the pattern has a null in the vertical direction because the direct and reflected signals cancel.
At heights below 1⁄2 wavelength, the dipole’s pattern is almost omnidirectional and is maximum straight up.

## Slide 24: NVIS Propagation
Near-vertical incidence sky-wave propagation are signals that go straight up
Signals radiated at high vertical angles on low frequencies are usually reflected back to the ground over a wide area, ensuring good communication
Horizontal dipoles from 1⁄10 to 1⁄4 wavelength high produce an omnidirectional, high-angle pattern ideal for NVIS use
Use by many public service teams

## Slide 25: Effects of Ground (cont.)
Polarization also affects the amount of signal that is lost from the resistance of the ground
Radio waves reflecting from the ground have lower losses when the polarization of the wave is parallel to the ground (i.e., horizontally polarized)
Because the radiation pattern is made up of reflected waves combining with direct waves that are not reflected, lower reflection loss results in stronger maximum signal strength

## Slide 26: Antenna Terms
Feed point impedance: Ratio of RF voltage to current at an antenna’s feed point
Resonant: When antenna feed point impedance is completely resistive with no reactance
Radiation pattern: Graph of antenna’s signal strength in every direction or at every vertical angle
Azimuthal pattern: Shows signal strength in horizontal directions
Elevation pattern: Shows signal strength in vertical directions
Lobes: Regions in the radiation pattern where antenna is radiating a signal
Nulls: Points at which radiation is at a minimum between lobes
Isotropic antenna: Radiates equally in every possible direction (theoretical only)
Omnidirectional antenna: Radiates a signal equally in every horizontal direction
Directional antenna: Radiates preferentially in one or more directions
Gain: Concentrating transmitted or received signals in a specific direction
Front-to-back ratio: Ratio of gain in the preferred or forward direction to the opposite direction
Front-to-side ratio: Ratio of gain in the preferred or forward direction to directions at right angles

## Slide 27: PRACTICE QUESTIONS

## Slide 28: What is the purpose of a capacitance hat on a mobile antenna?
To increase the power handling capacity of a whip antenna
To allow automatic band changing
To electrically lengthen a physically short antenna
To allow remote tuning
G4E01 (C) Page 7-6
28

## Slide 29: What is the purpose of a corona ball on an HF mobile antenna?
To narrow the operating bandwidth of the antenna
To increase the “Q” of the antenna
To reduce the chance of damage if the antenna should strike an object
To reduce RF voltage discharge from the tip of the antenna while transmitting
G4E02 (D) Page 7-6
29

## Slide 30: What is one disadvantage of using a shortened mobile antenna as opposed to a full-size antenna?
Short antennas are more likely to cause distortion of transmitted signals
Short antennas can only receive circularly polarized signals
Operating bandwidth may be very limited
Harmonic radiation may increase
G4E06 (C) Page 7-6
30

## Slide 31: Which of the following is a common way to adjust the feed-point impedance of a quarter wave ground-plane vertical antenna to be approximately 50 ohms?
Slope the radials upward
Slope the radials downward
Lengthen the radials
Shorten the radials
G9B02 (B) Page 7-5
31

## Slide 32: Which of the following best describes the radiation pattern of a quarter-wave, ground-plane vertical antenna?
Bi-directional in azimuth
Isotropic
Hemispherical
Omnidirectional in azimuth
G9B03 (D) Page 7-4
32

## Slide 33: What is the radiation pattern of a dipole antenna in free space in a plane containing the conductor?
It is a figure-eight at right angles to the antenna
It is a figure-eight off both ends of the antenna
It is a circle (equal radiation in all directions)
It has a pair of lobes on one side of the antenna and a single lobe on the other side
G9B04 (A) Page 7-2
33

## Slide 34: How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna?
If the antenna is too high, the pattern becomes unpredictable
Antenna height has no effect on the pattern
If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional
If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated
G9B05 (C) Page 7-6
34

## Slide 35: Where should the radial wires of a ground-mounted vertical antenna system be placed?
As high as possible above the ground
Parallel to the antenna element
On the surface of the Earth or buried a few inches below the ground
At the center of the antenna
G9B06 (C) Page 7-4
35

## Slide 36: How does the feed-point impedance of a 1/2 wave dipole antenna change as the antenna is lowered below 1/4 wave above ground?
It steadily increases
It steadily decreases
It peaks at about 1/8 wavelength above ground
It is unaffected by the height above ground
G9B07 (B) Page 7-6
36

## Slide 37: How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends?
It steadily increases
It steadily decreases
It peaks at about 1/8 wavelength from the end
It is unaffected by the location of the feed point
G9B08 (A) Page 7-3
37

## Slide 38: Which of the following is an advantage of a horizontally polarized as compared to a vertically polarized HF antenna?
Lower ground reflection losses
Lower feed-point impedance
Shorter radials
Lower radiation resistance
G9B09 (A) Page 7-7
38

## Slide 39: What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz?
8 feet
16 feet
24 feet
33 feet
G9B10 (D) Page 7-4
39

## Slide 40: What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz?
42 feet
84 feet
132 feet
263 feet
G9B11 (C) Page 7-3
40

## Slide 41: What is the approximate length for a 1/4 wave vertical antenna cut for 28.5 MHz?
8 feet
11 feet
16 feet
21 feet
G9B12 (A) Page 7-5
41

## Slide 42: How does antenna gain stated in dBi compare to gain stated in dBd for the same antenna?
dBi gain figures are 2.15 dB lower than dBd gain figures
dBi gain figures are 2.15 dB higher than dBd gain figures
dBi gain figures are the same as the square root of dBd gain figures multiplied by 2.15
dBi gain figures are the reciprocal of dBd gain figures + 2.15 dB
G9C04 (B) Page 7-3
42

## Slide 43: What is meant by the terms dBi and dBd when referring to antenna gain?
dBi refers to an isotropic antenna, dBd refers to a dipole antenna
dBi refers to an ionospheric reflecting antenna, dBd refers to a dissipative antenna
dBi refers to an inverted-vee antenna, dBd refers to a downward reflecting antenna
dBi refers to an isometric antenna, dBd refers to a discone antenna
G9C15 (A) Page 7-3
43

## Slide 44: Which of the following antenna types will be most effective as a Near Vertical Incidence Skywave (NVIS) antenna for short-skip communications on 40 meters during the day?
A horizontal dipole placed between 1/10 and 1/4 wavelength above the ground
A vertical antenna placed between 1/4 and 1/2 wavelength above the ground
A left-hand circularly polarized antenna
A right-hand circularly polarized antenna
G9D01 (A) Page 7-7
44

## Slide 45: What is the feed-point impedance of an end-fed half-wave antenna?
Very low
Approximately 50 ohms
Approximately 300 ohms
Very high
G9D02 (D) Page 7-3
45

## Slide 46: How does a “screwdriver” mobile antenna adjust its feed-point impedance?
By varying its body capacitance
By varying the base loading inductance
By extending and retracting the whip
By deploying a capacitance hat
G9D08 (B) Page 7-6
46

## Slide 47: What is the common name of a dipole with a single central support?
Inverted V
Inverted L
Sloper
Lazy H
G9D12 (A) Page 7-4
47

## Slide 48: Yagi/Directional Antenna Basics
Directional antennas create gain as well as reject interference and noise from other than the desired direction
By aiming your antenna in the direction shown on the azimuthal projection map, you will be beaming your signal directly at the other station
Dipole, ground-plane, and random wire antennas use a single radiating element
An array antenna uses two or more elements to create maximum field strength in a specific direction, called the main lobe or major lobe of the radiation pattern

## Slide 49: Directional Antennas (cont.)
Two types of arrays: driven and parasitic
  Driven array: all of the antenna elements are connected to the transmitter and are called driven elements
  Parasitic array: one or more of the elements are not connected to the feed line but influence the antenna’s pattern by interacting with the radiated energy from the driven element(s)
Whether an array is driven or parasitic, its radiation pattern is determined by constructive and destructive interference

## Slide 50: Yagi Structure
Most popular of all directional antennas because of its simple construction and good performance
Yagi is a parasitic array with a single driven element and at least one parasitic element
The driven element (DE) is a resonant dipole, approximately 1⁄2 wavelength long
Parasitic elements placed in the direction of maximum gain are called directors and are slightly shorter than the driven element
Parasitic elements in the direction of minimum gain are called reflectors and are slightly longer than the driven element
The front-to-back ratio is the ratio of signal strength at the peak of the radiation pattern’s major lobe to that in exactly the opposite direction

## Slide 51: Yagi Design Tradeoffs
Primary variables for Yagi antennas are the length and diameter of each element and their placement along the boom of the antenna
These affect gain, SWR, and front-to-back ratio in different ways:
  More directors increase gain
  A longer boom with a fixed number of directors increases gain up to a maximum length beyond which gain is reduced
  Larger diameter elements reduce SWR variation with frequency (increases SWR bandwidth
  Placement and tuning of elements affects gain and feed point impedance (and SWR)
There are other general rules of cause-and-effect, but these are typical of the decisions that antenna designers (and purchasers) should consider

## Slide 52: Yagi Impedance Matching
Most Yagi designs that have desirable radiation patterns also have a feed point impedance somewhat below 50 Ω (regular coax) … results in an undesirable SWR > 2:1
Most common technique for matching impedance is gamma match (see Fig 7.9A in text)
A mechanical advantage of the gamma match over other techniques is that the driven element need not be insulated from the boom, simplifying construction

## Slide 53: Yagi Impedance Matching (cont.)
Beta match (or “hairpin”) … see Fig 7.9C: a short length or “stub” of parallel conductor transmission line connected directly across the driven element feed point
  The stub acts as an inductive reactance that can compensate for any capacitive reactance at the feed point
  The balun is used to maintain electrical balance between both halves of the driven element
Other techniques, such as the omega match, impedance transformers, and transmission line stubs are described in references such as The ARRL Antenna Book

## Slide 54: PRACTICE QUESTIONS

## Slide 55: Which of the following describes an azimuthal projection map?
A map that shows accurate land masses
A map that shows true bearings and distances from a particular location
A map that shows the angle at which an amateur satellite crosses the equator
A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit
G2D04 (B) Page 7-9
55

## Slide 56: Which of the following would increase the bandwidth of a Yagi antenna?
Larger-diameter elements
Closer element spacing
Loading coils in series with the element
Tapered-diameter elements
G9C01 (A) Page 7-10
56

## Slide 57: What is the approximate length of the driven element of a Yagi antenna?
1/4 wavelength
1/2 wavelength
3/4 wavelength
1 wavelength
G9C02 (B) Page 7-10
57

## Slide 58: How do the lengths of a three-element Yagi reflector and director compare to that of the driven element?
The reflector is longer, and the director is shorter
The reflector is shorter, and the director is longer
They are all the same length
Relative length depends on the frequency of operation
G9C03 (A) Page 7-10
58

## Slide 59: How does increasing boom length and adding directors affect a Yagi antenna?
Gain increases
Beamwidth increases
Front-to-back ratio decreases
Front-to-side ratio decreases
G9C05 (A) Page 7-10
59

## Slide 60: What does “front-to-back ratio” mean in reference to a Yagi antenna?
The number of directors versus the number of reflectors
The relative position of the driven element with respect to the reflectors and directors
The power radiated in the major radiation lobe compared to that in the opposite direction
The ratio of forward gain to dipole gain
G9C07 (C) Page 7-10
60

## Slide 61: What is meant by the “main lobe” of a directive antenna?
The magnitude of the maximum vertical angle of radiation
The point of maximum current in a radiating antenna element
The maximum voltage standing wave point on a radiating element
The direction of maximum radiated field strength from the antenna
G9C08 (D) Page 7-9
61

## Slide 62: Which of the following can be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth of a Yagi antenna?
The physical length of the boom
The number of elements on the boom
The spacing of each element along the boom
All these choices are correct
G9C10 (D) Page 7-11
62

## Slide 63: Which HF antenna would be the best to use for minimizing interference?
A quarter-wave vertical antenna
An isotropic antenna
A directional antenna
An omnidirectional antenna
G9C11 (C) Page 7-8
63

## Slide 64: Which of the following is an advantage of using a gamma match with a Yagi antenna?
It does not require that the driven element be insulated from the boom
It does not require any inductors or capacitors
It is useful for matching multiband antennas
All these choices are correct
G9C12 (A) Page 7-12
64

## Slide 65: What is a beta or hairpin match?
It is a shorted transmission line stub placed at the feed point of a Yagi antenna to provide impedance matching
It is a ¼ wavelength section of 75 ohm coax in series with the feed point of a Yagi to provide impedance matching
It is a series capacitor selected to cancel the inductive reactance of a folded dipole antenna
It is a section of 300 ohm twinlead used to match a folded dipole antenna
G9C16 (A) Page 7-12
65

## Slide 66: Loop Antennas
Can be circular, square, triangular or any simple open shape that is not too narrow
Feed line can be attached at a break in the loop or a smaller loop can be used to couple RF energy to the main loop
A square loop with each leg 1⁄4 wavelength long is a quad loop
Triangular or delta loops are usually symmetrical, each leg 1⁄3 wavelength long
A one-wavelength loop acts electrically like two dipoles connected end-to-end with the open ends brought together
  Circumference much larger than 1 λ, current patterns around loop have more than 2 peaks and nulls … result is an essentially omnidirectional pattern with the peak angle of radiation somewhat lower than a dipole at the same height

## Slide 67: Quad and Delta Loop Beams
Popular variation of the Yagi beam uses quad loops for elements (quad)
  Has two or more full-sized loops mounted on a boom
Quad or delta loop beam driven elements are approximately 1 λ in circumference and operate on the same principles of re-radiation and phase shift as does the Yagi
The driven element of a quad is about 1⁄4 λ per side and of a symmetrical delta loop about 1⁄3 λ per side
Quad and delta loop reflectors are about 5% longer in circumference than the driven element, and the directors about 5% shorter
Front-to-back ratio is generally better for the Yagi

## Slide 68: Small Loops
When the circumference of the loop becomes less than 1⁄3 λ, the current in the loop becomes relatively uniform all the way around the loop
This causes the radiation pattern to develop sharp nulls broadside to the plane of the loop
In wide use as receiving antennas and portable or low-profile transmitting antennas
The sharp null broadside to the loop makes them effective for direction-finding

## Slide 69: Halo Antennas
Dipole bent into a circle or square (the “squalo”) with the ends separated by a small gap
Not a continuous loop, but often viewed as a 1⁄2 λ loop
Usually mounted horizontally so they produce an omnidirectional pattern with the horizontal polarization preferred for VHF weak-signal operation
Halos for 6 and 2 meters can be mounted on a vehicle for mobile operation

## Slide 70: PRACTICE QUESTIONS

## Slide 71: What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector?
The driven element must be fed with a balun transformer
There must be an open circuit in the driven element at the point opposite the feed point
The reflector element must be approximately 5 percent shorter than the driven element
The reflector element must be approximately 5 percent longer than the driven element
G9C06 (D) Page 7-13
71

## Slide 72: Approximately how long is each side of the driven element of a quad antenna?
1/4 wavelength
1/2 wavelength
3/4 wavelength
1 wavelength
G9C13 (A) Page 7-13
72

## Slide 73: How does the forward gain of a two-element quad antenna compare to the forward gain of a three element Yagi antenna?
About the same
About 2/3 as much
About 1.5 times as much
About twice as much
G9C14 (A) Page 7-15
73

## Slide 74: In which direction is the maximum radiation from a portable VHF/UHF “halo” antenna?
Broadside to the plane of the halo
Opposite the feed point
Omnidirectional in the plane of the halo
Toward the halo’s supporting mast
G9D03 (C) Page 7-15
74

## Slide 75: In which direction or directions does an electrically small loop (less than 1/3 wavelength in circumference) have nulls in its radiation pattern?
In the plane of the loop
Broadside to the loop
Broadside and in the plane of the loop
Electrically small loops are omnidirectional
G9D10 (B) Page 7-15
75

## Slide 76: What is the combined vertical and horizontal polarization pattern of a multi-wavelength, horizontal loop antenna?
A figure-eight, similar to a dipole
Four major loops with deep nulls
Virtually omnidirectional with a lower peak vertical radiation angle than a dipole
Radiation maximum is straight up
G9D13 (C) Page 7-13
76

## Slide 77: Random Wire Antennas
Not always practical to have a 1⁄2 or 1⁄4 λ long resonant antenna
  A random wire antenna can be used
Connected directly to the output of the transmitter (or tuner) without a feed line
May result in significant RF currents and voltages on the station equipment that could cause RF burns
Can give excellent results on any band for which the transmitter or tuner can accept the feed point impedance

## Slide 78: Stacked Antennas
Stacking antennas (vertically or horizontally) results in more gain (see Fig 7.14 in text)
As more and more directors are added, the beamwidth of the main lobe (angle between points on the main lobe at which gain is 3 dB less than maximum) narrows
Vertically stacking antennas increases gain and narrows the elevation beamwidth
Most vertical stacks, with the antennas directly above each other, space the antennas about λ/2 apart. Spaced λ/2 apart, the additional gain for a vertical stack of two horizontally-polarized beams is about 3 dB.

## Slide 79: Log Periodics (or Logs)
TV antennas are often log periodics
“Log” refers to as logarithmic … periodic means the spacing of the elements along the boom
The length and the spacing of the elements increases logarithmically from one end to the other
Designed to have a consistent radiation pattern and low SWR over a wide frequency bandwidth (as much as 10:1)
  Meaning the log periodic can be used over several bands
Not as much gain or front-to-back ratio as a Yagi antenna

## Slide 80: Beverage Antennas
Invented by Harold Beverage (see Fig 7.16 in text)
Designed not to have high gain, but to reject noise and interfering signals that are not from the desired direction
  Result is lower signal strength but a better signal-to-noise ratio
Referred to as a traveling wave antenna
Consists of a long, low wire (usually less than 20 feet high) aligned with the preferred signal direction
Used exclusively for directional receiving on the lower HF bands (40 meters and longer wavelengths)
Has high ground losses and is too inefficient for use as a transmitting antenna

## Slide 81: Multiband Antennas
What hams generally mean by multiband antenna is a design that reconfigures itself electrically for each band of operation
Most basic multiband antenna … trap dipole (See Fig 7.17 … next slide)
  Each trap is a parallel LC circuit
  At resonance acts like an open circuit, below resonance like an inductor, and above resonance like a capacitor
  At lower frequencies, the traps add inductance to the antenna, making the antenna look electrically longer
  At higher frequencies, the capacitance electrically shortens the antenna

## Slide 82: Fig 7.17
Traps are parallel LC circuits. They may be made from discrete inductors and capacitors or may use coaxial cable or metal sleeves.
The traps act like open circuits at their resonant frequency, causing different sections of the antenna to be active on different bands. This drawing shows a trap antenna that works on 10, 15, and 20 meters.

## Slide 83: Trap Dipoles (cont.)
The lowest frequency of operation the antenna acts like a regular dipole, shortened by the inductance of the trap
Yagis can also use traps to work on several bands
  3-element tribander Yagi with traps in the elements works well on 20, 15 & 10 meters
Trap drawbacks
  Because it works on multiple bands, radiates harmonics and spurious signals (up to transmitter operator to be sure those signals are not generated)
  Trap losses and reduce the efficiency of the antenna
  Will not radiate quite as well as a full-sized antenna

## Slide 84: PRACTICE QUESTIONS

## Slide 85: What is one disadvantage of a directly fed random-wire HF antenna?
It must be longer than 1 wavelength
You may experience RF burns when touching metal objects in your station
It produces only vertically polarized radiation
It is more effective on the lower HF bands than on the higher bands
G9B01 (B) Page 7-16
85

## Slide 86: How does the gain of two three-element, horizontally polarized Yagi antennas spaced vertically ½ wavelength apart typically compare to the gain of a single three-element Yagi?
Approximately 1.5 dB higher
Approximately 3 dB higher
Approximately 6 dB higher
Approximately 9 dB higher
G9C09 (B) Page 7-17
86

## Slide 87: What is the primary purpose of antenna traps?
To permit multiband operation
To notch spurious frequencies
To provide balanced feed-point impedance
To prevent out-of-band operation
G9D04 (A) Page 7-19
87

## Slide 88: What is an advantage of vertical stacking of horizontally polarized Yagi antennas?
It allows quick selection of vertical or horizontal polarization
It allows simultaneous vertical and horizontal polarization
It narrows the main lobe in azimuth
It narrows the main lobe in elevation
G9D05 (D) Page 7-17
88

## Slide 89: Which of the following is an advantage of a log periodic antenna?
Wide bandwidth
Higher gain per element than a Yagi antenna
Harmonic suppression
Polarization diversity
G9D06 (A) Page 7-17
89

## Slide 90: Which of the following describes a log periodic antenna?
Element length and spacing vary logarithmically along the boom
Impedance varies periodically as a function of frequency
Gain varies logarithmically as a function of frequency
SWR varies periodically as a function of boom length
G9D07 (A) Page 7-17
90

## Slide 91: What is the primary use of a Beverage antenna?
Directional receiving for low HF bands
Directional transmitting for low HF bands
Portable direction finding at higher HF frequencies
Portable direction finding at lower HF frequencies
G9D09 (A) Page 7-17
91

## Slide 92: Which of the following is a disadvantage of multiband antennas?
They present low impedance on all design frequencies
They must be used with an antenna tuner
They must be fed with open wire line
They have poor harmonic rejection
G9D11 (D) Page 7-19
92

## Slide 93: Feed Lines / Characteristic Impedance
Balanced feed lines consist of two parallel conductors separated by insulating material in the form of strips or spacers
Have different characteristic impedances (Z0) that characterize how electromagnetic energy is carried by the feed line (different from resistance)
For parallel-conductor feed lines, the radius of the conductors and the distance between them determine Z0
Most common type is window line
Typical impedance for window line is 450 Ω (some as low as 400 Ω)
Most common characteristic impedances for coaxial feed lines used by amateurs are 50 Ω and 75 Ω

## Slide 94: Fig 7.18
Some common types of parallel conductor and coaxial cables used by amateurs. Parallel conductor line (A, B, C) has two parallel conductors separated by insulation (dielectric). Coaxial cable (D, E, F, G) or “coax” has a center conductor surrounded by insulation. The center conductor may be made from stranded or solid wire. The second conductor, called the shield, covers the insulation and is in turn covered by the plastic outer jacket. The shield may be made from braid, or from solid aluminum or copper.

## Slide 95: Forward & Reflected Power & SWR
A feed line transfers ALL of its power to an antenna when the antenna and feed line impedances are matched
  If impedances don’t match, some of the power is reflected by antenna
    Forward power: power traveling toward the antenna
    Reflected power: power reflected by the antenna
Power in a feed line is reflected at any point at which the impedance of the feed line changes
  Can be at an antenna, connector, or from a different type of feed line

## Slide 96: SWR
Standing waves carry forward power and reflected power from stationary interference patterns inside the feed line
The ratio of the peak voltage in the standing wave to the minimum voltage is called the standing wave ratio (SWR)
  Measures how well antenna and feed line impedances are matched
  1:1 is a perfect match … none of the power is reflected
  SWR = infinity (∞) indicates that all the power was reflected
SWR is always greater than 1:1 (for example, 3:1 and not 1:3)

## Slide 97: Calculating SWR
SWR is equal to the ratio of the higher of antenna feed point impedance or feed line characteristic impedance to the lower.
Example: What is the SWR in a 50-Ω feed line connected to a 200-Ω load?
Example: What is the SWR in a 50-Ω feed line connected to a 10-Ω load?

## Slide 98: SWR (cont.)
Can be measured anywhere along feed line
  Most commonly measured at connection to transmitter
Transmitting equipment is designed to work at full power with an SWR at the input to the feed line of 2:1 or lower
Antennas that are much too short or too long will not work well and will have extreme feed point impedances, causing high SWR

## Slide 99: Impedance Matching
Matching feed line and load (antenna) impedances eliminates standing waves from reflected power and maximizes power delivered to the load (but, not always practical)
Devices used to reduce SWR are called: impedance matcher, transmatch, antenna coupler, and antenna tuner
  Tuners do NOT tune the antenna at all — only changes impedance of the antenna system at end of feed line to match that of transmitter
T network: impedance matching circuit for HF antennas (Fig 7.19)

## Slide 100: Impedance Matching (cont.)
Devices constructed from inductors and capacitors that are adjustable by the operator
T circuit can match a wide range of impedances at the feed line connection to 50 Ω that matches transmitter output impedance
It is important to remember that the SWR in the feed line between the impedance matching device and the antenna does not change … the device just changes the load going to the transmitter … SWR in feed line stays the same

## Slide 101: Feed Line Loss
Feed lines dissipate a little of the energy they carry as heat (called attenuation or loss)
Loss is measured in dB per unit of length, usually dB/100 feet
Loss increases with frequency for all types of feed lines
The smaller the cable diameter, the higher the loss
Increasing SWR in a feed line also increases the total loss
The higher the feed line loss, the lower the measured SWR will be at the input to the line

## Slide 102: PRACTICE QUESTIONS

## Slide 103: What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms?
Balanced modulator
SWR bridge
Antenna coupler or antenna tuner
Q multiplier
G4A06 (C) Page 7-22
103

## Slide 104: Which of the following factors determine the characteristic impedance of a parallel conductor antenna feed line?
The distance between the centers of the conductors and the radius of the conductors
The distance between the centers of the conductors and the length of the line
The radius of the conductors and the frequency of the signal
The frequency of the signal and the length of the line
G9A01 (A) Page 7-21
104

## Slide 105: What are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations?
25 and 30 ohms
50 and 75 ohms
80 and 100 ohms
500 and 750 ohms
G9A02 (B) Page 7-21
105

## Slide 106: What is the typical characteristic impedance of “window line” parallel transmission line?
50 ohms
75 ohms
100 ohms
450 ohms
G9A03 (D) Page 7-21
106

## Slide 107: What might cause reflected power at the point where a feed line connects to an antenna?
Operating an antenna at its resonant frequency
Using more transmitter power than the antenna can handle
A difference between feed-line impedance and antenna feed-point impedance
Feeding the antenna with unbalanced feed line
G9A04 (C) Page 7-21
107

## Slide 108: How does the attenuation of coaxial cable change as the frequency of the signal it is carrying increases?
Attenuation is independent of frequency
Attenuation increases
Attenuation decreases
Attenuation reaches a maximum at approximately 18 MHz
G9A05 (B) Page 7-23
108

## Slide 109: In what units is RF feed line loss usually expressed?
Ohms per 1000 feet
Decibels per 1000 feet
Ohms per 100 feet
Decibels per 100 feet
G9A06 (D) Page 7-23
109

## Slide 110: What must be done to prevent standing waves on an antenna feed line?
The antenna feed point must be at DC ground potential
The feed line must be cut to a length equal to an odd number of electrical quarter wavelengths
The feed line must be cut to a length equal to an even number of physical half wavelengths
The antenna feed point impedance must be matched to the characteristic impedance of the feed line
G9A07 (D) Page 7-22
110

## Slide 111: If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, what is the resulting SWR on the feed line?
1 to 1
5 to 1
Between 1 to 1 and 5 to 1 depending on the characteristic impedance of the line
Between 1 to 1 and 5 to 1 depending on the reflected power at the transmitter
G9A08 (B) Page 7-22
111

## Slide 112: What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance?
4:1
1:4
2:1
1:2
G9A09 (A) Page 7-21
112

## Slide 113: What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 10 ohm impedance?
2:1
50:1
1:5
5:1
G9A10 (D) Page 7-21
113

## Slide 114: What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 50 ohm impedance?
2:1
1:1
50:50
0:0
G9A11 (B) Page 7-21
114

## Slide 115: What is the interaction between high standing wave ratio (SWR) and transmission line loss?
There is no interaction between transmission line loss and SWR
If a transmission line is lossy, high SWR will increase the loss
High SWR makes it difficult to measure transmission line loss
High SWR reduces the relative effect of transmission line loss
G9A12 (B) Page 7-23
115

## Slide 116: What is the effect of transmission line loss on SWR measured at the input to the line?
The higher the transmission line loss, the more the SWR will read artificially low
The higher the transmission line loss, the more the SWR will read artificially high
The higher the transmission line loss, the more accurate the SWR measurement will be
Transmission line loss does not affect the SWR measurement
G9A13 (A) Page 7-23
116

## Slide 117: END OF MODULE 7

## Slide 118
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.