## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Module 8 ARRL General Class Chapter 8 – Propagation (8.1, 8.2, 8.3) The Ionosphere, The Sun, Scatter Modes

## Slide 4: The Ionosphere
Upper reaches of the atmosphere gets thinner with distance
Beginning at about 30 miles, remaining gas is thin enough for ionization to occur
This region of the atmosphere becomes a very weak conductor (ionosphere)

## Slide 5: Ionosphere
D layer (30 to 60 miles in altitude) is only present when illuminated by the sun. Disappears at night because ions and free electrons are close enough together to recombine quickly when no UV is present, returning to a neutral condition.
Figure 8.1 — The ionosphere consists of several regions of ionized particles at different heights above the Earth. At night, the D and E regions disappear and the F1 and F2 regions combine to form a single F region.

## Slide 6: Ionosphere (cont.)
E layer (60 to 70 miles in altitude) acts similarly to D
  Higher and less dense than D region, enables it to last longer after sunset
F layer (100 to 300 miles in altitude), least dense of the three
  Remains partially ionized at night
  During the day, F region splits into F1 and F2
  Height of the F region varies quite with local time, season, latitude, and solar activity
  At any particular location, the stronger the illumination from the sun, the higher the F2 layer will be, so its maximum height is reached at noon when the sun is overhead

## Slide 7: Reflection
Ionosphere refracts radio waves (it’s a weak conductor)
  Refraction amount depends on amount of ionization and wave frequency
    The HIGHER the ionization, the more the refraction
    The LOWER the frequency, the more the refraction
    HF signals … relatively good refraction … REFLECTED back to the Earth’s surface
    VHF & UHF signals … essentially no refraction
Each reflection is a hop; allows signal to be received hundreds or thousands of miles away (called skywave and propagation via the ionosphere is called skip)

## Slide 8: Reflection (cont.)
The higher the region from which the reflection takes place, the longer the hop
Waves reflected from F2 layer travel up to 2,500 miles before returning to ground
Hops from E layer are shorter, up to 1,200 miles, because of lower reflecting height
Some combinations of frequency and ionization level result in weak bending … wave must leave the Earth’s surface at a low enough angle for the bending of the wave to send it back
  Highest takeoff angle at which a wave can be returned to Earth is the critical angle
  Critical angle depends on ionospheric conditions and frequency

## Slide 9: Critical Angle
Critical frequency: Highest frequency on which a wave transmitted straight up will be returned to Earth.

## Slide 10: Absorption
Enemy of propagation is absorption
  In D and E regions, waves passing through the denser gas are partially absorbed (D region is not very good at refraction)
In HF bands below 10 MHz, AM broadcast bands, and at lower frequencies, the D region completely absorbs radio waves during the day, preventing those waves from returning to Earth
Absorption increases in daytime and when solar UV is more intense
  QUESTION: When is the best time to transmit on HF below 10 MHz?

## Slide 11: Noise
Noise is another enemy of propagation (covers up weak signals)
Stronger at frequencies below VHF (due to atmospheric disturbances)
Lower you go in frequency, the stronger the noise or static
Varies seasonally
Most noticeable on lower frequency HF bands in the summer when atmospheric noise is strongest

## Slide 12: Long Path and Short Path
When ionosphere along short path does not support propagation, sometimes long path will
Occasionally, propagation over both long and short paths will be supported (at same time)
Unless the paths are almost equal there will be an echo (delayed signal arrives a fraction of a second later)
Round-the-world propagation: you can hear your own signal coming all the way around to your location about 1/7 of a second later!
  25,000 miles divided by 186,000 miles/sec

## Slide 13: PRACTICE QUESTIONS

## Slide 14: How is a directional antenna pointed when making a “long-path” contact with another station?
Toward the rising sun
Along the grayline
180 degrees from the station’s short-path heading
Toward the north
G2D06 (C) Page 8-5
14

## Slide 15: Which of the following is typical of the lower HF frequencies during the summer?
Poor propagation at any time of day
World-wide propagation during the daylight hours
Heavy distortion on signals due to photon absorption
High levels of atmospheric noise or “static”
G2D11 (D) Page 8-5
15

## Slide 16: What is a characteristic of skywave signals arriving at your location by both short-path and longpath propagation?
Periodic fading approximately every 10 seconds
Signal strength increased by 3 dB
The signal might be cancelled causing severe attenuation
A slightly delayed echo might be heard
G3B01 (D) Page 8-6
16

## Slide 17: What is the approximate maximum distance along the Earth’s surface that is normally covered in one hop using the F2 region?
180 miles
1,200 miles
2,500 miles
12,000 miles
G3B09 (C) Page 8-2
17

## Slide 18: What is the approximate maximum distance along the Earth’s surface that is normally covered in one hop using the E region?
180 miles
1,200 miles
2,500 miles
12,000 miles
G3B10 (B) Page 8-2
18

## Slide 19: Which ionospheric layer is closest to the surface of Earth?
The D layer
The E layer
The F1 layer
The F2 layer
G3C01 (A) Page 8-2
19

## Slide 20: Where on Earth do ionospheric layers reach their maximum height?
Where the sun is overhead
Where the sun is on the opposite side of Earth
Where the sun is rising
Where the sun has just set
G3C02 (A) Page 8-2
20

## Slide 21: Why is the F2 region mainly responsible for the longest distance radio wave propagation?
Because it is the densest ionospheric layer
Because of the Doppler effect
Because it is the highest ionospheric region
Because of meteor trails at that level
G3C03 (C) Page 8-2
21

## Slide 22: What does the term “critical angle” mean, as used in radio wave propagation?
The long path azimuth of a distant station
The short path azimuth of a distant station
The lowest takeoff angle that will return a radio wave to Earth under specific ionospheric conditions
The highest takeoff angle that will return a radio wave to Earth under specific ionospheric conditions
G3C04 (D) Page 8-2
22

## Slide 23: Why is long-distance communication on the 40-meter, 60-meter, 80-meter, and 160-meter bands more difficult during the day?
The F layer absorbs signals at these frequencies during daylight hours
The F layer is unstable during daylight hours
The D layer absorbs signals at these frequencies during daylight hours
The E layer is unstable during daylight hours
G3C05 (C) Page 8-5
23

## Slide 24: Which ionospheric layer is the most absorbent of long skip signals during daylight hours on frequencies below 10 MHz?
The F2 layer
The F1 layer
The E layer
The D layer
G3C11 (D) Page 8-5
24

## Slide 25: Sunspots and Cycles
Ionosphere is dependent on solar UV to separate electrons from atoms
Much of the variation in UV radiation is due to sunspot activity
When more sunspots are observed, more UV is being generated, creating more intense ionization and improving propagation on higher frequency bands above 10 MHz and even into lower VHF range

## Slide 26: Sunspots and Cycles (cont.)
At peak of cycle, there may be sufficient solar UV to cause higher frequency bands (10 meters) to stay open for long-distance contacts at night
High ionization negatively impacts low frequency bands (80 and 160 m) because it increases absorption
When solar activity is low, lower HF bands have good propagation and higher HF bands above 20 MHz (15 m and up) are often closed
One band that seems to do well at all times in sunspot cycle is 20 meters (14 MHz), supporting daytime communications worldwide nearly every day

## Slide 27: Table 8.1: Daytime/Nighttime HF Propagation
Sunspots also seem to move across the sun’s surface because the sun rotates once every 28 days. That is why propagation conditions (good and bad) on the HF bands often repeat themselves in 28-day cycles as sunspots rotate back into view from Earth.

## Slide 28: Measuring Solar Activity
Sunspot Number: See Fig 8.6
Solar-Flux Index (SFI): Describes amount of 2800 MHz (λ = 10.7 cm) radio energy. Higher levels indicate higher solar activity and better HF propagation above 10 MHz (Fig 8.6)
K-index: Values from 0 to 9 represent the short-term stability of the Earth’s magnetic or geomagnetic field. Higher values indicate geomagnetic field is disturbed, which disrupts HF.
A-index: Gives a good picture of long-term geomagnetic field stability. Ranges from 0 (stable) to 400 (greatly disturbed). Calculated from K-index.

## Slide 29: PRACTICE QUESTIONS

## Slide 30: What is the significance of the sunspot number with regard to HF propagation?
Higher sunspot numbers generally indicate a greater probability of good propagation at higher frequencies
Lower sunspot numbers generally indicate greater probability of sporadic E propagation
A zero sunspot number indicates that radio propagation is not possible on any band
A zero sunspot number indicates undisturbed conditions
G3A01 (A) Page 8-7
30

## Slide 31: Which of the following are least reliable for long-distance communications during periods of low solar activity?
80 meters and 160 meters
60 meters and 40 meters
30 meters and 20 meters
15 meters, 12 meters, and 10 meters
G3A04 (D) Page 8-7
31

## Slide 32: What is the solar flux index?
A measure of the highest frequency that is useful for ionospheric propagation between two points on Earth
A count of sunspots that is adjusted for solar emissions
Another name for the American sunspot number
A measure of solar radiation at 10.7 centimeters wavelength
G3A05 (D) Page 8-9
32

## Slide 33: At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours?
At the summer solstice
Only at the maximum point of the solar cycle
Only at the minimum point of the solar cycle
At any point in the solar cycle
G3A07 (D) Page 8-8
33

## Slide 34: What causes HF propagation conditions to vary periodically in a roughly 28-day cycle?
Long term oscillations in the upper atmosphere
Cyclic variation in Earth’s radiation belts
The sun’s rotation on its axis
The position of the moon in its orbit
G3A10 (C) Page 8-8
34

## Slide 35: What does the K-index indicate?
The relative position of sunspots on the surface of the sun
The short-term stability of Earth’s magnetic field
The stability of the sun’s magnetic field
The solar radio flux at Boulder, Colorado
G3A12 (B) Page 8-9
35

## Slide 36: What does the A-index indicate?
The relative position of sunspots on the surface of the sun
The amount of polarization of the sun’s electric field
The long-term stability of Earth’s geomagnetic field
The solar radio flux at Boulder, Colorado
G3A13 (C) Page 8-9
36

## Slide 37: Assessing Propagation
MUF: Maximum usable frequency. Highest frequency at which propagation exists between two points.
LUF: Lowest usable frequency.
Depends on the specific path between two points — their location and distance apart
Varies with time of day, season, amount of solar radiation, and ionospheric stability
Operating near MUF often gives excellent results because absorption is lowest just below the MUF
One way to check actual band conditions between two points is to listen for propagation beacons
  Many stations between 28.190 and 28.225 MHz that are excellent sources of information about 10-meter propagation.

## Slide 38: Solar Disturbances
Solar flare: A large eruption of energy and solar material when magnetic field disruptions occur on the surface of the sun.
Coronal hole: A weak area in the sun’s corona (the outer layer) through which plasma (ionized gas and charged particles) escapes the sun’s magnetic field and streams away into space at high velocities.
Coronal mass ejection (CME): An ejection of large amounts of material from the corona.
All of these disrupt HF propagation

## Slide 39: Sudden Ionospheric Disturbances
UV and X-ray radiation from a solar flare travels at speed of light to impact the ionosphere about 8 minutes later
When radiation hits the ionosphere, the level of ionization increases rapidly, particularly in D region
This increases absorption dramatically, causing a sudden ionospheric disturbance (SID) also known as a radio blackout
Lower bands are more strongly affected so communication may still be possible on a higher band

## Slide 40: Fig 8.7
SIDs affect only the sunlit side of the Earth, so dark-side communications may be relatively unaffected.

## Slide 41: Geomagnetic Disturbances
Interaction between solar wind and geomagnetic field creates a region of space called the magnetosphere
Charged particles from coronal holes and coronal mass ejections travel considerably slower and take longer to reach Earth (20 to 40 hours)
These particles deposit their energy into Earth’s geomagnetic field and increase ionization in E region, causing auroral displays and creating a geomagnetic storm … affects higher HF bands first
Long-distance paths that traverse high latitudes, particularly those that pass near the magnetic poles, may be completely wiped out for hours to days
Can create auroras that reflect radio waves above 20 MHz
Auroral propagation strongest on 6 and 2 m, modulating the signals with a hiss or buzz

## Slide 42: PRACTICE QUESTIONS

## Slide 43: What effect does a Sudden Ionospheric Disturbance have on the daytime ionospheric propagation of HF radio waves?
It enhances propagation on all HF frequencies
It disrupts signals on lower frequencies more than those on higher frequencies
It disrupts communications via satellite more than direct communications
None, because only areas on the night side of the Earth are affected
G3A02 (B) Page 8-11
43

## Slide 44: Approximately how long does it take the increased ultraviolet and X-ray radiation from solar flares to affect radio propagation on Earth?
28 days
1 to 2 hours
8 minutes
20 to 40 hours
G3A03 (C) Page 8-10
44

## Slide 45: What is a geomagnetic storm?
A sudden drop in the solar flux index
A thunderstorm that affects radio propagation
Ripples in the ionosphere
A temporary disturbance in Earth’s magnetosphere
G3A06 (D) Page 8-11
45

## Slide 46: What benefit can high geomagnetic activity have on radio communications?
Auroras that can reflect VHF signals
Higher signal strength for HF signals passing through the polar regions
Improved HF long path propagation
Reduced long delayed echoes
G3A09 (A) Page 8-12
46

## Slide 47: How long does it take charged particles from coronal mass ejections to affect radio propagation on Earth?
28 days
14 days
4 to 8 minutes
20 to 40 hours
G3A11 (D) Page 8-11
47

## Slide 48: How are radio communications usually affected by the charged particles that reach Earth from solar coronal holes?
HF communications are improved
HF communications are disturbed
VHF/UHF ducting is improved
VHF/UHF ducting is disturbed
G3A14 (B) Page 8-12
48

## Slide 49: What factors affect the MUF?
Path distance and location
Time of day and season
Solar radiation and ionospheric disturbances
All these choices are correct
G3B02 (D) Page 8-9
49

## Slide 50: Which of the following applies when selecting a frequency for lowest attenuation when transmitting on HF?
Select a frequency just below the MUF
Select a frequency just above the LUF
Select a frequency just below the critical frequency
Select a frequency just above the critical frequency
G3B03 (A) Page 8-10
50

## Slide 51: What is a reliable way to determine if the MUF is high enough to support skip propagation between your station and a distant location on frequencies between 14 and 30 MHz?
Listen for signals from an international beacon in the frequency range you plan to use
Send a series of dots on the band and listen for echoes from your signal
Check the strength of TV signals from western Europe
Check the strength of signals in the MF AM broadcast band
G3B04 (A) Page 8-10
51

## Slide 52: What usually happens to radio waves with frequencies below the MUF and above the LUF when they are sent into the ionosphere?
They are bent back to Earth
They pass through the ionosphere
They are amplified by interaction with the ionosphere
They are bent and trapped in the ionosphere to circle Earth
G3B05 (A) Page 8-10
52

## Slide 53: What usually happens to radio waves with frequencies below the LUF?
They are bent back to Earth
They pass through the ionosphere
They are completely absorbed by the ionosphere
They are bent and trapped in the ionosphere to circle Earth
G3B06 (C) Page 8-10
53

## Slide 54: What does LUF stand for?
The Lowest Usable Frequency for communications between two points
The Longest Universal Function for communications between two points
The Lowest Usable Frequency during a 24-hour period
The Longest Universal Function during a 24-hour period
G3B07 (A) Page 8-9
54

## Slide 55: What does MUF stand for?
The Minimum Usable Frequency for communications between two points
The Maximum Usable Frequency for communications between two points
The Minimum Usable Frequency during a 24-hour period
The Maximum Usable Frequency during a 24-hour period
G3B08 (B) Page 8-9
55

## Slide 56: What happens to HF propagation when the LUF exceeds the MUF?
No HF radio frequency will support ordinary skywave communications over the path
HF communications over the path are enhanced
Double hop propagation along the path is more common
Propagation over the path on all HF frequencies is enhanced
G3B11 (A) Page 8-10
56

## Slide 57: Scatter Characteristics
Backscatter: Reflections from features on Earth’s surface
Waves can also be scattered from within the ionosphere, allowing signals to be heard from stations too distant to be heard by ground wave and on frequencies too high for short hop sky-wave propagation
Scatter and backscatter help fill in the skip zone where signals would otherwise not be heard

## Slide 58: Fig 8.8
Scatter and Backscatter

## Slide 59: Near Vertical Incidence Sky-wave (NVIS)
For waves below the critical frequency, the ionosphere reflects waves arriving at any angle — even vertical
NVIS Definition: For a signal below the critical frequency, when it is radiated vertically the reflection scatters the signal back to Earth throughout a region of up to 200-300 miles
To make use of NVIS horizontally polarized dipoles are placed low to the ground so that their radiation pattern is almost omnidirectional and concentrated at high elevation angles

## Slide 60: Fig 8.9
NIVS Communications

## Slide 61: PRACTICE QUESTIONS

## Slide 62: What is a characteristic of HF scatter?
Phone signals have high intelligibility
Signals have a fluttering sound
There are very large, sudden swings in signal strength
Scatter propagation occurs only at night
G3C06 (B) Page 8-12
62

## Slide 63: What makes HF scatter signals often sound distorted?
The ionospheric layer involved is unstable
Ground waves are absorbing much of the signal
The E-region is not present
Energy is scattered into the skip zone through several different radio wave paths
G3C07 (D) Page 8-12
63

## Slide 64: Why are HF scatter signals in the skip zone usually weak?
Only a small part of the signal energy is scattered into the skip zone
Signals are scattered from the magnetosphere, which is not a good reflector
Propagation is through ground waves, which absorb most of the signal energy
Propagation is through ducts in the F region, which absorb most of the energy
G3C08 (A) Page 8-12
64

## Slide 65: What type of propagation allows signals to be heard in the transmitting station’s skip zone?
Faraday rotation
Scatter
Chordal hop
Short-path
G3C09 (B) Page 8-12
65

## Slide 66: What is Near Vertical Incidence Skywave (NVIS) propagation?
Propagation near the MUF
Short distance MF or HF propagation using high elevation angles
Long path HF propagation at sunrise and sunset
Double hop propagation near the LUF
G3C10 (B) Page 8-12
66

## Slide 67: END OF MODULE 8

## Slide 68
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.