## Slide 2: General Class License Manual and other resources
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3: Module 9 ARRL General Class Chapter 9 – Electrical and RF Safety (9.1, 9.2, 9.3) Electrical Safety, RF Exposure, Outdoor Safety

## Slide 4: Preventing Electric Shock
Have a master OFF/ON switch for station and workbench
  Clearly labeled and somewhat away from the equipment
Don’t put yourself in a position to be shocked
When working inside equipment, remove, insulate, or secure loose wires and cables
Use grounding stick to remove charge from capacitors

## Slide 5: Table 9.1: Effects of Electric Current Through the Body of an Average Person

## Slide 6: Soldering Safety
Primarily lead-based; tin added to lower melting point
  Lead is a known toxin
  Solder in a well-ventilated area
  When finished, wash hands to remove solder or flux residue
As of 2006, environmental regulations require that solder become lead-free

## Slide 7: Wiring Practices
National Electrical Code Handbook contains details for handling ac wiring in home and station
Use local building codes to ensure home is properly wired to meet special local conditions
Standard wire color conventions
  Hot: Red or Black insulation, connect to brass terminal or screw
  Neutral: White insulation, connect to silver terminal or screw
  Ground: Green insulation or bare wire, connect to green or bare terminal or screw

## Slide 8: Fig 9.3
House ac wiring, most common sizes are #12 AWG for 20 A circuits and #14 AWG for 15 A circuits.
Use fuse or circuit breaker in the hot conductor for 120 V circuits or both hot conductors of a 240 V circuit using three or four wires.

## Slide 9: Ground fault circuit interrupter (GFCI) circuit breakers
Used in ac power circuits to prevent shock hazards
Trips if imbalance is sensed in currents carried by hot and neutral conductors
Sensitive to just a few milliamperes (mA) of imbalance between hot and neutral, well below threshold for electrical injury

## Slide 10: Safety Interlock
Switch that prevents dangerous voltages or intense RF from being present when a cabinet or enclosure is opened
Several types …
  Physically disconnects high voltage (HV) or RF when activated
  Shorts or grounds HV circuit when activated, possibly blowing a circuit breaker or fuse in a power supply

## Slide 11: PRACTICE QUESTIONS

## Slide 12: Which of the following is a danger from lead-tin solder?
Lead can contaminate food if hands are not washed carefully after handling the solder
High voltages can cause lead-tin solder to disintegrate suddenly
Tin in the solder can “cold flow,” causing shorts in the circuit
RF energy can convert the lead into a poisonous gas
G0B10 (A) Page 9-3
12

## Slide 13: Which wire or wires in a four-conductor connection should be attached to fuses or circuit breakers in a device operated from a 240 VAC single phase source?
Only the two wires carrying voltage
Only the neutral wire
Only the ground wire
All wires
G0B01 (A) Page 9-5
13

## Slide 14: According the National Electrical Code, what is the minimum wire size that may be used safely for wiring with a 20 ampere circuit breaker?
AWG number 20
AWG number 16
AWG number 12
AWG number 8
G0B02 (C) Page 9-5
14

## Slide 15: Which of the following conditions will cause a Ground Fault Circuit Interrupter (GFCI) to disconnect the 120 or 240 Volt AC line power to a device?
Current flowing from one or more of the voltage-carrying wires to the neutral wire
Current flowing from one or more of the voltage-carrying wires directly to ground
Overvoltage on the voltage-carrying wires
All these choices are correct
G0B05 (B) Page 9-6
15

## Slide 16: Which of the following is covered by the National Electrical Code?
Acceptable bandwidth limits
Acceptable modulation limits
Electrical safety inside the ham shack
RF exposure limits of the human body
G0B06 (C) Page 9-4
16

## Slide 17: What is the purpose of a power supply interlock?
To prevent unauthorized changes to the circuit that would void the manufacturer’s warranty
To shut down the unit if it becomes too hot
To ensure that dangerous voltages are removed if the cabinet is opened
To shut off the power supply if too much voltage is produced
G0B12 (C) Page 9-6
17

## Slide 18: Generator Safety
Fueling and ventilation problems cause more injuries associated with generators than from any other cause
Install generators outdoors
  Carbon monoxide (CO) in exhaust can quickly build up to toxic levels
When using generators regularly, install CO detector alarms in living and working areas
Generator output connected directly to a home’s wiring system must have the ability to disconnect power service from utility lines

## Slide 19: PRACTICE QUESTIONS

## Slide 20: Which of the following is a primary reason for not placing a gasoline-fueled generator inside an occupied area?
Danger of carbon monoxide poisoning
Danger of engine over torque
Lack of oxygen for adequate combustion
Lack of nitrogen for adequate combustion
G0B04 (A) Page 9-7
20

## Slide 21: Which of the following is true of an emergency generator installation?
The generator should be located in a well-ventilated area
The generator must be insulated from ground
Fuel should be stored near the generator for rapid refueling in case of an emergency
All these choices are correct
G0B09 (A) Page 9-7
21

## Slide 22: What must you do when powering your house from an emergency generator?
Disconnect the incoming utility power feed
Insure that the generator is not grounded
Insure that all lightning grounds are disconnected
All these choices are correct
G0B13 (A) Page 9-7
22

## Slide 23: Lightning
Lightning protection goals: Provide fire prevention and reduce or prevent electrical damage to equipment
A metal entry panel where signal and control cables enter the house is a good place to provide a lightning ground
  Panel should be grounded to a nearby ground rod
Towers should be grounded with separate 8-foot ground rods for each tower leg
Grounding wires and straps should be as short and direct as possible
All towers, masts and antenna mounts should be grounded
Lightning grounds should be bonded to other safety grounds
Do not solder connections since solder joints would likely melt and be destroyed if hit with a lightning-sized current

## Slide 24: PRACTICE QUESTIONS

## Slide 25: Why should soldered joints not be used with the wires that connect the base of a tower to a system of ground rods?
The resistance of solder is too high
Solder flux will prevent a low conductivity connection
Solder has too high a dielectric constant to provide adequate lightning protection
A soldered joint will likely be destroyed by the heat of a lightning strike
G4C07 (D) Page 9-8
25

## Slide 26: Which of the following is good practice for lightning protection grounds?
They must be bonded to all buried water and gas lines
Bends in ground wires must be made as close as possible to a right angle
Lightning grounds must be connected to all ungrounded wiring
They must be bonded together with all other grounds
G0B11 (D) Page 9-8
26

## Slide 27: RF Exposure
At high power levels, for some frequencies, the amount of energy that the body absorbs can be a problem
The maximum permissible exposure (MPE): Maximum intensity of RF radiation to which a human being may be exposed
Factors to consider when estimating MPE: power level or density, frequency, average exposure time, and duty cycle of the transmission (power density & frequency are primary ones)

## Slide 28: Power Density
Heating from exposure to RF signals is caused by the body tissue absorbing RF energy
Measured in mW/cm2 (milliwatts per square centimeter)
RF field strengths can be measured in V/m and A/m, (mW/cm2 is the most useful for amateur requirements)
Power density is highest near antennas and in the directions in which antennas have the most gain
Decreasing transmitter power and increasing distance from an antenna lowers power density (lowers RF energy)

## Slide 29: Absorption and Limits
SAR (specific absorption rate): Rate at which energy is absorbed from the power to which the body is exposed
  Best measure of RF exposure
  Varies with frequency, power density, average amount of exposure, and duty cycle of transmission
  Depends on frequency and size of the body or body part affected; highest where the body and body parts are naturally resonant
Safe levels of SAR based on demonstrated hazards have been established for by the FCC in the form of maximum permissible exposure (MPE) limits

## Slide 30: Fig 9.9
Maximum Permissible Exposure
(MPE) limits vary with frequency because the body responds differently to energy at different frequencies. The controlled and uncontrolled limits refer to the environment in which people are exposed to the RF energy.
These take into account the variations in the body’s sensitivity to RF energy at different frequencies. Also see Table 9.3 (next slide).

## Slide 31: Table 9.3 Maximum Permissible Exposure (MPE) Limits

## Slide 32: Duty Cycle & Controlled/Uncontrolled Environments
Exposure to RF energy is averaged over fixed time intervals
Time-averaging evaluates total RF exposure over a fixed time interval
Two types of averaging periods: Controlled & uncontrolled
Controlled = You’re aware of your exposure and are expected to take reasonable steps to minimize
Controlled Environment Examples: Transmitting facilities, near antennas
Uncontrolled environments: General public has access
  People in uncontrolled environments are not aware of their exposure, but are much less likely to receive continuous exposure

## Slide 33: Duty Cycle
Ratio of the time the transmitter is ON to the total time during the exposure (max = 100%)
A lower transmission duty cycle permits greater short-term exposure levels for a given average exposure (called operating duty cycle)
Along with operational duty cycle, the different modes themselves have different emission duty cycles (see Table 9.4)

## Slide 34: Table 9.4
Operating Duty Factor of Modes Commonly Used by Amateurs
For most amateurs operating, listening and transmitting time are about the same, so operating duty cycle is rarely higher than 50%.

## Slide 35: Estimating Exposure & Station Evaluation
All fixed amateur stations must evaluate their capability to cause RF exposure, no matter whether they use high or low power
  Mobile and handheld transceivers are exempt
Limits vary with frequency and PEP
You are required to perform the evaluation only if your output power exceeds the levels shown for any band (Table 9.5)
Evaluation is performed by measuring the RF field strength with calibrated field strength meters and calibrated antennas

## Slide 36: Table 9.5
Power Thresholds for RF Exposure Evaluation
What you need to calculate RF exposure …
Power at the antenna, including adjustments for duty cycle and feed line loss
Antenna type (or gain)
Antenna height above ground
Operating frequency

## Slide 37: Exposure Safety Measures
Locate or move antennas away from where people can be exposed to excessive RF fields … locate antenna away from property lines and place fence around base of ground-mounted antennas
Don’t point gain antennas where people are likely to be
Use beam antennas to direct RF energy away from people
When using stealth, attic, or other indoor antennas, make sure MPE limits are not exceeded in living quarters
On VHF and UHF, place mobile antennas on roof or trunk of car to maximize shielding of passengers
Use dummy load or dummy antenna when testing a transmitter
Reduce the power and duty cycle of your transmissions

## Slide 38: PRACTICE QUESTIONS

## Slide 39: What is one way that RF energy can affect human body tissue?
It heats body tissue
It causes radiation poisoning
It causes the blood count to reach a dangerously low level
It cools body tissue
G0A01 (A) Page 9-9
39

## Slide 40: Which of the following properties is important in estimating whether an RF signal exceeds the maximum permissible exposure (MPE)?
Its duty cycle
Its frequency
Its power density
All these choices are correct
G0A02 (D) Page 9-9
40

## Slide 41: How can you determine that your station complies with FCC RF exposure regulations?
By calculation based on FCC OET Bulletin 65
By calculation based on computer modeling
By measurement of field strength using calibrated equipment
All these choices are correct
G0A03 (D) [97.13(c)(1)] Page 9-12
41

## Slide 42: What does “time averaging” mean in reference to RF radiation exposure?
The average amount of power developed by the transmitter over a specific 24-hour period
The average time it takes RF radiation to have any long-term effect on the body
The total time of the exposure
The total RF exposure averaged over a certain time
G0A04 (D) Page 9-10
42

## Slide 43: What must you do if an evaluation of your station shows RF energy radiated from your station exceeds permissible limits?
Take action to prevent human exposure to the excessive RF fields
File an Environmental Impact Statement (EIS-97) with the FCC
Secure written permission from your neighbors to operate above the controlled MPE limits
All these choices are correct
G0A05 (A) Page 9-13
43

## Slide 44: What precaution should be taken when installing a ground-mounted antenna?
It should not be installed higher than you can reach
It should not be installed in a wet area
It should be limited to 10 feet in height
It should be installed such that it is protected against unauthorized access
G0A06 (D) Page 9-13
44

## Slide 45: What effect does transmitter duty cycle have when evaluating RF exposure?
A lower transmitter duty cycle permits greater short-term exposure levels
A higher transmitter duty cycle permits greater short-term exposure levels
Low duty cycle transmitters are exempt from RF exposure evaluation requirements
High duty cycle transmitters are exempt from RF exposure requirements
G0A07 (A) Page 9-11
45

## Slide 46: Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations when transmitter power exceeds levels specified in FCC Part 97.13?
Post a copy of FCC Part 97.13 in the station
Post a copy of OET Bulletin 65 in the station
Perform a routine RF exposure evaluation
Contact the FCC for a visit to conduct a station evaluation
G0A08 (C) Page 9-12
46

## Slide 47: What type of instrument can be used to accurately measure an RF field?
A receiver with an S meter
A calibrated field strength meter with a calibrated antenna
An SWR meter with a peak-reading function
An oscilloscope with a high-stability crystal marker generator
G0A09 (B) Page 9-12
47

## Slide 48: What is one thing that can be done if evaluation shows that a neighbor might receive more than the allowable limit of RF exposure from the main lobe of a directional antenna?
Change to a non-polarized antenna with higher gain
Post a warning sign that is clearly visible to the neighbor
Use an antenna with a higher front-to-back ratio
Take precautions to ensure that the antenna cannot be pointed in their direction
G0A10 (D) Page 9-13
48

## Slide 49: What precaution should you take if you install an indoor transmitting antenna?
Locate the antenna close to your operating position to minimize feed-line radiation
Position the antenna along the edge of a wall to reduce parasitic radiation
Make sure that MPE limits are not exceeded in occupied areas
Make sure the antenna is properly shielded
G0A11 (C) Page 9-14
49

## Slide 50: Outdoor Safety … Installing Antennas
Place all antennas and feed lines well clear of power lines!
No part of antenna system should be closer than 10 feet from power lines
When working on roofs, trees, or towers, climbers and helpers should wear appropriate protective gear at all times … run through a safety checklist every time
Turn off and unplug all ac equipment, locking circuits out and tagging them if possible
Transmitters should be off and disconnected from feed line to avoid shock or excessive RF exposure
Transmitters should be off and disconnected from feed line to avoid shock or excessive RF exposure
Belts and harnesses must be within their service life and adequately rated for weight

## Slide 51: PRACTICE QUESTIONS

## Slide 52: Which of these choices should be observed when climbing a tower using a safety belt or harness?
Never lean back and rely on the belt alone to support your weight
Confirm that the belt is rated for the weight of the climber and that it is within its allowable service life
Ensure that all heavy tools are securely fastened to the belt D-ring
All these choices are correct
G0B07 (B) Page 9-15
52

## Slide 53: What should be done by any person preparing to climb a tower that supports electrically powered devices?
Notify the electric company that a person will be working on the tower
Make sure all circuits that supply power to the tower are locked out and tagged
Unground the base of the tower
All these choices are correct
G0B08 (B) Page 9-15
53

## Slide 54: What precaution should you take whenever you adjust or repair an antenna?
Ensure that you and the antenna structure are grounded
Turn off the transmitter and disconnect the feed line
Wear a radiation badge
All these choices are correct
G0B14 (B) Page 9-15
54

## Slide 55: END OF MODULE 9

## Slide 56
Slides created by …
Jerry D. Kilpatrick
KØILP (Amateur Radio)
PGØØØ72373 (Commercial Operator)
K0ILP.NC@gmail.com
Feel free to contact me if you find errors or have suggestions for improvement.