## Slide 1
Level2

## Slide 2
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General - G0A
RF safety principles, rules, and guidelines; routine station evaluation
For use with The ARRL General Class License Manual, Tenth Edition

## Slide 3
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 4
G0A01- RF safety principles, rules, and guidelines; routine station evaluation
What is one way that RF energy can affect human body tissue?
A. It heats body tissue
B. It causes radiation poisoning
C. It causes the blood count to reach a dangerously low level
D. It cools body tissue

## Slide 5
G0A01- RF safety principles, rules, and guidelines; routine station evaluation
What is one way that RF energy can affect human body tissue?
A. It heats body tissue
B. It causes radiation poisoning
C. It causes the blood count to reach a dangerously low level
D. It cools body tissue

## Slide 6
G0A02
Which of the following is used to determine RF exposure from a transmitted signal?
A. Its duty cycle
B. Its frequency
C. Its power density
D. All these choices are correct

## Slide 7
G0A02
Which of the following is used to determine RF exposure from a transmitted signal?
A. Its duty cycle
B. Its frequency
C. Its power density
D. All these choices are correct

## Slide 8
G0A03 [97.13(c)(1)]
How can you determine that your station complies with FCC RF exposure regulations?
A. By calculation based on FCC OET Bulletin 65
B. By calculation based on computer modeling
C. By measurement of field strength using calibrated equipment
D. All these choices are correct

## Slide 9
G0A03 [97.13(c)(1)]
How can you determine that your station complies with FCC RF exposure regulations?
A. By calculation based on FCC OET Bulletin 65
B. By calculation based on computer modeling
C. By measurement of field strength using calibrated equipment
D. All these choices are correct

## Slide 10
G0A04
What does "time averaging" mean when evaluating RF radiation exposure?
A. The average amount of power developed by the transmitter over a specific 24-hour period
B. The average time it takes RF radiation to have any long-term effect on the body
C. The total time of the exposure
D. The total RF exposure averaged over a certain period

## Slide 11
G0A04
What does "time averaging" mean when evaluating RF radiation exposure?
A. The average amount of power developed by the transmitter over a specific 24-hour period
B. The average time it takes RF radiation to have any long-term effect on the body
C. The total time of the exposure
D. The total RF exposure averaged over a certain period

## Slide 12
G0A05 [97.13(c)(2), 1.1307(b)]
What must you do if an evaluation of your station shows that the RF energy radiated by your station exceeds permissible limits for possible human absorption?
A. Take action to prevent human exposure to the excessive RF fields
B. File an Environmental Impact Statement (EIS-97) with the FCC
C. Secure written permission from your neighbors to operate above the controlled MPE limits
D. All these choices are correct

## Slide 13
G0A05 [97.13(c)(2), 1.1307(b)]
What must you do if an evaluation of your station shows that the RF energy radiated by your station exceeds permissible limits for possible human absorption?
A. Take action to prevent human exposure to the excessive RF fields
B. File an Environmental Impact Statement (EIS-97) with the FCC
C. Secure written permission from your neighbors to operate above the controlled MPE limits
D. All these choices are correct

## Slide 14
G0A06 [97.13(c)(2), 1.1307(1)(b)(3)(i)]
What must you do if your station fails to meet the FCC RF exposure exemption criteria?
A. Perform an RF Exposure Evaluation in accordance with FCC OET Bulletin 65
B. Contact the FCC for permission to transmit
C. Perform an RF exposure evaluation in accordance with World Meteorological Organization guidelines
D. Use an FCC-approved band-pass filter

## Slide 15
G0A06 [97.13(c)(2), 1.1307(1)(b)(3)(i)]
What must you do if your station fails to meet the FCC RF exposure exemption criteria?
A. Perform an RF Exposure Evaluation in accordance with FCC OET Bulletin 65
B. Contact the FCC for permission to transmit
C. Perform an RF exposure evaluation in accordance with World Meteorological Organization guidelines
D. Use an FCC-approved band-pass filter

## Slide 16
G0A07
What is the effect of modulation duty cycle on RF exposure?
A. A lower duty cycle permits greater power levels to be transmitted
B. A higher duty cycle permits greater power levels to be transmitted
C. Low duty cycle transmitters are exempt from RF exposure evaluation requirements
D. High duty cycle transmitters are exempt from RF exposure requirements

## Slide 17
G0A07
What is the effect of modulation duty cycle on RF exposure?
A. A lower duty cycle permits greater power levels to be transmitted
B. A higher duty cycle permits greater power levels to be transmitted
C. Low duty cycle transmitters are exempt from RF exposure evaluation requirements
D. High duty cycle transmitters are exempt from RF exposure requirements

## Slide 18
G0A08 [97.13(c)(2)]
Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations?
A. Post a copy of FCC Part 97.13 in the station
B. Notify neighbors within a 100-foot radius of the antenna of the existence of the station and power levels
C. Perform a routine RF exposure evaluation and prevent access to any identified high exposure areas
D. All these choices are correct

## Slide 19
G0A08 [97.13(c)(2)]
Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations?
A. Post a copy of FCC Part 97.13 in the station
B. Notify neighbors within a 100-foot radius of the antenna of the existence of the station and power levels
C. Perform a routine RF exposure evaluation and prevent access to any identified high exposure areas
D. All these choices are correct

## Slide 20
G0A09
What type of instrument can be used to accurately measure an RF field strength?
A. A receiver with digital signal processing (DSP) noise reduction
B. A calibrated field strength meter with a calibrated antenna
C. An SWR meter with a peak-reading function
D. An oscilloscope with a high-stability crystal marker generator

## Slide 21
G0A09
What type of instrument can be used to accurately measure an RF field strength?
A. A receiver with digital signal processing (DSP) noise reduction
B. A calibrated field strength meter with a calibrated antenna
C. An SWR meter with a peak-reading function
D. An oscilloscope with a high-stability crystal marker generator

## Slide 22
G0A10
What should be done if evaluation shows that a neighbor might experience more than the allowable limit of RF exposure from the main lobe of a directional antenna?
A. Change to a non-polarized antenna with higher gain
B. Use an antenna with a higher front-to-back ratio
C. Take precautions to ensure that the antenna cannot be pointed in their direction when they are present
D. All these choices are correct

## Slide 23
G0A10
What should be done if evaluation shows that a neighbor might experience more than the allowable limit of RF exposure from the main lobe of a directional antenna?
A. Change to a non-polarized antenna with higher gain
B. Use an antenna with a higher front-to-back ratio
C. Take precautions to ensure that the antenna cannot be pointed in their direction when they are present
D. All these choices are correct

## Slide 24
G0A11
What precaution should be taken if you install an indoor transmitting antenna?
A. Locate the antenna close to your operating position to minimize feed-line radiation
B. Position the antenna along the edge of a wall to reduce parasitic radiation
C. Make sure that MPE limits are not exceeded in occupied areas
D. Make sure the antenna is properly shielded

## Slide 25
G0A11
What precaution should be taken if you install an indoor transmitting antenna?
A. Locate the antenna close to your operating position to minimize feed-line radiation
B. Position the antenna along the edge of a wall to reduce parasitic radiation
C. Make sure that MPE limits are not exceeded in occupied areas
D. Make sure the antenna is properly shielded

## Slide 26
G0A12 [1.1307(1)(b)(3)(i)(A)]
What stations are subject to the FCC rules on RF exposure?
A. All commercial stations; amateur radio stations are exempt
B. Only stations with antennas lower than one wavelength above the ground
C. Only stations transmitting more than 500 watts PEP
D. All stations with a time-averaged transmission of more than one milliwatt

## Slide 27
G0A12 [1.1307(1)(b)(3)(i)(A)]
What stations are subject to the FCC rules on RF exposure?
A. All commercial stations; amateur radio stations are exempt
B. Only stations with antennas lower than one wavelength above the ground
C. Only stations transmitting more than 500 watts PEP
D. All stations with a time-averaged transmission of more than one milliwatt