## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General - G0B
Station safety: electrical shock, grounding, fusing, interlocks, and wiring; antenna and tower safety
For use with The ARRL General Class License Manual, Tenth Edition

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G0B01 - Station safety: electrical shock, grounding, fusing, interlocks, and wiring; antenna and tower safety
Which wire or wires in a four-conductor 240 VAC circuit should be attached to fuses or circuit breakers?
A. Only the hot wires
B. Only the neutral wire
C. Only the ground wire
D. All wires

## Slide 4
G0B01 - Station safety: electrical shock, grounding, fusing, interlocks, and wiring; antenna and tower safety
Which wire or wires in a four-conductor 240 VAC circuit should be attached to fuses or circuit breakers?
A. Only the hot wires
B. Only the neutral wire
C. Only the ground wire
D. All wires

## Slide 5
G0B02
According to the National Electrical Code, what is the minimum wire size that may be used safely for wiring with a 20-ampere circuit breaker?
A. AWG number 20
B. AWG number 16
C. AWG number 12
D. AWG number 8

## Slide 6
G0B02
According to the National Electrical Code, what is the minimum wire size that may be used safely for wiring with a 20-ampere circuit breaker?
A. AWG number 20
B. AWG number 16
C. AWG number 12
D. AWG number 8

## Slide 7
G0B03
Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring?
A. 30 amperes
B. 25 amperes
C. 20 amperes
D. 15 amperes

## Slide 8
G0B03
Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring?
A. 30 amperes
B. 25 amperes
C. 20 amperes
D. 15 amperes

## Slide 9
G0B04
Where should the station's lightning protection ground system be located?
A. As close to the station equipment as possible
B. Outside the building
C. Next to the closest power pole
D. Parallel to the water supply line

## Slide 10
G0B04
Where should the station's lightning protection ground system be located?
A. As close to the station equipment as possible
B. Outside the building
C. Next to the closest power pole
D. Parallel to the water supply line

## Slide 11
G0B05
Which of the following conditions will cause a ground fault circuit interrupter (GFCI) to disconnect AC power?
A. Current flowing from one or more of the hot wires to the neutral wire
B. Current flowing from one or more of the hot wires directly to ground
C. Overvoltage on the hot wires
D. All these choices are correct

## Slide 12
G0B05
Which of the following conditions will cause a ground fault circuit interrupter (GFCI) to disconnect AC power?
A. Current flowing from one or more of the hot wires to the neutral wire
B. Current flowing from one or more of the hot wires directly to ground
C. Overvoltage on the hot wires
D. All these choices are correct

## Slide 13
G0B06
Which of the following is covered by the National Electrical Code?
A. Acceptable bandwidth limits
B. Acceptable modulation limits
C. Electrical safety of the station
D. RF exposure limits of the human body

## Slide 14
G0B06
Which of the following is covered by the National Electrical Code?
A. Acceptable bandwidth limits
B. Acceptable modulation limits
C. Electrical safety of the station
D. RF exposure limits of the human body

## Slide 15
G0B07
Which of these choices should be observed when climbing a tower using a safety harness?
A. Always hold on to the tower with one hand
B. Confirm that the harness is rated for the weight of the climber and that it is within its allowable service life
C. Ensure that all heavy tools are securely fastened to the harness
D. All these choices are correct

## Slide 16
G0B07
Which of these choices should be observed when climbing a tower using a safety harness?
A. Always hold on to the tower with one hand
B. Confirm that the harness is rated for the weight of the climber and that it is within its allowable service life
C. Ensure that all heavy tools are securely fastened to the harness
D. All these choices are correct

## Slide 17
G0B08
What should be done before climbing a tower that supports electrically powered devices?
A. Notify the electric company that a person will be working on the tower
B. Make sure all circuits that supply power to the tower are locked out and tagged
C. Unground the base of the tower
D. All these choices are correct

## Slide 18
G0B08
What should be done before climbing a tower that supports electrically powered devices?
A. Notify the electric company that a person will be working on the tower
B. Make sure all circuits that supply power to the tower are locked out and tagged
C. Unground the base of the tower
D. All these choices are correct

## Slide 19
G0B09
Which of the following is true of an emergency generator installation?
A. The generator should be operated in a well-ventilated area
B. The generator must be insulated from ground
C. Fuel should be stored near the generator for rapid refueling in case of an emergency
D. All these choices are correct

## Slide 20
G0B09
Which of the following is true of an emergency generator installation?
A. The generator should be operated in a well-ventilated area
B. The generator must be insulated from ground
C. Fuel should be stored near the generator for rapid refueling in case of an emergency
D. All these choices are correct

## Slide 21
G0B10
Which of the following is a danger from lead-tin solder?
A. Lead can contaminate food if hands are not washed carefully after handling the solder
B. High voltages can cause lead-tin solder to disintegrate suddenly
C. Tin in the solder can "cold flow," causing shorts in the circuit
D. RF energy can convert the lead into a poisonous gas

## Slide 22
G0B10
Which of the following is a danger from lead-tin solder?
A. Lead can contaminate food if hands are not washed carefully after handling the solder
B. High voltages can cause lead-tin solder to disintegrate suddenly
C. Tin in the solder can "cold flow," causing shorts in the circuit
D. RF energy can convert the lead into a poisonous gas

## Slide 23
G0B11
Which of the following is required for lightning protection ground rods?
A. They must be bonded to all buried water and gas lines
B. Bends in ground wires must be made as close as possible to a right angle
C. Lightning grounds must be connected to all ungrounded wiring
D. They must be bonded together with all other grounds

## Slide 24
G0B11
Which of the following is required for lightning protection ground rods?
A. They must be bonded to all buried water and gas lines
B. Bends in ground wires must be made as close as possible to a right angle
C. Lightning grounds must be connected to all ungrounded wiring
D. They must be bonded together with all other grounds

## Slide 25
G0B12
What is the purpose of a power supply interlock?
A. To prevent unauthorized changes to the circuit that would void the manufacturer's warranty
B. To shut down the unit if it becomes too hot
C. To ensure that dangerous voltages are removed if the cabinet is opened
D. To shut off the power supply if too much voltage is produced

## Slide 26
G0B12
What is the purpose of a power supply interlock?
A. To prevent unauthorized changes to the circuit that would void the manufacturer's warranty
B. To shut down the unit if it becomes too hot
C. To ensure that dangerous voltages are removed if the cabinet is opened
D. To shut off the power supply if too much voltage is produced

## Slide 27
G0B13
Where should lightning arrestors be located?
A. Where the feed lines enter the building
B. On the antenna, opposite the feed point
C. In series with each ground lead
D. At the closest power pole ground electrode

## Slide 28
G0B13
Where should lightning arrestors be located?
A. Where the feed lines enter the building
B. On the antenna, opposite the feed point
C. In series with each ground lead
D. At the closest power pole ground electrode