## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G1C
For use with The ARRL General Class License Manual, Eighth Edition
Transmitter power regulations; data emission standards; 60-meter operation requirements

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G1C01 [97.313(c)(1)]
What is the maximum transmitting power an amateur station may use on 10.140 MHz?
A. 200 watts PEP output
B. 1000 watts PEP output
C. 1500 watts PEP output
D. 2000 watts PEP output

## Slide 4
G1C01 [97.313(c)(1)]
What is the maximum transmitting power an amateur station may use on 10.140 MHz?
A. 200 watts PEP output
B. 1000 watts PEP output
C. 1500 watts PEP output
D. 2000 watts PEP output

## Slide 5
G1C02 [97.313]
What is the maximum transmitting power an amateur station may use on the 12-meter band?
A. 50 watts PEP output
B. 200 watts PEP output
C. 1500 watts PEP output
D. An effective radiated power equivalent to 100 watts from a half-wave dipole

## Slide 6
G1C02 [97.313]
What is the maximum transmitting power an amateur station may use on the 12-meter band?
A. 50 watts PEP output
B. 200 watts PEP output
C. 1500 watts PEP output
D. An effective radiated power equivalent to 100 watts from a half-wave dipole

## Slide 7
G1C03 [97.303(h)(1)]
What is the maximum bandwidth permitted by FCC rules for amateur radio stations transmitting on USB frequencies in the 60-meter band?
A. 2.8 kHz
B. 5.6 kHz
C. 1.8 kHz
D. 3 kHz

## Slide 8
G1C03 [97.303(h)(1)]
What is the maximum bandwidth permitted by FCC rules for amateur radio stations transmitting on USB frequencies in the 60-meter band?
A. 2.8 kHz
B. 5.6 kHz
C. 1.8 kHz
D. 3 kHz

## Slide 9
G1C04 [97.303(i)]
Which of the following is required by the FCC rules when operating in the 60-meter band?
A. If you are using an antenna other than a dipole, you must keep a record of the gain of your antenna
B. You must keep a record of the date, time, frequency, power level, and stations worked
C. You must keep a record of all third-party traffic
D. You must keep a record of the manufacturer of your equipment and the antenna used

## Slide 10
G1C04 [97.303(i)]
Which of the following is required by the FCC rules when operating in the 60-meter band?
A. If you are using an antenna other than a dipole, you must keep a record of the gain of your antenna
B. You must keep a record of the date, time, frequency, power level, and stations worked
C. You must keep a record of all third-party traffic
D. You must keep a record of the manufacturer of your equipment and the antenna used

## Slide 11
G1C05 [97.313]
What is the limit for transmitter power on the 28 MHz band for a General Class control operator?
A. 100 watts PEP output
B. 1000 watts PEP output
C. 1500 watts PEP output
D. 2000 watts PEP output

## Slide 12
G1C05 [97.313]
What is the limit for transmitter power on the 28 MHz band for a General Class control operator?
A. 100 watts PEP output
B. 1000 watts PEP output
C. 1500 watts PEP output
D. 2000 watts PEP output

## Slide 13
G1C06 [97.313]
What is the limit for transmitter power on the 1.8 MHz band?
A. 200 watts PEP output
B. 1000 watts PEP output
C. 1200 watts PEP output
D. 1500 watts PEP output

## Slide 14
G1C06 [97.313]
What is the limit for transmitter power on the 1.8 MHz band?
A. 200 watts PEP output
B. 1000 watts PEP output
C. 1200 watts PEP output
D. 1500 watts PEP output

## Slide 15
G1C07 [97.309(a)(4)]
What must be done before using a new digital protocol on the air?
A. Type-certify equipment to FCC standards
B. Obtain an experimental license from the FCC
C. Publicly document the technical characteristics of the protocol
D. Submit a rule-making proposal to the FCC describing the codes and methods of the technique

## Slide 16
G1C07 [97.309(a)(4)]
What must be done before using a new digital protocol on the air?
A. Type-certify equipment to FCC standards
B. Obtain an experimental license from the FCC
C. Publicly document the technical characteristics of the protocol
D. Submit a rule-making proposal to the FCC describing the codes and methods of the technique

## Slide 17
G1C08 [97.307(f)(3)]
What is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud

## Slide 18
G1C08 [97.307(f)(3)]
What is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud

## Slide 19
G1C09 [97.313(i)]
What is the maximum power limit on the 60-meter band?
A. 1500 watts PEP
B. 10 watts RMS
C. ERP of 100 watts PEP with respect to a dipole
D. ERP of 100 watts PEP with respect to an isotropic antenna

## Slide 20
G1C09 [97.313(i)]
What is the maximum power limit on the 60-meter band?
A. 1500 watts PEP
B. 10 watts RMS
C. ERP of 100 watts PEP with respect to a dipole
D. ERP of 100 watts PEP with respect to an isotropic antenna

## Slide 21
G1C10 [97.305(c) and 97.307(f)(4)]
What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10-meter band?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud

## Slide 22
G1C10 [97.305(c) and 97.307(f)(4)]
What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10-meter band?
A. 56 kilobaud
B. 19.6 kilobaud
C. 1200 baud
D. 300 baud

## Slide 23
G1C11 [97.313]
What measurement is specified by FCC rules that regulate maximum power?
A. RMS output from the transmitter
B. RMS input to the antenna
C. PEP input to the antenna
D. PEP output from the transmitter

## Slide 24
G1C11 [97.313]
What measurement is specified by FCC rules that regulate maximum power?
A. RMS output from the transmitter
B. RMS input to the antenna
C. PEP input to the antenna
D. PEP output from the transmitter