## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G2A
For use with The ARRL General Class License Manual, Eighth Edition
Phone operating procedures: USB/LSB conventions, breaking into a contact, transmitter setup for voice operation; answering DX stations

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G2A01
Which mode is most commonly used for voice communications on frequencies of 14 MHz or higher?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Double sideband

## Slide 4
G2A01
Which mode is most commonly used for voice communications on frequencies of 14 MHz or higher?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Double sideband

## Slide 5
G2A02
Which mode is most commonly used for voice communications on the 160-, 75-, and 40-meter bands?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Double sideband

## Slide 6
G2A02
Which mode is most commonly used for voice communications on the 160-, 75-, and 40-meter bands?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Double sideband

## Slide 7
G2A03
Which mode is most commonly used for SSB voice communications in the VHF and UHF bands?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Double sideband

## Slide 8
G2A03
Which mode is most commonly used for SSB voice communications in the VHF and UHF bands?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Double sideband

## Slide 9
G2A04
Which mode is most commonly used for voice communications on the 17- and 12-meter bands?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Double sideband

## Slide 10
G2A04
Which mode is most commonly used for voice communications on the 17- and 12-meter bands?
A. Upper sideband
B. Lower sideband
C. Suppressed sideband
D. Double sideband

## Slide 11
G2A05
Which mode of voice communication is most commonly used on the HF amateur bands?
A. Frequency modulation
B. Double sideband
C. Single sideband
D. Single phase modulation

## Slide 12
G2A05
Which mode of voice communication is most commonly used on the HF amateur bands?
A. Frequency modulation
B. Double sideband
C. Single sideband
D. Single phase modulation

## Slide 13
G2A06
Which of the following is an advantage of using single sideband, as compared to other analog voice modes on the HF amateur bands?
A. Very high-fidelity voice modulation
B. Less subject to interference from atmospheric static crashes
C. Ease of tuning on receive and immunity to impulse noise
D. Less bandwidth used and greater power efficiency

## Slide 14
G2A06
Which of the following is an advantage of using single sideband, as compared to other analog voice modes on the HF amateur bands?
A. Very high-fidelity voice modulation
B. Less subject to interference from atmospheric static crashes
C. Ease of tuning on receive and immunity to impulse noise
D. Less bandwidth used and greater power efficiency

## Slide 15
G2A07
Which of the following statements is true of single sideband (SSB)?
A. Only one sideband and the carrier are transmitted; the other sideband is suppressed
B. Only one sideband is transmitted; the other sideband and carrier are suppressed
C. SSB is the only voice mode authorized on the 20-, 15-, and 10-meter amateur bands
D. SSB is the only voice mode authorized on the 160-, 75-, and 40-meter amateur bands

## Slide 16
G2A07
Which of the following statements is true of single sideband (SSB)?
A. Only one sideband and the carrier are transmitted; the other sideband is suppressed
B. Only one sideband is transmitted; the other sideband and carrier are suppressed
C. SSB is the only voice mode authorized on the 20-, 15-, and 10-meter amateur bands
D. SSB is the only voice mode authorized on the 160-, 75-, and 40-meter amateur bands

## Slide 17
G2A08
What is the recommended way to break into a phone contact?
A. Say “QRZ” several times, followed by your call sign
B. Say your call sign once
C. Say “Breaker Breaker”
D. Say “CQ” followed by the call sign of either station

## Slide 18
G2A08
What is the recommended way to break into a phone contact?
A. Say “QRZ” several times, followed by your call sign
B. Say your call sign once
C. Say “Breaker Breaker”
D. Say “CQ” followed by the call sign of either station

## Slide 19
G2A09
Why do most amateur stations use lower sideband on the 160-, 75-, and 40-meter bands?
A. Lower sideband is more efficient than upper sideband at these frequencies
B. Lower sideband is the only sideband legal on these frequency bands
C. Because it is fully compatible with an AM detector
D. It is commonly accepted amateur practice

## Slide 20
G2A09
Why do most amateur stations use lower sideband on the 160-, 75-, and 40-meter bands?
A. Lower sideband is more efficient than upper sideband at these frequencies
B. Lower sideband is the only sideband legal on these frequency bands
C. Because it is fully compatible with an AM detector
D. It is commonly accepted amateur practice

## Slide 21
G2A10
Which of the following statements is true of VOX operation versus PTT operation?
A. The received signal is more natural sounding
B. It allows “hands free” operation
C. It occupies less bandwidth
D. It provides more power output

## Slide 22
G2A10
Which of the following statements is true of VOX operation versus PTT operation?
A. The received signal is more natural sounding
B. It allows “hands free” operation
C. It occupies less bandwidth
D. It provides more power output

## Slide 23
G2A11
Generally, who should respond to a station in the contiguous 48 states calling “CQ DX”?
A. Any caller is welcome to respond
B. Only stations in Germany
C. Any stations outside the lower 48 states
D. Only contest stations

## Slide 24
G2A11
Generally, who should respond to a station in the contiguous 48 states calling “CQ DX”?
A. Any caller is welcome to respond
B. Only stations in Germany
C. Any stations outside the lower 48 states
D. Only contest stations

## Slide 25
G2A12
What control is typically adjusted for proper ALC setting on a single sideband transceiver?
A. RF clipping level
B. Transmit audio or microphone gain
C. Antenna inductance or capacitance
D. Attenuator level

## Slide 26
G2A12
What control is typically adjusted for proper ALC setting on a single sideband transceiver?
A. RF clipping level
B. Transmit audio or microphone gain
C. Antenna inductance or capacitance
D. Attenuator level