## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G2C
For use with The ARRL General Class License Manual, Tenth Edition
CW operating procedures and procedural signals; Q signals; full break-in

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G2C01
Which of the following describes full break-in CW operation (QSK)?
A. Breaking stations send the Morse code prosign “BK”
B. Automatic keyers, instead of hand keys, are used to send Morse code
C. An operator must activate a manual send/receive switch before and after every transmission
D. Transmitting stations can receive between code characters and elements

## Slide 4
G2C01
Which of the following describes full break-in CW operation (QSK)?
A. Breaking stations send the Morse code prosign “BK”
B. Automatic keyers, instead of hand keys, are used to send Morse code
C. An operator must activate a manual send/receive switch before and after every transmission
D. Transmitting stations can receive between code characters and elements

## Slide 5
G2C02
What should you do if a CW station sends “QRS?”
A. Send slower
B. Change frequency
C. Increase your power
D. Repeat everything twice

## Slide 6
G2C02
What should you do if a CW station sends “QRS?”
A. Send slower
B. Change frequency
C. Increase your power
D. Repeat everything twice

## Slide 7
G2C03
What does it mean when a CW operator sends “KN” at the end of a transmission?
A. No US stations should call
B. Operating full break-in
C. Listening only for a specific station or stations
D. Closing station now

## Slide 8
G2C03
What does it mean when a CW operator sends “KN” at the end of a transmission?
A. No US stations should call
B. Operating full break-in
C. Listening only for a specific station or stations
D. Closing station now

## Slide 9
G2C04
What does the Q signal “QRL?” mean?
A. “Will you keep the frequency clear?”
B. “Are you operating full break-in?” or “Can you operate full break-in?”
C. “Are you listening only for a specific station?”
D. “Are you busy?” or “Is this frequency in use?”

## Slide 10
G2C04
What does the Q signal “QRL?” mean?
A. “Will you keep the frequency clear?”
B. “Are you operating full break-in?” or “Can you operate full break-in?”
C. “Are you listening only for a specific station?”
D. “Are you busy?” or “Is this frequency in use?”

## Slide 11
G2C05
What is the best speed to use when answering a CQ in Morse code?
A. The fastest speed at which you are comfortable copying, but no slower than the CQ
B. The fastest speed at which you are comfortable copying, but no faster than the CQ
C. At the standard calling speed of 10 wpm
D. At the standard calling speed of 5 wpm

## Slide 12
G2C05
What is the best speed to use when answering a CQ in Morse code?
A. The fastest speed at which you are comfortable copying, but no slower than the CQ
B. The fastest speed at which you are comfortable copying, but no faster than the CQ
C. At the standard calling speed of 10 wpm
D. At the standard calling speed of 5 wpm

## Slide 13
G2C06
What does the term “zero beat” mean in CW operation?
A. Matching the speed of the transmitting station
B. Operating split to avoid interference on frequency
C. Sending without error
D. Matching the transmit frequency to the frequency of a received signal

## Slide 14
G2C06
What does the term “zero beat” mean in CW operation?
A. Matching the speed of the transmitting station
B. Operating split to avoid interference on frequency
C. Sending without error
D. Matching the transmit frequency to the frequency of a received signal

## Slide 15
G2C07
When sending CW, what does a “C” mean when added to the RST report?
A. Chirpy or unstable signal
B. Report was read from an S meter rather than estimated
C. 100 percent copy
D. Key clicks

## Slide 16
G2C07
When sending CW, what does a “C” mean when added to the RST report?
A. Chirpy or unstable signal
B. Report was read from an S meter rather than estimated
C. 100 percent copy
D. Key clicks

## Slide 17
G2C08
What prosign is sent to indicate the end of a formal message when using CW?
A. SK
B. BK
C. AR
D. KN

## Slide 18
G2C08
What prosign is sent to indicate the end of a formal message when using CW?
A. SK
B. BK
C. AR
D. KN

## Slide 19
G2C09
What does the Q signal “QSL” mean?
A. Send slower
B. We have already confirmed the contact
C. I have received and understood
D. We have worked before

## Slide 20
G2C09
What does the Q signal “QSL” mean?
A. Send slower
B. We have already confirmed the contact
C. I have received and understood
D. We have worked before

## Slide 21
G2C10
What does the Q signal “QRN” mean?
A. Send more slowly
B. Stop sending
C. Zero beat my signal
D. I am troubled by static

## Slide 22
G2C10
What does the Q signal “QRN” mean?
A. Send more slowly
B. Stop sending
C. Zero beat my signal
D. I am troubled by static

## Slide 23
G2C11
What does the Q signal “QRV” mean?
A. You are sending too fast
B. There is interference on the frequency
C. I am quitting for the day
D. I am ready to receive

## Slide 24
G2C11
What does the Q signal “QRV” mean?
A. You are sending too fast
B. There is interference on the frequency
C. I am quitting for the day
D. I am ready to receive