## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G2E
For use with The ARRL General Class License Manual, Tenth Edition
Digital mode operating procedures

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G2E01
Which mode is normally used when sending RTTY signals via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB

## Slide 4
G2E01
Which mode is normally used when sending RTTY signals via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB

## Slide 5
G2E02
What is VARA?
A. A low signal-to-noise digital mode used for EME (moonbounce)
B. A digital protocol used with Winlink
C. A radio direction finding system used on VHF and UHF
D.A DX spotting system using a network of software defined radios

## Slide 6
G2E02
What is VARA?
A. A low signal-to-noise digital mode used for EME (moonbounce)
B. A digital protocol used with Winlink
C. A radio direction finding system used on VHF and UHF
D.A DX spotting system using a network of software defined radios

## Slide 7
G2E03
What symptoms may result from other signals interfering with a PACTOR or VARA transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All these choices are correct

## Slide 8
G2E03
What symptoms may result from other signals interfering with a PACTOR or VARA transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All these choices are correct

## Slide 9
G2E04
Which of the following is good practice when choosing a transmitting frequency to answer a station calling CQ using FT8?
A. Always call on the station’s frequency
B. Call on any frequency in the waterfall except the station’s frequency
C. Find a clear frequency during the same time slot as the calling station
D. Find a clear frequency during the alternate time slot to the calling station

## Slide 10
G2E04
Which of the following is good practice when choosing a transmitting frequency to answer a station calling CQ using FT8?
A. Always call on the station’s frequency
B. Call on any frequency in the waterfall except the station’s frequency
C. Find a clear frequency during the same time slot as the calling station
D. Find a clear frequency during the alternate time slot to the calling station

## Slide 11
G2E05
What is the standard sideband for JT65, JT9, FT4, or FT8 digital signal when using AFSK?
A. LSB
B. USB
C. DSB
D. SSB

## Slide 12
G2E05
What is the standard sideband for JT65, JT9, FT4, or FT8 digital signal when using AFSK?
A. LSB
B. USB
C. DSB
D. SSB

## Slide 13
G2E06
What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz

## Slide 14
G2E06
What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz

## Slide 15
G2E07
Which of the following is required when using FT8?
A. A special hardware modem
B. Computer time accurate to within approximately 1 second
C. Receiver attenuator set to -12 dB
D. A vertically polarized antenna

## Slide 16
G2E07
Which of the following is required when using FT8?
A. A special hardware modem
B. Computer time accurate to within approximately 1 second
C. Receiver attenuator set to -12 dB
D. A vertically polarized antenna

## Slide 17
G2E08
In what segment of the 20-meter band are most digital mode operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment, near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Between 14.070 MHz and 14.100 MHz

## Slide 18
G2E08
In what segment of the 20-meter band are most digital mode operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment, near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Between 14.070 MHz and 14.100 MHz

## Slide 19
G2E09
How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode
B. Transmit a steady carrier until the PACTOR protocol times out and disconnects
C. Joining an existing contact is not possible, PACTOR connections are limited to two stations
D. Send a NAK code

## Slide 20
G2E09
How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode
B. Transmit a steady carrier until the PACTOR protocol times out and disconnects
C. Joining an existing contact is not possible, PACTOR connections are limited to two stations
D. Send a NAK code

## Slide 21
G2E10
Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Send an email to the system control operator
B. Send QRL in Morse code
C. Respond when the station broadcasts its SSID
D. Transmit a connect message on the station’s published frequency

## Slide 22
G2E10
Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Send an email to the system control operator
B. Send QRL in Morse code
C. Respond when the station broadcasts its SSID
D. Transmit a connect message on the station’s published frequency

## Slide 23
G2E11
What is the primary purpose of an Amateur Radio Emergency Data Network (AREDN) mesh network?
A. To provide FM repeater coverage in remote areas
B. To provide real time propagation data by monitoring amateur radio transmissions worldwide
C. To provide high-speed data services during an emergency or community event
D. To provide DX spotting reports to aid contesters and DXers

## Slide 24
G2E11
What is the primary purpose of an Amateur Radio Emergency Data Network (AREDN) mesh network?
A. To provide FM repeater coverage in remote areas
B. To provide real time propagation data by monitoring amateur radio transmissions worldwide
C. To provide high-speed data services during an emergency or community event
D. To provide DX spotting reports to aid contesters and DXers

## Slide 25
G2E12
Which of the following describes Winlink?
A. An amateur radio wireless network to send and receive email on the internet
B. A form of Packet Radio
C. A wireless network capable of both VHF and HF band operation
D. All of the above

## Slide 26
G2E12
Which of the following describes Winlink?
A. An amateur radio wireless network to send and receive email on the internet
B. A form of Packet Radio
C. A wireless network capable of both VHF and HF band operation
D. All of the above

## Slide 27
G2E13
What is another name for a Winlink Remote Message Server?
A. Terminal Node Controller
B. Gateway
C. RJ-45
D. Printer/Server

## Slide 28
G2E13
What is another name for a Winlink Remote Message Server?
A. Terminal Node Controller
B. Gateway
C. RJ-45
D. Printer/Server

## Slide 29
G2E14
What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed
B. You may have selected the wrong baud rate
C. You may be listening on the wrong sideband
D. All these choices are correct

## Slide 30
G2E14
What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed
B. You may have selected the wrong baud rate
C. You may be listening on the wrong sideband
D. All these choices are correct

## Slide 31
G2E15
Which of the following is a common location for FT8?
A. Anywhere in the voice portion of the band
B. Anywhere in the CW portion of the band
C. Approximately 14.074 MHz to 14.077 MHz
D. Approximately 14.110 MHz to 14.113 MHz

## Slide 32
G2E15
Which of the following is a common location for FT8?
A. Anywhere in the voice portion of the band
B. Anywhere in the CW portion of the band
C. Approximately 14.074 MHz to 14.077 MHz
D. Approximately 14.110 MHz to 14.113 MHz