## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G3A
For use with The ARRL General Class License Manual, Tenth Edition
Sunspots and solar radiation; geomagnetic field and stability indices

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G3A01
How does a higher sunspot number affect HF propagation?
A. Higher sunspot numbers generally indicate a greater probability of good propagation at higher frequencies
B. Lower sunspot numbers generally indicate greater probability of sporadic E propagation
C. A zero sunspot number indicates that radio propagation is not possible on any band
D. A zero sunspot number indicates undisturbed conditions

## Slide 4
G3A01
How does a higher sunspot number affect HF propagation?
A. Higher sunspot numbers generally indicate a greater probability of good propagation at higher frequencies
B. Lower sunspot numbers generally indicate greater probability of sporadic E propagation
C. A zero sunspot number indicates that radio propagation is not possible on any band
D. A zero sunspot number indicates undisturbed conditions

## Slide 5
G3A02
What effect does a sudden ionospheric disturbance have on the daytime ionospheric propagation?
A. It enhances propagation on all HF frequencies
B. It disrupts signals on lower frequencies more than those on higher frequencies
C. It disrupts communications via satellite more than direct communications
D. None, because only areas on the night side of the Earth are affected

## Slide 6
G3A02
What effect does a sudden ionospheric disturbance have on the daytime ionospheric propagation?
A. It enhances propagation on all HF frequencies
B. It disrupts signals on lower frequencies more than those on higher frequencies
C. It disrupts communications via satellite more than direct communications
D. None, because only areas on the night side of the Earth are affected

## Slide 7
G3A03
Approximately how long does it take the increased ultraviolet and X-ray radiation from a solar flare to affect radio propagation on Earth?
A. 28 days
B. 1 to 2 hours
C. 8 minutes
D. 20 to 40 hours

## Slide 8
G3A03
Approximately how long does it take the increased ultraviolet and X-ray radiation from a solar flare to affect radio propagation on Earth?
A. 28 days
B. 1 to 2 hours
C. 8 minutes
D. 20 to 40 hours

## Slide 9
G3A04
Which of the following are the least reliable bands for long-distance communications during periods of low solar activity?
A. 80 meters and 160 meters
B. 60 meters and 40 meters
C. 30 meters and 20 meters
D. 15 meters, 12 meters, and 10 meters

## Slide 10
G3A04
Which of the following are the least reliable bands for long-distance communications during periods of low solar activity?
A. 80 meters and 160 meters
B. 60 meters and 40 meters
C. 30 meters and 20 meters
D. 15 meters, 12 meters, and 10 meters

## Slide 11
G3A05
What is the solar flux index?
A. A measure of the highest frequency that is useful for ionospheric propagation between two points on Earth
B. A count of sunspots that is adjusted for solar emissions
C. Another name for the American sunspot number
D. A measure of solar radiation with a wavelength of 10.7 centimeters

## Slide 12
G3A05
What is the solar flux index?
A. A measure of the highest frequency that is useful for ionospheric propagation between two points on Earth
B. A count of sunspots that is adjusted for solar emissions
C. Another name for the American sunspot number
D. A measure of solar radiation with a wavelength of 10.7 centimeters

## Slide 13
G3A06
What is a geomagnetic storm?
A. A sudden drop in the solar flux index
B. A thunderstorm that affects radio propagation
C. Ripples in the geomagnetic force
D. A temporary disturbance in Earth’s geomagnetic field

## Slide 14
G3A06
What is a geomagnetic storm?
A. A sudden drop in the solar flux index
B. A thunderstorm that affects radio propagation
C. Ripples in the geomagnetic force
D. A temporary disturbance in Earth’s geomagnetic field

## Slide 15
G3A07
At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours?
A. At the summer solstice
B. Only at the maximum point
C. Only at the minimum point
D. At any point

## Slide 16
G3A07
At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours?
A. At the summer solstice
B. Only at the maximum point
C. Only at the minimum point
D. At any point

## Slide 17
G3A08
How can a geomagnetic storm affect HF propagation?
A. Improve high-latitude HF propagation
B. Degrade ground wave propagation
C. Improve ground wave propagation
D. Degrade high-latitude HF propagation

## Slide 18
G3A08
How can a geomagnetic storm affect HF propagation?
A. Improve high-latitude HF propagation
B. Degrade ground wave propagation
C. Improve ground wave propagation
D. Degrade high-latitude HF propagation

## Slide 19
G3A09
How can high geomagnetic activity benefit radio communications?
A. Creates auroras that can reflect VHF signals
B. Increases signal strength for HF signals passing through the polar regions
C. Improve HF long path propagation
D. Reduce long delayed echoes

## Slide 20
G3A09
How can high geomagnetic activity benefit radio communications?
A. Creates auroras that can reflect VHF signals
B. Increases signal strength for HF signals passing through the polar regions
C. Improve HF long path propagation
D. Reduce long delayed echoes

## Slide 21
G3A10
What causes HF propagation conditions to vary periodically in a 26- to 28-day cycle?
A. Long term oscillations in the upper atmosphere
B. Cyclic variation in Earth’s radiation belts
C. Rotation of the Sun’s surface layers around its axis
D. The position of the Moon in its orbit

## Slide 22
G3A10
What causes HF propagation conditions to vary periodically in a 26- to 28-day cycle?
A. Long term oscillations in the upper atmosphere
B. Cyclic variation in Earth’s radiation belts
C. Rotation of the Sun’s surface layers around its axis
D. The position of the Moon in its orbit

## Slide 23
G3A11
How long does it take a coronal mass ejection to affect radio propagation on Earth?
A. 28 days
B. 14 days
C. 4 to 8 minutes
D. 15 hours to several days

## Slide 24
G3A11
How long does it take a coronal mass ejection to affect radio propagation on Earth?
A. 28 days
B. 14 days
C. 4 to 8 minutes
D. 15 hours to several days

## Slide 25
G3A12
What does the K-index measure?
A. The relative position of sunspots on the surface of the Sun
B. The short-term stability of Earth’s geomagnetic field
C. The short-term stability of the Sun’s magnetic field
D. The solar radio flux at Boulder, Colorado

## Slide 26
G3A12
What does the K-index measure?
A. The relative position of sunspots on the surface of the Sun
B. The short-term stability of Earth’s geomagnetic field
C. The short-term stability of the Sun’s magnetic field
D. The solar radio flux at Boulder, Colorado

## Slide 27
G3A13
What does the A-index measure?
A. The relative position of sunspots on the surface of the Sun
B. The amount of polarization of the Sun’s electric field
C. The long-term stability of Earth’s geomagnetic field
D. The solar radio flux at Boulder, Colorado

## Slide 28
G3A13
What does the A-index measure?
A. The relative position of sunspots on the surface of the Sun
B. The amount of polarization of the Sun’s electric field
C. The long-term stability of Earth’s geomagnetic field
D. The solar radio flux at Boulder, Colorado

## Slide 29
G3A14
How is long distance radio communication usually affected by the charged particles that reach Earth from solar coronal holes?
A. HF communication is improved
B. HF communication is disturbed
C. VHF/UHF ducting is improved
D. VHF/UHF ducting is disturbed

## Slide 30
G3A14
How is long distance radio communication usually affected by the charged particles that reach Earth from solar coronal holes?
A. HF communication is improved
B. HF communication is disturbed
C. VHF/UHF ducting is improved
D. VHF/UHF ducting is disturbed