## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G3B
For use with The ARRL General Class License Manual, Tenth Edition
Maximum Usable Frequency; Lowest Usable Frequency; short path and long path propagation; determining propagation conditions; ionospheric refraction

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G3B01
What is a characteristic of skywave signals arriving at your location by both short-path and long-path propagation?
A. Periodic fading approximately every 10 seconds
B. Signal strength increased by 3 dB
C. The signal might be cancelled causing severe attenuation
D. A slightly delayed echo might be heard

## Slide 4
G3B01
What is a characteristic of skywave signals arriving at your location by both short-path and long-path propagation?
A. Periodic fading approximately every 10 seconds
B. Signal strength increased by 3 dB
C. The signal might be cancelled causing severe attenuation
D. A slightly delayed echo might be heard

## Slide 5
G3B02
What factors affect the MUF?
A. Path distance and location
B. Time of day and season
C. Solar radiation and ionospheric disturbances
D. All these choices are correct

## Slide 6
G3B02
What factors affect the MUF?
A. Path distance and location
B. Time of day and season
C. Solar radiation and ionospheric disturbances
D. All these choices are correct

## Slide 7
G3B03
Which frequency will have the least attenuation for long-distance skip propagation?
A. Just below the MUF
B. Just above the LUF
C. Just below the critical frequency
D. Just above the critical frequency

## Slide 8
G3B03
Which frequency will have the least attenuation for long-distance skip propagation?
A. Just below the MUF
B. Just above the LUF
C. Just below the critical frequency
D. Just above the critical frequency

## Slide 9
G3B04
Which of the following is a way to determine current propagation on a desired band from your station?
A. Use a network of automated receiving stations on the internet to see where your transmissions are being received
B. Check the A-index
C. Send a series of dots and listen for echoes
D. All these choices are correct

## Slide 10
G3B04
Which of the following is a way to determine current propagation on a desired band from your station?
A. Use a network of automated receiving stations on the internet to see where your transmissions are being received
B. Check the A-index
C. Send a series of dots and listen for echoes
D. All these choices are correct

## Slide 11
G3B05
How does the ionosphere affect radio waves with frequencies below the MUF and above the LUF?
A. They are refracted back to Earth
B. They pass through the ionosphere
C. They are amplified by interaction with the ionosphere
D. They are refracted and trapped in the ionosphere to circle Earth

## Slide 12
G3B05
How does the ionosphere affect radio waves with frequencies below the MUF and above the LUF?
A. They are refracted back to Earth
B. They pass through the ionosphere
C. They are amplified by interaction with the ionosphere
D. They are refracted and trapped in the ionosphere to circle Earth

## Slide 13
G3B06
What usually happens to radio waves with frequencies below the LUF?
A. They are refracted back to Earth
B. They pass through the ionosphere
C. They are attenuated before reaching the destination
D. They are refracted and trapped in the ionosphere to circle Earth

## Slide 14
G3B06
What usually happens to radio waves with frequencies below the LUF?
A. They are refracted back to Earth
B. They pass through the ionosphere
C. They are attenuated before reaching the destination
D. They are refracted and trapped in the ionosphere to circle Earth

## Slide 15
G3B07
What does LUF stand for?
A. The Lowest Usable Frequency for communications between two specific points
B. Lowest Usable Frequency for communications to any point outside a 100-mile radius
C. The Lowest Usable Frequency during a 24-hour period
D. Lowest Usable Frequency during the past 60 minutes

## Slide 16
G3B07
What does LUF stand for?
A. The Lowest Usable Frequency for communications between two specific points
B. Lowest Usable Frequency for communications to any point outside a 100-mile radius
C. The Lowest Usable Frequency during a 24-hour period
D. Lowest Usable Frequency during the past 60 minutes

## Slide 17
G3B08
What does MUF stand for?
A. The Minimum Usable Frequency for communications between two points
B. The Maximum Usable Frequency for communications between two points
C. The Minimum Usable Frequency during a 24-hour period
D. The Maximum Usable Frequency during a 24-hour period

## Slide 18
G3B08
What does MUF stand for?
A. The Minimum Usable Frequency for communications between two points
B. The Maximum Usable Frequency for communications between two points
C. The Minimum Usable Frequency during a 24-hour period
D. The Maximum Usable Frequency during a 24-hour period

## Slide 19
G3B09
What is the approximate maximum distance along the Earth’s surface normally covered in one hop using the F2 region?
A. 180 miles
B. 1,200 miles
C. 2,500 miles
D. 12,000 miles

## Slide 20
G3B09
What is the approximate maximum distance along the Earth’s surface normally covered in one hop using the F2 region?
A. 180 miles
B. 1,200 miles
C. 2,500 miles
D. 12,000 miles

## Slide 21
G3B10
What is the approximate maximum distance along the Earth’s surface normally covered in one hop using the E region?
A. 180 miles
B. 1,200 miles
C. 2,500 miles
D. 12,000 miles

## Slide 22
G3B10
What is the approximate maximum distance along the Earth’s surface normally covered in one hop using the E region?
A. 180 miles
B. 1,200 miles
C. 2,500 miles
D. 12,000 miles

## Slide 23
G3B11
What happens to HF propagation when the LUF exceeds the MUF?
A. Propagation via ordinary skywave communications is not possible over that path
B. HF communications over the path are enhanced
C. Double-hop propagation along the path is more common
D. Propagation over the path on all HF frequencies is enhanced

## Slide 24
G3B11
What happens to HF propagation when the LUF exceeds the MUF?
A. Propagation via ordinary skywave communications is not possible over that path
B. HF communications over the path are enhanced
C. Double-hop propagation along the path is more common
D. Propagation over the path on all HF frequencies is enhanced

## Slide 25
G3B12
Which of the following is typical of the lower HF frequencies during the summer?
A. Poor propagation at any time of day
B. World-wide propagation during daylight hours
C. Heavy distortion on signals due to photon absorption
D. High levels of atmospheric noise or static

## Slide 26
G3B12
Which of the following is typical of the lower HF frequencies during the summer?
A. Poor propagation at any time of day
B. World-wide propagation during daylight hours
C. Heavy distortion on signals due to photon absorption
D. High levels of atmospheric noise or static