## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G3C
For use with The ARRL General Class License Manual, Tenth Edition
Ionospheric regions; critical angle and frequency; HF scatter; near vertical incidence skywave (NVIS)

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G3C01
Which ionospheric region is closest to the surface of Earth?
A. The D region
B. The E region
C. The F1 region
D. The F2 region

## Slide 4
G3C01
Which ionospheric region is closest to the surface of Earth?
A. The D region
B. The E region
C. The F1 region
D. The F2 region

## Slide 5
G3C02
What is meant by the term “critical frequency” at a given incidence angle?
A. The highest frequency which is refracted back to Earth
B. The lowest frequency which is refracted back to Earth
C. The frequency at which the signal-to-noise ratio approaches unity
D. The frequency at which the signal-to-noise ratio is 6 dB

## Slide 6
G3C02
What is meant by the term “critical frequency” at a given incidence angle?
A. The highest frequency which is refracted back to Earth
B. The lowest frequency which is refracted back to Earth
C. The frequency at which the signal-to-noise ratio approaches unity
D. The frequency at which the signal-to-noise ratio is 6 dB

## Slide 7
G3C03
Why is skip propagation via the F2 region longer than that via the other ionospheric regions?
A. Because it is the densest
B. Because of the Doppler effect
C. Because it is the highest
D. Because of temperature inversions

## Slide 8
G3C03
Why is skip propagation via the F2 region longer than that via the other ionospheric regions?
A. Because it is the densest
B. Because of the Doppler effect
C. Because it is the highest
D. Because of temperature inversions

## Slide 9
G3C04
What does the term “critical angle” mean, as applied to radio wave propagation?
A. The long path azimuth of a distant station
B. The short path azimuth of a distant station
C. The lowest takeoff angle that will return a radio wave to Earth under specific ionospheric conditions
D. The highest takeoff angle that will return a radio wave to Earth under specific ionospheric conditions

## Slide 10
G3C04
What does the term “critical angle” mean, as applied to radio wave propagation?
A. The long path azimuth of a distant station
B. The short path azimuth of a distant station
C. The lowest takeoff angle that will return a radio wave to Earth under specific ionospheric conditions
D. The highest takeoff angle that will return a radio wave to Earth under specific ionospheric conditions

## Slide 11
G3C05
Why is long-distance communication on the 40-, 60-, 80-, and 160-meter bands more difficult during the day?
A. The F region absorbs signals at these frequencies during daylight hours
B. The F region is unstable during daylight hours
C. The D region absorbs signals at these frequencies during daylight hours
D. The E region is unstable during daylight hours

## Slide 12
G3C05
Why is long-distance communication on the 40-, 60-, 80-, and 160-meter bands more difficult during the day?
A. The F region absorbs signals at these frequencies during daylight hours
B. The F region is unstable during daylight hours
C. The D region absorbs signals at these frequencies during daylight hours
D. The E region is unstable during daylight hours

## Slide 13
G3C06
What is a characteristic of HF scatter?
A. Phone signals have high intelligibility
B. Signals have a fluttering sound
C. There are very large, sudden swings in signal strength
D. Scatter propagation occurs only at night

## Slide 14
G3C06
What is a characteristic of HF scatter?
A. Phone signals have high intelligibility
B. Signals have a fluttering sound
C. There are very large, sudden swings in signal strength
D. Scatter propagation occurs only at night

## Slide 15
G3C07
What makes HF scatter signals often sound distorted?
A. The ionospheric region involved is unstable
B. Ground waves are absorbing much of the signal
C. The E region is not present
D. Energy is scattered into the skip zone through several different paths

## Slide 16
G3C07
What makes HF scatter signals often sound distorted?
A. The ionospheric region involved is unstable
B. Ground waves are absorbing much of the signal
C. The E region is not present
D. Energy is scattered into the skip zone through several different paths

## Slide 17
G3C08
Why are HF scatter signals in the skip zone usually weak?
A. Only a small part of the signal energy is scattered into the skip zone
B. Signals are scattered from the magnetosphere, which is not a good reflector
C. Propagation is via ground waves, which absorb most of the signal energy
D. Propagation is via ducts in the F region, which absorb most of the energy

## Slide 18
G3C08
Why are HF scatter signals in the skip zone usually weak?
A. Only a small part of the signal energy is scattered into the skip zone
B. Signals are scattered from the magnetosphere, which is not a good reflector
C. Propagation is via ground waves, which absorb most of the signal energy
D. Propagation is via ducts in the F region, which absorb most of the energy

## Slide 19
G3C09
What type of propagation allows signals to be heard in the transmitting station’s skip zone?
A. Faraday rotation
B. Scatter
C. Chordal hop
D. Short-path

## Slide 20
G3C09
What type of propagation allows signals to be heard in the transmitting station’s skip zone?
A. Faraday rotation
B. Scatter
C. Chordal hop
D. Short-path

## Slide 21
G3C10
What is near vertical incidence skywave (NVIS) propagation?
A. Propagation near the MUF
B. Short distance MF or HF propagation at high elevation angles
C. Long path HF propagation at sunrise and sunset
D. Double hop propagation near the LUF

## Slide 22
G3C10
What is near vertical incidence skywave (NVIS) propagation?
A. Propagation near the MUF
B. Short distance MF or HF propagation at high elevation angles
C. Long path HF propagation at sunrise and sunset
D. Double hop propagation near the LUF

## Slide 23
G3C11
Which ionospheric region is the most absorbent of signals below 10 MHz during daylight hours?
A. The F2 region
B. The F1 region
C. The E region
D. The D region

## Slide 24
G3C11
Which ionospheric region is the most absorbent of signals below 10 MHz during daylight hours?
A. The F2 region
B. The F1 region
C. The E region
D. The D region