## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G4B
For use with The ARRL General Class License Manual, Tenth Edition
Tests and test equipment

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G4B01
What item of test equipment contains horizontal and vertical channel amplifiers?
A. An ohmmeter
B. A signal generator
C. An ammeter
D. An oscilloscope

## Slide 4
G4B01
What item of test equipment contains horizontal and vertical channel amplifiers?
A. An ohmmeter
B. A signal generator
C. An ammeter
D. An oscilloscope

## Slide 5
G4B02
Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
A. An oscilloscope uses less power
B. Complex impedances can be easily measured
C. Greater precision
D. Complex waveforms can be measured

## Slide 6
G4B02
Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
A. An oscilloscope uses less power
B. Complex impedances can be easily measured
C. Greater precision
D. Complex waveforms can be measured

## Slide 7
G4B03
Which of the following is the best instrument to use for checking the keying waveform of a CW transmitter?
A. An oscilloscope
B. A field strength meter
C. A sidetone monitor
D. A wavemeter

## Slide 8
G4B03
Which of the following is the best instrument to use for checking the keying waveform of a CW transmitter?
A. An oscilloscope
B. A field strength meter
C. A sidetone monitor
D. A wavemeter

## Slide 9
G4B04
What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
A. The local oscillator of the transmitter
B. An external RF oscillator
C. The transmitter balanced mixer output
D. The attenuated RF output of the transmitter

## Slide 10
G4B04
What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
A. The local oscillator of the transmitter
B. An external RF oscillator
C. The transmitter balanced mixer output
D. The attenuated RF output of the transmitter

## Slide 11
G4B05
Why do voltmeters have high input impedance?
A. It improves the frequency response
B. It allows for higher voltages to be safely measured
C. It improves the resolution of the readings
D. It decreases the loading on circuits being measured

## Slide 12
G4B05
Why do voltmeters have high input impedance?
A. It improves the frequency response
B. It allows for higher voltages to be safely measured
C. It improves the resolution of the readings
D. It decreases the loading on circuits being measured

## Slide 13
G4B06
What is an advantage of a digital multimeter as compared to an analog multimeter?
A. Better for measuring computer circuits
B. Less prone to overload
C. Higher precision
D. Faster response

## Slide 14
G4B06
What is an advantage of a digital multimeter as compared to an analog multimeter?
A. Better for measuring computer circuits
B. Less prone to overload
C. Higher precision
D. Faster response

## Slide 15
G4B07
What signals are used to conduct a two-tone test?
A. Two audio signals of the same frequency shifted 90 degrees
B. Two non-harmonically related audio signals
C. Two swept frequency tones
D. Two audio frequency range square wave signals of equal amplitude

## Slide 16
G4B07
What signals are used to conduct a two-tone test?
A. Two audio signals of the same frequency shifted 90 degrees
B. Two non-harmonically related audio signals
C. Two swept frequency tones
D. Two audio frequency range square wave signals of equal amplitude

## Slide 17
G4B08
What transmitter performance parameter does a two-tone test analyze?
A. Linearity
B. Percentage of suppression of the carrier and undesired sideband for SSB
C. Percentage of frequency modulation
D. Percentage of carrier phase shift

## Slide 18
G4B08
What transmitter performance parameter does a two-tone test analyze?
A. Linearity
B. Percentage of suppression of the carrier and undesired sideband for SSB
C. Percentage of frequency modulation
D. Percentage of carrier phase shift

## Slide 19
G4B09
When is an analog multimeter preferred to a digital multimeter?
A. When testing logic circuits
B. When high precision is desired
C. When measuring the frequency of an oscillator
D. When adjusting circuits for maximum or minimum values

## Slide 20
G4B09
When is an analog multimeter preferred to a digital multimeter?
A. When testing logic circuits
B. When high precision is desired
C. When measuring the frequency of an oscillator
D. When adjusting circuits for maximum or minimum values

## Slide 21
G4B10
Which of the following can be determined with a directional wattmeter?
A. Standing wave ratio
B. Antenna front-to-back ratio
C. RF interference
D. Radio wave propagation

## Slide 22
G4B10
Which of the following can be determined with a directional wattmeter?
A. Standing wave ratio
B. Antenna front-to-back ratio
C. RF interference
D. Radio wave propagation

## Slide 23
G4B11
Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
A. Receiver
B. Transmitter
C. Antenna and feed line
D. All these choices are correct

## Slide 24
G4B11
Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
A. Receiver
B. Transmitter
C. Antenna and feed line
D. All these choices are correct

## Slide 25
G4B12
What effect can strong signals from nearby transmitters have on an antenna analyzer?
A. Desensitization which can cause intermodulation products which interfere with impedance readings
B. Received power that interferes with SWR readings
C. Generation of harmonics which interfere with frequency readings
D. All these choices are correct

## Slide 26
G4B12
What effect can strong signals from nearby transmitters have on an antenna analyzer?
A. Desensitization which can cause intermodulation products which interfere with impedance readings
B. Received power that interferes with SWR readings
C. Generation of harmonics which interfere with frequency readings
D. All these choices are correct

## Slide 27
G4B13
Which of the following can be measured with an antenna analyzer?
A. Front-to-back ratio of an antenna
B. Power output from a transmitter
C. Impedance of coaxial cable
D. Gain of a directional antenna

## Slide 28
G4B13
Which of the following can be measured with an antenna analyzer?
A. Front-to-back ratio of an antenna
B. Power output from a transmitter
C. Impedance of coaxial cable
D. Gain of a directional antenna