## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G4C
For use with The ARRL General Class License Manual, Tenth Edition
Interference to consumer electronics; grounding and bonding

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G4C01
Which of the following might be useful in reducing RF interference to audio frequency circuits?
A. Bypass inductor
B. Bypass capacitor
C. Forward-biased diode
D. Reverse-biased diode

## Slide 4
G4C01
Which of the following might be useful in reducing RF interference to audio frequency circuits?
A. Bypass inductor
B. Bypass capacitor
C. Forward-biased diode
D. Reverse-biased diode

## Slide 5
G4C02
Which of the following could be a cause of interference covering a wide range of frequencies?
A. Not using a balun or line isolator to feed balanced antennas
B. Lack of rectification of the transmitter’s signal in power conductors
C. Arcing at a poor electrical connection
D. Using a balun to feed an unbalanced antenna

## Slide 6
G4C02
Which of the following could be a cause of interference covering a wide range of frequencies?
A. Not using a balun or line isolator to feed balanced antennas
B. Lack of rectification of the transmitter’s signal in power conductors
C. Arcing at a poor electrical connection
D. Using a balun to feed an unbalanced antenna

## Slide 7
G4C03
What sound is heard from an audio device experiencing RF interference from a single sideband phone transmitter?
A. A steady hum whenever the transmitter is on the air
B. On-and-off humming or clicking
C. Distorted speech
D. Clearly audible speech

## Slide 8
G4C03
What sound is heard from an audio device experiencing RF interference from a single sideband phone transmitter?
A. A steady hum whenever the transmitter is on the air
B. On-and-off humming or clicking
C. Distorted speech
D. Clearly audible speech

## Slide 9
G4C04
What sound is heard from an audio device experiencing RF interference from a CW transmitter?
A. On-and-off humming or clicking
B. A CW signal at a nearly pure audio frequency
C. A chirpy CW signal
D. Severely distorted audio

## Slide 10
G4C04
What sound is heard from an audio device experiencing RF interference from a CW transmitter?
A. On-and-off humming or clicking
B. A CW signal at a nearly pure audio frequency
C. A chirpy CW signal
D. Severely distorted audio

## Slide 11
G4C05
What is a possible cause of high voltages that produce RF burns?
A. Flat braid rather than round wire has been used for the ground wire
B. Insulated wire has been used for the ground wire
C. The ground rod is resonant
D. The ground wire has high impedance on that frequency

## Slide 12
G4C05
What is a possible cause of high voltages that produce RF burns?
A. Flat braid rather than round wire has been used for the ground wire
B. Insulated wire has been used for the ground wire
C. The ground rod is resonant
D. The ground wire has high impedance on that frequency

## Slide 13
G4C06
What is a possible effect of a resonant ground connection?
A. Overheating of ground straps
B. Corrosion of the ground rod
C. High RF voltages on the enclosures of station equipment
D. A ground loop

## Slide 14
G4C06
What is a possible effect of a resonant ground connection?
A. Overheating of ground straps
B. Corrosion of the ground rod
C. High RF voltages on the enclosures of station equipment
D. A ground loop

## Slide 15
G4C07
Why should soldered joints not be used in lightning protection ground connections?
A. A soldered joint will likely be destroyed by the heat of a lightning strike
B. Solder flux will prevent a low conductivity connection
C. Solder has too high a dielectric constant to provide adequate lightning protection
D. All these choices are correct

## Slide 16
G4C07
Why should soldered joints not be used in lightning protection ground connections?
A. A soldered joint will likely be destroyed by the heat of a lightning strike
B. Solder flux will prevent a low conductivity connection
C. Solder has too high a dielectric constant to provide adequate lightning protection
D. All these choices are correct

## Slide 17
G4C08
Which of the following would reduce RF interference caused by common-mode current on an audio cable?
A. Place a ferrite choke on the cable
B. Connect the center conductor to the shield of all cables to short circuit the RFI signal
C. Ground the center conductor of the audio cable causing the interference
D. Add an additional insulating jacket to the cable

## Slide 18
G4C08
Which of the following would reduce RF interference caused by common-mode current on an audio cable?
A. Place a ferrite choke on the cable
B. Connect the center conductor to the shield of all cables to short circuit the RFI signal
C. Ground the center conductor of the audio cable causing the interference
D. Add an additional insulating jacket to the cable

## Slide 19
G4C09
How can the effects of ground loops be minimized?
A. Connect all ground conductors in series
B. Connect the AC neutral conductor to the ground wire
C. Avoid using lock washers and star washers when making ground connections
D. Bond equipment enclosures together

## Slide 20
G4C09
How can the effects of ground loops be minimized?
A. Connect all ground conductors in series
B. Connect the AC neutral conductor to the ground wire
C. Avoid using lock washers and star washers when making ground connections
D. Bond equipment enclosures together

## Slide 21
G4C10
What could be a symptom caused by a ground loop in your station’s audio connections?
A. You receive reports of “hum” on your station’s transmitted signal
B. The SWR reading for one or more antennas is suddenly very high
C. An item of station equipment starts to draw excessive amounts of current
D. You receive reports of harmonic interference from your station

## Slide 22
G4C10
What could be a symptom caused by a ground loop in your station’s audio connections?
A. You receive reports of “hum” on your station’s transmitted signal
B. The SWR reading for one or more antennas is suddenly very high
C. An item of station equipment starts to draw excessive amounts of current
D. You receive reports of harmonic interference from your station

## Slide 23
G4C11
What technique helps to minimize RF “hot spots” in an amateur station?
A. Building all equipment in a metal enclosure
B. Using surge suppressor power outlets
C. Bonding all equipment enclosures together
D. Placing low-pass filters on all feed lines

## Slide 24
G4C11
What technique helps to minimize RF “hot spots” in an amateur station?
A. Building all equipment in a metal enclosure
B. Using surge suppressor power outlets
C. Bonding all equipment enclosures together
D. Placing low-pass filters on all feed lines

## Slide 25
G4C12
Why must all metal enclosures of station equipment be grounded?
A. It prevents a blown fuse in the event of an internal short circuit
B. It prevents signal overload
C. It ensures that the neutral wire is grounded
D. It ensures that hazardous voltages cannot appear on the chassis

## Slide 26
G4C12
Why must all metal enclosures of station equipment be grounded?
A. It prevents a blown fuse in the event of an internal short circuit
B. It prevents signal overload
C. It ensures that the neutral wire is grounded
D. It ensures that hazardous voltages cannot appear on the chassis