## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G4D
For use with The ARRL General Class License Manual, Tenth Edition
Speech processors; S meters; sideband operation near band edges

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G4D01
What is the purpose of a speech processor in a transceiver?
A. Increase the apparent loudness of transmitted voice signals
B. Increase transmitter bass response for more natural-sounding SSB signals
C. Prevent distortion of voice signals
D. Decrease high-frequency voice output to prevent out-of-band operation

## Slide 4
G4D01
What is the purpose of a speech processor in a transceiver?
A. Increase the apparent loudness of transmitted voice signals
B. Increase transmitter bass response for more natural-sounding SSB signals
C. Prevent distortion of voice signals
D. Decrease high-frequency voice output to prevent out-of-band operation

## Slide 5
G4D02
How does a speech processor affect a single sideband phone signal?
A. It increases peak power
B. It increases average power
C. It reduces harmonic distortion
D. It reduces intermodulation distortion

## Slide 6
G4D02
How does a speech processor affect a single sideband phone signal?
A. It increases peak power
B. It increases average power
C. It reduces harmonic distortion
D. It reduces intermodulation distortion

## Slide 7
G4D03
What is the effect of an incorrectly adjusted speech processor?
A. Distorted speech
B. Excess intermodulation products
C. Excessive background noise
D. All these choices are correct

## Slide 8
G4D03
What is the effect of an incorrectly adjusted speech processor?
A. Distorted speech
B. Excess intermodulation products
C. Excessive background noise
D. All these choices are correct

## Slide 9
G4D04
What does an S meter measure?
A. Carrier suppression
B. Impedance
C. Received signal strength
D. Transmitter power output

## Slide 10
G4D04
What does an S meter measure?
A. Carrier suppression
B. Impedance
C. Received signal strength
D. Transmitter power output

## Slide 11
G4D05
How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
A. It is 10 times less powerful
B. It is 20 times less powerful
C. It is 20 times more powerful
D. It is 100 times more powerful

## Slide 12
G4D05
How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
A. It is 10 times less powerful
B. It is 20 times less powerful
C. It is 20 times more powerful
D. It is 100 times more powerful

## Slide 13
G4D06
How much change in signal strength is typically represented by one S unit?
A. 6 dB
B. 12 dB
C. 15 dB
D. 18 dB

## Slide 14
G4D06
How much change in signal strength is typically represented by one S unit?
A. 6 dB
B. 12 dB
C. 15 dB
D. 18 dB

## Slide 15
G4D07
How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
A. Approximately 1.5 times
B. Approximately 2 times
C. Approximately 4 times
D. Approximately 8 times

## Slide 16
G4D07
How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
A. Approximately 1.5 times
B. Approximately 2 times
C. Approximately 4 times
D. Approximately 8 times

## Slide 17
G4D08
What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
A. 7.178 MHz to 7.181 MHz
B. 7.178 MHz to 7.184 MHz
C. 7.175 MHz to 7.178 MHz
D. 7.1765 MHz to 7.1795 MHz

## Slide 18
G4D08
What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
A. 7.178 MHz to 7.181 MHz
B. 7.178 MHz to 7.184 MHz
C. 7.175 MHz to 7.178 MHz
D. 7.1765 MHz to 7.1795 MHz

## Slide 19
G4D09
What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
A. 14.347 MHz to 14.647 MHz
B. 14.347 MHz to 14.350 MHz
C. 14.344 MHz to 14.347 MHz
D. 14.3455 MHz to 14.3485 MHz

## Slide 20
G4D09
What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
A. 14.347 MHz to 14.647 MHz
B. 14.347 MHz to 14.350 MHz
C. 14.344 MHz to 14.347 MHz
D. 14.3455 MHz to 14.3485 MHz

## Slide 21
G4D10
How close to the lower edge of a band’s phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
A. At least 3 kHz above the edge of the segment
B. At least 3 kHz below the edge of the segment
C. At least 1 kHz below the edge of the segment
D. At least 1 kHz above the edge of the segment

## Slide 22
G4D10
How close to the lower edge of a band’s phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
A. At least 3 kHz above the edge of the segment
B. At least 3 kHz below the edge of the segment
C. At least 1 kHz below the edge of the segment
D. At least 1 kHz above the edge of the segment

## Slide 23
G4D11
How close to the upper edge of a band’s phone segment should your displayed carrier frequency be when using 3 kHz wide USB?
A. At least 3 kHz above the edge of the band
B. At least 3 kHz below the edge of the band
C. At least 1 kHz above the edge of the segment
D. At least 1 kHz below the edge of the segment

## Slide 24
G4D11
How close to the upper edge of a band’s phone segment should your displayed carrier frequency be when using 3 kHz wide USB?
A. At least 3 kHz above the edge of the band
B. At least 3 kHz below the edge of the band
C. At least 1 kHz above the edge of the segment
D. At least 1 kHz below the edge of the segment