## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G4E
For use with The ARRL General Class License Manual, Tenth Edition
Mobile and portable HF stations; alternative energy source operation

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G4E01
What is the purpose of a capacitance hat on a mobile antenna?
A. To increase the power handling capacity of a whip antenna
B. To reduce radiation resistance
C. To electrically lengthen a physically short antenna
D. To lower the radiation angle

## Slide 4
G4E01
What is the purpose of a capacitance hat on a mobile antenna?
A. To increase the power handling capacity of a whip antenna
B. To reduce radiation resistance
C. To electrically lengthen a physically short antenna
D. To lower the radiation angle

## Slide 5
G4E02
What is the purpose of a corona ball on an HF mobile antenna?
A. To narrow the operating bandwidth of the antenna
B. To increase the “Q” of the antenna
C. To reduce the chance of damage if the antenna should strike an object
D. To reduce RF voltage discharge from the tip of the antenna while transmitting

## Slide 6
G4E02
What is the purpose of a corona ball on an HF mobile antenna?
A. To narrow the operating bandwidth of the antenna
B. To increase the “Q” of the antenna
C. To reduce the chance of damage if the antenna should strike an object
D. To reduce RF voltage discharge from the tip of the antenna while transmitting

## Slide 7
G4E03
Which of the following direct, fused power connections would be the best for a 100-watt HF mobile installation?
A. To the battery using heavy-gauge wire
B. To the alternator or generator using heavy-gauge wire
C. To the battery using insulated heavy duty balanced transmission line
D. To the alternator or generator using insulated heavy duty balanced transmission line

## Slide 8
G4E03
Which of the following direct, fused power connections would be the best for a 100-watt HF mobile installation?
A. To the battery using heavy-gauge wire
B. To the alternator or generator using heavy-gauge wire
C. To the battery using insulated heavy duty balanced transmission line
D. To the alternator or generator using insulated heavy duty balanced transmission line

## Slide 9
G4E04
Why should DC power for a 100-watt HF transceiver not be supplied by a vehicle’s auxiliary power socket?
A. The socket is not wired with an RF-shielded power cable
B. The socket’s wiring may be inadequate for the current drawn by the transceiver
C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
D. Drawing more than 50 watts from this socket could cause the engine to overheat

## Slide 10
G4E04
Why should DC power for a 100-watt HF transceiver not be supplied by a vehicle’s auxiliary power socket?
A. The socket is not wired with an RF-shielded power cable
B. The socket’s wiring may be inadequate for the current drawn by the transceiver
C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
D. Drawing more than 50 watts from this socket could cause the engine to overheat

## Slide 11
G4E05
Which of the following most limits an HF mobile installation?
A. “Picket fencing”
B. The wire gauge of the DC power line to the transceiver
C. Efficiency of the electrically short antenna
D. FCC rules limiting mobile output power on the 75-meter band

## Slide 12
G4E05
Which of the following most limits an HF mobile installation?
A. “Picket fencing”
B. The wire gauge of the DC power line to the transceiver
C. Efficiency of the electrically short antenna
D. FCC rules limiting mobile output power on the 75-meter band

## Slide 13
G4E06
What is one disadvantage of using a shortened mobile antenna as opposed to a full-size antenna?
A. Short antennas are more likely to cause distortion of transmitted signals
B. Q of the antenna will be very low
C. Operating bandwidth may be very limited
D. Harmonic radiation may increase

## Slide 14
G4E06
What is one disadvantage of using a shortened mobile antenna as opposed to a full-size antenna?
A. Short antennas are more likely to cause distortion of transmitted signals
B. Q of the antenna will be very low
C. Operating bandwidth may be very limited
D. Harmonic radiation may increase

## Slide 15
G4E07
Which of the following may cause receive interference to an HF transceiver installed in a vehicle?
A. The battery charging system
B. The fuel delivery system
C. The control computers
D. All these choices are correct

## Slide 16
G4E07
Which of the following may cause receive interference to an HF transceiver installed in a vehicle?
A. The battery charging system
B. The fuel delivery system
C. The control computers
D. All these choices are correct

## Slide 17
G4E08
In what configuration are the individual cells in a solar panel connected together?
A. Series-parallel
B. Shunt
C. Bypass
D. Full-wave bridge

## Slide 18
G4E08
In what configuration are the individual cells in a solar panel connected together?
A. Series-parallel
B. Shunt
C. Bypass
D. Full-wave bridge

## Slide 19
G4E09
What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
A. 0.02 VDC
B. 0.5 VDC
C. 0.2 VDC
D. 1.38 VDC

## Slide 20
G4E09
What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
A. 0.02 VDC
B. 0.5 VDC
C. 0.2 VDC
D. 1.38 VDC

## Slide 21
G4E10
Why should a series diode be connected between a solar panel and a storage battery that is being charged by the panel?
A. To prevent overload by regulating the charging voltage
B. To prevent discharge of the battery through the panel during times of low or no illumination
C. To limit the current flowing from the panel to a safe value
D. To prevent damage to the battery due to excessive voltage at high illumination levels

## Slide 22
G4E10
Why should a series diode be connected between a solar panel and a storage battery that is being charged by the panel?
A. To prevent overload by regulating the charging voltage
B. To prevent discharge of the battery through the panel during times of low or no illumination
C. To limit the current flowing from the panel to a safe value
D. To prevent damage to the battery due to excessive voltage at high illumination levels

## Slide 23
G4E11
What precaution should be taken when connecting a solar panel to a lithium iron phosphate battery?
A. Ground the solar panel outer metal framework
B. Ensure the battery is placed terminals-up
C. A series resistor must be in place
D. The solar panel must have a charge controller

## Slide 24
G4E11
What precaution should be taken when connecting a solar panel to a lithium iron phosphate battery?
A. Ground the solar panel outer metal framework
B. Ensure the battery is placed terminals-up
C. A series resistor must be in place
D. The solar panel must have a charge controller