## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G5A
For use with The ARRL General Class License Manual, Tenth Edition
Reactance; inductance; capacitance; impedance; impedance transformation; resonance

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G5A01
What happens when inductive and capacitive reactance are equal in a series LC circuit?
A. Resonance causes impedance to be very high
B. Impedance is equal to the geometric mean of the inductance and capacitance
C. Resonance causes impedance to be very low
D. Impedance is equal to the arithmetic mean of the inductance and capacitance

## Slide 4
G5A01
What happens when inductive and capacitive reactance are equal in a series LC circuit?
A. Resonance causes impedance to be very high
B. Impedance is equal to the geometric mean of the inductance and capacitance
C. Resonance causes impedance to be very low
D. Impedance is equal to the arithmetic mean of the inductance and capacitance

## Slide 5
G5A02
What is reactance?
A. Opposition to the flow of direct current caused by resistance
B. Opposition to the flow of alternating current caused by capacitance or inductance
C. Reinforcement of the flow of direct current caused by resistance
D. Reinforcement of the flow of alternating current caused by capacitance or inductance

## Slide 6
G5A02
What is reactance?
A. Opposition to the flow of direct current caused by resistance
B. Opposition to the flow of alternating current caused by capacitance or inductance
C. Reinforcement of the flow of direct current caused by resistance
D. Reinforcement of the flow of alternating current caused by capacitance or inductance

## Slide 7
G5A03
Which of the following is opposition to the flow of alternating current in an inductor?
A. Conductance
B. Reluctance
C. Admittance
D. Reactance

## Slide 8
G5A03
Which of the following is opposition to the flow of alternating current in an inductor?
A. Conductance
B. Reluctance
C. Admittance
D. Reactance

## Slide 9
G5A04
Which of the following is opposition to the flow of alternating current in a capacitor?
A. Conductance
B. Reluctance
C. Reactance
D. Admittance

## Slide 10
G5A04
Which of the following is opposition to the flow of alternating current in a capacitor?
A. Conductance
B. Reluctance
C. Reactance
D. Admittance

## Slide 11
G5A05
How does an inductor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the amplitude of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance decreases
D. As the frequency of the applied AC increases, the reactance increases

## Slide 12
G5A05
How does an inductor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the amplitude of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance decreases
D. As the frequency of the applied AC increases, the reactance increases

## Slide 13
G5A06
How does a capacitor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the frequency of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance increases
D. As the amplitude of the applied AC increases, the reactance decreases

## Slide 14
G5A06
How does a capacitor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the frequency of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance increases
D. As the amplitude of the applied AC increases, the reactance decreases

## Slide 15
G5A07
What is the term for the inverse of impedance?
A. Conductance
B. Susceptance
C. Reluctance
D. Admittance

## Slide 16
G5A07
What is the term for the inverse of impedance?
A. Conductance
B. Susceptance
C. Reluctance
D. Admittance

## Slide 17
G5A08
What is impedance?
A. The ratio of current to voltage
B. The product of current and voltage
C. The ratio of voltage to current
D. The product of current and reactance

## Slide 18
G5A08
What is impedance?
A. The ratio of current to voltage
B. The product of current and voltage
C. The ratio of voltage to current
D. The product of current and reactance

## Slide 19
G5A09
What unit is used to measure reactance?
A. Farad
B. Ohm
C. Ampere
D. Siemens

## Slide 20
G5A09
What unit is used to measure reactance?
A. Farad
B. Ohm
C. Ampere
D. Siemens

## Slide 21
G5A10
Which of the following devices can be used for impedance matching at radio frequencies?
A. A transformer
B. A Pi-network
C. A length of transmission line
D. All these choices are correct

## Slide 22
G5A10
Which of the following devices can be used for impedance matching at radio frequencies?
A. A transformer
B. A Pi-network
C. A length of transmission line
D. All these choices are correct

## Slide 23
G5A11
What letter is used to represent reactance?
A. Z
B. X
C. B
D. Y

## Slide 24
G5A11
What letter is used to represent reactance?
A. Z
B. X
C. B
D. Y

## Slide 25
G5A12
What occurs in an LC circuit at resonance?
A. Current and voltage are equal
B. Resistance is cancelled
C. The circuit radiates all its energy in the form of radio waves
D. Inductive reactance and capacitive reactance cancel

## Slide 26
G5A12
What occurs in an LC circuit at resonance?
A. Current and voltage are equal
B. Resistance is cancelled
C. The circuit radiates all its energy in the form of radio waves
D. Inductive reactance and capacitive reactance cancel