## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G5B
For use with The ARRL General Class License Manual, Tenth Edition
The decibel; current and voltage dividers; electrical power calculations; sine wave root-mean-square (RMS) values; PEP calculations

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G5B01
What dB change represents a factor of two increase or decrease in power?
A. Approximately 2 dB
B. Approximately 3 dB
C. Approximately 6 dB
D. Approximately 9 dB

## Slide 4
G5B01
What dB change represents a factor of two increase or decrease in power?
A. Approximately 2 dB
B. Approximately 3 dB
C. Approximately 6 dB
D. Approximately 9 dB

## Slide 5
G5B02
How does the total current relate to the individual currents in a circuit of parallel resistors?
A. It equals the average of the branch currents
B. It decreases as more parallel branches are added to the circuit
C. It equals the sum of the currents through each branch
D. It is the sum of the reciprocal of each individual voltage drop

## Slide 6
G5B02
How does the total current relate to the individual currents in a circuit of parallel resistors?
A. It equals the average of the branch currents
B. It decreases as more parallel branches are added to the circuit
C. It equals the sum of the currents through each branch
D. It is the sum of the reciprocal of each individual voltage drop

## Slide 7
G5B03
How many watts of electrical power are consumed if 400 VDC is supplied to an 800-ohm load?
A. 0.5 watts
B. 200 watts
C. 400 watts
D. 3200 watts

## Slide 8
G5B03
How many watts of electrical power are consumed if 400 VDC is supplied to an 800-ohm load?
A. 0.5 watts
B. 200 watts
C. 400 watts
D. 3200 watts

## Slide 9
G5B04
How many watts of electrical power are consumed by a 12 VDC light bulb that draws 0.2 amperes?
A. 2.4 watts
B. 24 watts
C. 6 watts
D. 60 watts

## Slide 10
G5B04
How many watts of electrical power are consumed by a 12 VDC light bulb that draws 0.2 amperes?
A. 2.4 watts
B. 24 watts
C. 6 watts
D. 60 watts

## Slide 11
G5B05
How many watts are consumed when a current of 7.0 milliamperes flows through a 1,250-ohm resistance?
A. Approximately 61 milliwatts
B. Approximately 61 watts
C. Approximately 11 milliwatts
D. Approximately 11 watts

## Slide 12
G5B05
How many watts are consumed when a current of 7.0 milliamperes flows through a 1,250-ohm resistance?
A. Approximately 61 milliwatts
B. Approximately 61 watts
C. Approximately 11 milliwatts
D. Approximately 11 watts

## Slide 13
G5B06
What is the PEP produced by 200 volts peak-to-peak across a 50-ohm dummy load?
A. 1.4 watts
B. 100 watts
C. 353.5 watts
D. 400 watts

## Slide 14
G5B06
What is the PEP produced by 200 volts peak-to-peak across a 50-ohm dummy load?
A. 1.4 watts
B. 100 watts
C. 353.5 watts
D. 400 watts

## Slide 15
G5B07
What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value?
A. The peak-to-peak value
B. The peak value
C. The RMS value
D. The reciprocal of the RMS value

## Slide 16
G5B07
What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value?
A. The peak-to-peak value
B. The peak value
C. The RMS value
D. The reciprocal of the RMS value

## Slide 17
G5B08
What is the peak-to-peak voltage of a sine wave with an RMS voltage of 120 volts?
A. 84.8 volts
B. 169.7 volts
C. 240.0 volts
D. 339.4 volts

## Slide 18
G5B08
What is the peak-to-peak voltage of a sine wave with an RMS voltage of 120 volts?
A. 84.8 volts
B. 169.7 volts
C. 240.0 volts
D. 339.4 volts

## Slide 19
G5B09
What is the RMS voltage of a sine wave with a value of 17 volts peak?
A. 8.5 volts
B. 12 volts
C. 24 volts
D. 34 volts

## Slide 20
G5B09
What is the RMS voltage of a sine wave with a value of 17 volts peak?
A. 8.5 volts
B. 12 volts
C. 24 volts
D. 34 volts

## Slide 21
G5B10
What percentage of power loss is equivalent to a loss of 1 dB?
A. 10.9 percent
B. 12.2 percent
C. 20.6 percent
D. 25.9 percent

## Slide 22
G5B10
What percentage of power loss is equivalent to a loss of 1 dB?
A. 10.9 percent
B. 12.2 percent
C. 20.6 percent
D. 25.9 percent

## Slide 23
G5B11
What is the ratio of PEP to average power for an unmodulated carrier?
A. 0.707
B. 1.00
C. 1.414
D. 2.00

## Slide 24
G5B11
What is the ratio of PEP to average power for an unmodulated carrier?
A. 0.707
B. 1.00
C. 1.414
D. 2.00

## Slide 25
G5B12
What is the RMS voltage across a 50-ohm dummy load dissipating 1200 watts?
A. 173 volts
B. 245 volts
C. 346 volts
D. 692 volts

## Slide 26
G5B12
What is the RMS voltage across a 50-ohm dummy load dissipating 1200 watts?
A. 173 volts
B. 245 volts
C. 346 volts
D. 692 volts

## Slide 27
G5B13
What is the output PEP of an unmodulated carrier if the average power is 1060 watts?
A. 530 watts
B. 1060 watts
C. 1500 watts
D. 2120 watts

## Slide 28
G5B13
What is the output PEP of an unmodulated carrier if the average power is 1060 watts?
A. 530 watts
B. 1060 watts
C. 1500 watts
D. 2120 watts

## Slide 29
G5B14
What is the output PEP of 500 volts peak-to-peak across a 50-ohm load?
A. 8.75 watts
B. 625 watts
C. 2500 watts
D. 5000 watts

## Slide 30
G5B14
What is the output PEP of 500 volts peak-to-peak across a 50-ohm load?
A. 8.75 watts
B. 625 watts
C. 2500 watts
D. 5000 watts