## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G5C
For use with The ARRL General Class License Manual, Tenth Edition
Resistors, capacitors, and inductors in series and parallel; transformers

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G5C01
What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding?
A. Capacitive coupling
B. Displacement current coupling
C. Mutual inductance
D. Mutual capacitance

## Slide 4
G5C01
What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding?
A. Capacitive coupling
B. Displacement current coupling
C. Mutual inductance
D. Mutual capacitance

## Slide 5
G5C02
What is the output voltage if an output signal is applied to the secondary winding of a 4:1 voltage step-down transformer instead of the primary winding?
A. The input voltage is multiplied by 4
B. The input voltage is divided by 4
C. Additional resistance must be added in series with the primary to prevent overload
D. Additional resistance must be added in parallel with the secondary to prevent overload

## Slide 6
G5C02
What is the output voltage if an output signal is applied to the secondary winding of a 4:1 voltage step-down transformer instead of the primary winding?
A. The input voltage is multiplied by 4
B. The input voltage is divided by 4
C. Additional resistance must be added in series with the primary to prevent overload
D. Additional resistance must be added in parallel with the secondary to prevent overload

## Slide 7
G5C03
What is the total resistance of a 10-, a 20-, and a 50-ohm resistor connected in parallel?
A. 5.9 ohms
B. 0.17 ohms
C. 17 ohms
D. 80 ohms

## Slide 8
G5C03
What is the total resistance of a 10-, a 20-, and a 50-ohm resistor connected in parallel?
A. 5.9 ohms
B. 0.17 ohms
C. 17 ohms
D. 80 ohms

## Slide 9
G5C04
What is the approximate total resistance of a 100- and a 200-ohm resistor in parallel?
A. 300 ohms
B. 150 ohms
C. 75 ohms
D. 67 ohms

## Slide 10
G5C04
What is the approximate total resistance of a 100- and a 200-ohm resistor in parallel?
A. 300 ohms
B. 150 ohms
C. 75 ohms
D. 67 ohms

## Slide 11
G5C05
Why is the primary winding wire of a voltage step-up transformer usually a larger size than that of the secondary winding?
A. To improve the coupling between the primary and secondary
B. To accommodate the higher current of the primary
C. To prevent parasitic oscillations due to resistive losses in the primary
D. To ensure that the volume of the primary winding is equal to the volume of the secondary winding

## Slide 12
G5C05
Why is the primary winding wire of a voltage step-up transformer usually a larger size than that of the secondary winding?
A. To improve the coupling between the primary and secondary
B. To accommodate the higher current of the primary
C. To prevent parasitic oscillations due to resistive losses in the primary
D. To ensure that the volume of the primary winding is equal to the volume of the secondary winding

## Slide 13
G5C06
What is the voltage output of a transformer with a 500-turn primary and a 1500-turn secondary when 120 VAC is applied to the primary?
A. 360 volts
B. 120 volts
C. 40 volts
D. 25.5 volts

## Slide 14
G5C06
What is the voltage output of a transformer with a 500-turn primary and a 1500-turn secondary when 120 VAC is applied to the primary?
A. 360 volts
B. 120 volts
C. 40 volts
D. 25.5 volts

## Slide 15
G5C07
What transformer turns ratio matches an antenna’s 600-ohm feed point impedance to a 50-ohm coaxial cable?
A. 3.5 to 1
B. 12 to 1
C. 24 to 1
D. 144 to 1

## Slide 16
G5C07
What transformer turns ratio matches an antenna’s 600-ohm feed point impedance to a 50-ohm coaxial cable?
A. 3.5 to 1
B. 12 to 1
C. 24 to 1
D. 144 to 1

## Slide 17
G5C08
What is the equivalent capacitance of two 5.0-nanofarad capacitors and one 750-picofarad capacitor connected in parallel?
A. 576.9 nanofarads
B. 1,733 picofarads
C. 3,583 picofarads
D. 10.750 nanofarads

## Slide 18
G5C08
What is the equivalent capacitance of two 5.0-nanofarad capacitors and one 750-picofarad capacitor connected in parallel?
A. 576.9 nanofarads
B. 1,733 picofarads
C. 3,583 picofarads
D. 10.750 nanofarads

## Slide 19
G5C09
What is the capacitance of three 100-microfarad capacitors connected in series?
A. 0.33 microfarads
B. 3.0 microfarads
C. 33.3 microfarads
D. 300 microfarads

## Slide 20
G5C09
What is the capacitance of three 100-microfarad capacitors connected in series?
A. 0.33 microfarads
B. 3.0 microfarads
C. 33.3 microfarads
D. 300 microfarads

## Slide 21
G5C10
What is the inductance of three 10-millihenry inductors connected in parallel?
A. 0.30 henries
B. 3.3 henries
C. 3.3 millihenries
D. 30 millihenries

## Slide 22
G5C10
What is the inductance of three 10-millihenry inductors connected in parallel?
A. 0.30 henries
B. 3.3 henries
C. 3.3 millihenries
D. 30 millihenries

## Slide 23
G5C11
What is the inductance of a circuit with a 20-millihenry inductor connected in series with a 50-millihenry inductor?
A. 7 millihenries
B. 14.3 millihenries
C. 70 millihenries
D. 1,000 millihenries

## Slide 24
G5C11
What is the inductance of a circuit with a 20-millihenry inductor connected in series with a 50-millihenry inductor?
A. 7 millihenries
B. 14.3 millihenries
C. 70 millihenries
D. 1,000 millihenries

## Slide 25
G5C12
What is the capacitance of a 20-microfarad capacitor connected in series with a 50-microfarad capacitor?
A. 0.07 microfarads
B. 14.3 microfarads
C. 70 microfarads
D. 1,000 microfarads

## Slide 26
G5C12
What is the capacitance of a 20-microfarad capacitor connected in series with a 50-microfarad capacitor?
A. 0.07 microfarads
B. 14.3 microfarads
C. 70 microfarads
D. 1,000 microfarads

## Slide 27
G5C13
Which of the following components should be added to a capacitor to increase the capacitance?
A. An inductor in series
B. An inductor in parallel
C. A capacitor in parallel
D. A capacitor in series

## Slide 28
G5C13
Which of the following components should be added to a capacitor to increase the capacitance?
A. An inductor in series
B. An inductor in parallel
C. A capacitor in parallel
D. A capacitor in series

## Slide 29
G5C14
Which of the following components should be added to an inductor to increase the inductance?
A. A capacitor in series
B. A capacitor in parallel
C. An inductor in parallel
D. An inductor in series

## Slide 30
G5C14
Which of the following components should be added to an inductor to increase the inductance?
A. A capacitor in series
B. A capacitor in parallel
C. An inductor in parallel
D. An inductor in series