## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G6A
For use with The ARRL General Class License Manual, Tenth Edition
Resistors; capacitors; inductors; rectifiers; solid-state diodes and transistors; vacuum tubes; batteries

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G6A01
What is the minimum allowable discharge voltage for maximum life of a standard 12-volt lead-acid battery?
A. 6 volts
B. 8.5 volts
C. 10.5 volts
D. 12 volts

## Slide 4
G6A01
What is the minimum allowable discharge voltage for maximum life of a standard 12-volt lead-acid battery?
A. 6 volts
B. 8.5 volts
C. 10.5 volts
D. 12 volts

## Slide 5
G6A02
What is an advantage of batteries with low internal resistance?
A. Long life
B. High discharge current
C. High voltage
D. Rapid recharge

## Slide 6
G6A02
What is an advantage of batteries with low internal resistance?
A. Long life
B. High discharge current
C. High voltage
D. Rapid recharge

## Slide 7
G6A03
What is the approximate forward threshold voltage of a germanium diode?
A. 0.1 volt
B. 0.3 volts
C. 0.7 volts
D. 1.0 volts

## Slide 8
G6A03
What is the approximate forward threshold voltage of a germanium diode?
A. 0.1 volt
B. 0.3 volts
C. 0.7 volts
D. 1.0 volts

## Slide 9
G6A04
Which of the following is characteristic of an electrolytic capacitor?
A. Tight tolerance
B. Much less leakage than any other type
C. High capacitance for a given volume
D. Inexpensive RF capacitor

## Slide 10
G6A04
Which of the following is characteristic of an electrolytic capacitor?
A. Tight tolerance
B. Much less leakage than any other type
C. High capacitance for a given volume
D. Inexpensive RF capacitor

## Slide 11
G6A05
What is the approximate forward threshold voltage of a silicon junction diode?
A. 0.1 volt
B. 0.3 volts
C. 0.7 volts
D. 1.0 volts

## Slide 12
G6A05
What is the approximate forward threshold voltage of a silicon junction diode?
A. 0.1 volt
B. 0.3 volts
C. 0.7 volts
D. 1.0 volts

## Slide 13
G6A06
Why should wire-wound resistors not be used in RF circuits?
A. The resistor’s tolerance value would not be adequate
B. The resistor’s inductance could make circuit performance unpredictable
C. The resistor could overheat
D. The resistor’s internal capacitance would detune the circuit

## Slide 14
G6A06
Why should wire-wound resistors not be used in RF circuits?
A. The resistor’s tolerance value would not be adequate
B. The resistor’s inductance could make circuit performance unpredictable
C. The resistor could overheat
D. The resistor’s internal capacitance would detune the circuit

## Slide 15
G6A07
What are the operating points for a bipolar transistor used as a switch?
A. Saturation and cutoff
B. The active region (between cutoff and saturation)
C. Peak and valley current points
D. Enhancement and depletion modes

## Slide 16
G6A07
What are the operating points for a bipolar transistor used as a switch?
A. Saturation and cutoff
B. The active region (between cutoff and saturation)
C. Peak and valley current points
D. Enhancement and depletion modes

## Slide 17
G6A08
Which of the following is characteristic of low voltage ceramic capacitors?
A. Tight tolerance
B. High stability
C. High capacitance for given volume
D. Comparatively low cost

## Slide 18
G6A08
Which of the following is characteristic of low voltage ceramic capacitors?
A. Tight tolerance
B. High stability
C. High capacitance for given volume
D. Comparatively low cost

## Slide 19
G6A09
Which of the following describes MOSFET construction?
A. The gate is formed by a back-biased junction
B. The gate is separated from the channel by a thin insulating layer
C. The source is separated from the drain by a thin insulating layer
D. The source is formed by depositing metal on silicon

## Slide 20
G6A09
Which of the following describes MOSFET construction?
A. The gate is formed by a back-biased junction
B. The gate is separated from the channel by a thin insulating layer
C. The source is separated from the drain by a thin insulating layer
D. The source is formed by depositing metal on silicon

## Slide 21
G6A10
Which element of a vacuum tube regulates the flow of electrons between cathode and plate?
A. Control grid
B. Suppressor grid
C. Screen grid
D. Trigger electrode

## Slide 22
G6A10
Which element of a vacuum tube regulates the flow of electrons between cathode and plate?
A. Control grid
B. Suppressor grid
C. Screen grid
D. Trigger electrode

## Slide 23
G6A11
What happens when an inductor is operated above its self-resonant frequency?
A. Its reactance increases
B. Harmonics are generated
C. It becomes capacitive
D. Catastrophic failure is likely

## Slide 24
G6A11
What happens when an inductor is operated above its self-resonant frequency?
A. Its reactance increases
B. Harmonics are generated
C. It becomes capacitive
D. Catastrophic failure is likely

## Slide 25
G6A12
What is the primary purpose of a screen grid in a vacuum tube?
A. To reduce grid-to-plate capacitance
B. To increase efficiency
C. To increase the control grid resistance
D. To decrease plate resistance

## Slide 26
G6A12
What is the primary purpose of a screen grid in a vacuum tube?
A. To reduce grid-to-plate capacitance
B. To increase efficiency
C. To increase the control grid resistance
D. To decrease plate resistance