## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G6B
For use with The ARRL General Class License Manual, Tenth Edition
Analog and digital integrated circuits (ICs); microwave ICs (MMICs); display devices; RF connectors; ferrite cores

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G6B01
What determines the performance of a ferrite core at different frequencies?
A. Its conductivity
B. Its thickness
C. The composition, or “mix,” of materials used
D. The ratio of outer diameter to inner diameter

## Slide 4
G6B01
What determines the performance of a ferrite core at different frequencies?
A. Its conductivity
B. Its thickness
C. The composition, or “mix,” of materials used
D. The ratio of outer diameter to inner diameter

## Slide 5
G6B02
What is meant by the term MMIC?
A. Multi-Mode Integrated Circuit
B. Monolithic Microwave Integrated Circuit
C. Metal Monolayer Integrated Circuit
D. Mode Modulated Integrated Circuit

## Slide 6
G6B02
What is meant by the term MMIC?
A. Multi-Mode Integrated Circuit
B. Monolithic Microwave Integrated Circuit
C. Metal Monolayer Integrated Circuit
D. Mode Modulated Integrated Circuit

## Slide 7
G6B03
Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits?
A. Low power consumption
B. High power handling capability
C. Better suited for RF amplification
D. Better suited for power supply regulation

## Slide 8
G6B03
Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits?
A. Low power consumption
B. High power handling capability
C. Better suited for RF amplification
D. Better suited for power supply regulation

## Slide 9
G6B04
What is a typical upper frequency limit for low SWR operation of 50-ohm BNC connectors?
A. 50 MHz
B. 500 MHz
C. 4 GHz
D. 40 GHz

## Slide 10
G6B04
What is a typical upper frequency limit for low SWR operation of 50-ohm BNC connectors?
A. 50 MHz
B. 500 MHz
C. 4 GHz
D. 40 GHz

## Slide 11
G6B05
What is an advantage of using a ferrite core toroidal inductor?
A. Large values of inductance may be obtained
B. The magnetic properties of the core may be optimized for a specific range of frequencies
C. Most of the magnetic field is contained in the core
D. All these choices are correct

## Slide 12
G6B05
What is an advantage of using a ferrite core toroidal inductor?
A. Large values of inductance may be obtained
B. The magnetic properties of the core may be optimized for a specific range of frequencies
C. Most of the magnetic field is contained in the core
D. All these choices are correct

## Slide 13
G6B06
What kind of device is an integrated circuit operational amplifier?
A. Digital
B. MMIC
C. Programmable Logic
D. Analog

## Slide 14
G6B06
What kind of device is an integrated circuit operational amplifier?
A. Digital
B. MMIC
C. Programmable Logic
D. Analog

## Slide 15
G6B07
Which of the following describes a type N connector?
A. A moisture-resistant RF connector useful to 10 GHz
B. A small bayonet connector used for data circuits
C. A low noise figure VHF connector
D. A nickel plated version of the PL-259

## Slide 16
G6B07
Which of the following describes a type N connector?
A. A moisture-resistant RF connector useful to 10 GHz
B. A small bayonet connector used for data circuits
C. A low noise figure VHF connector
D. A nickel plated version of the PL-259

## Slide 17
G6B08
How is an LED biased when emitting light?
A. In the tunnel-effect region
B. At the Zener voltage
C. Reverse biased
D. Forward biased

## Slide 18
G6B08
How is an LED biased when emitting light?
A. In the tunnel-effect region
B. At the Zener voltage
C. Reverse biased
D. Forward biased

## Slide 19
G6B09
How does a liquid crystal display compare to an LED display?
A. Higher contrast in high ambient lighting
B. Wider dynamic range
C. Higher power consumption
D. Shorter lifetime

## Slide 20
G6B09
How does a liquid crystal display compare to an LED display?
A. Higher contrast in high ambient lighting
B. Wider dynamic range
C. Higher power consumption
D. Shorter lifetime

## Slide 21
G6B10
How does a ferrite bead or core reduce common-mode RF current on the shield of a coaxial cable?
A. By creating an impedance in the current’s path
B. It converts common-mode current to differential mode current
C. By creating an out-of-phase current to cancel the common-mode current
D. Ferrites expel magnetic fields

## Slide 22
G6B10
How does a ferrite bead or core reduce common-mode RF current on the shield of a coaxial cable?
A. By creating an impedance in the current’s path
B. It converts common-mode current to differential mode current
C. By creating an out-of-phase current to cancel the common-mode current
D. Ferrites expel magnetic fields

## Slide 23
G6B11
What is an SMA connector?
A. A type-S to type-M adaptor
B. A small threaded connector suitable for signals up to several GHz
C. A connector designed for serial multiple access signals
D. A type of push-on connector intended for high-voltage applications

## Slide 24
G6B11
What is an SMA connector?
A. A type-S to type-M adaptor
B. A small threaded connector suitable for signals up to several GHz
C. A connector designed for serial multiple access signals
D. A type of push-on connector intended for high-voltage applications

## Slide 25
G6B12
Which of these connector types is commonly used for low frequency or dc signal connections to a transceiver?
A. PL-259
B. BNC
C. RCA Phono
D. Type N

## Slide 26
G6B12
Which of these connector types is commonly used for low frequency or dc signal connections to a transceiver?
A. PL-259
B. BNC
C. RCA Phono
D. Type N