## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G7C
For use with The ARRL General Class License Manual, Tenth Edition
Transceiver design; filters; oscillators; digital signal processing (DSP)

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G7C01
What circuit is used to select one of the sidebands from a balanced modulator?
A. Carrier oscillator
B. Filter
C. IF amplifier
D. RF amplifier

## Slide 4
G7C01
What circuit is used to select one of the sidebands from a balanced modulator?
A. Carrier oscillator
B. Filter
C. IF amplifier
D. RF amplifier

## Slide 5
G7C02
What output is produced by a balanced modulator?
A. Frequency modulated RF
B. Audio with equalized frequency response
C. Audio extracted from the modulation signal
D. Double-sideband modulated RF

## Slide 6
G7C02
What output is produced by a balanced modulator?
A. Frequency modulated RF
B. Audio with equalized frequency response
C. Audio extracted from the modulation signal
D. Double-sideband modulated RF

## Slide 7
G7C03
What is one reason to use an impedance matching transformer at a transmitter output?
A. To minimize transmitter power output
B. To present the desired impedance to the transmitter and feed line
C. To reduce power supply ripple
D. To minimize radiation resistance

## Slide 8
G7C03
What is one reason to use an impedance matching transformer at a transmitter output?
A. To minimize transmitter power output
B. To present the desired impedance to the transmitter and feed line
C. To reduce power supply ripple
D. To minimize radiation resistance

## Slide 9
G7C04
How is a product detector used?
A. Used in test gear to detect spurious mixing products
B. Used in transmitter to perform frequency multiplication
C. Used in an FM receiver to filter out unwanted sidebands
D. Used in a single sideband receiver to extract the modulated signal

## Slide 10
G7C04
How is a product detector used?
A. Used in test gear to detect spurious mixing products
B. Used in transmitter to perform frequency multiplication
C. Used in an FM receiver to filter out unwanted sidebands
D. Used in a single sideband receiver to extract the modulated signal

## Slide 11
G7C05
Which of the following is characteristic of a direct digital synthesizer (DDS)?
A. Extremely narrow tuning range
B. Relatively high-power output
C. Pure sine wave output
D. Variable output frequency with the stability of a crystal oscillator

## Slide 12
G7C05
Which of the following is characteristic of a direct digital synthesizer (DDS)?
A. Extremely narrow tuning range
B. Relatively high-power output
C. Pure sine wave output
D. Variable output frequency with the stability of a crystal oscillator

## Slide 13
G7C06
Which of the following is an advantage of a digital signal processing (DSP) filter compared to an analog filter?
A. A wide range of filter bandwidths and shapes can be created
B. Fewer digital components are required
C. Mixing products are greatly reduced
D. The DSP filter is much more effective at VHF frequencies

## Slide 14
G7C06
Which of the following is an advantage of a digital signal processing (DSP) filter compared to an analog filter?
A. A wide range of filter bandwidths and shapes can be created
B. Fewer digital components are required
C. Mixing products are greatly reduced
D. The DSP filter is much more effective at VHF frequencies

## Slide 15
G7C07
What term specifies a filter’s attenuation inside its passband?
A. Insertion loss
B. Return loss
C. Q
D. Ultimate rejection

## Slide 16
G7C07
What term specifies a filter’s attenuation inside its passband?
A. Insertion loss
B. Return loss
C. Q
D. Ultimate rejection

## Slide 17
G7C08
Which parameter affects receiver sensitivity?
A. Input amplifier gain
B. Demodulator stage bandwidth
C. Input amplifier noise figure
D. All these choices are correct

## Slide 18
G7C08
Which parameter affects receiver sensitivity?
A. Input amplifier gain
B. Demodulator stage bandwidth
C. Input amplifier noise figure
D. All these choices are correct

## Slide 19
G7C09
What is the phase difference between the I and Q RF signals that software-defined radio (SDR) equipment uses for modulation and demodulation?
A. Zero
B. 90 degrees
C. 180 degrees
D. 45 degrees

## Slide 20
G7C09
What is the phase difference between the I and Q RF signals that software-defined radio (SDR) equipment uses for modulation and demodulation?
A. Zero
B. 90 degrees
C. 180 degrees
D. 45 degrees

## Slide 21
G7C10
What is an advantage of using I-Q modulation with software-defined radios (SDRs)?
A. The need for high resolution analog-to-digital converters is eliminated
B. All types of modulation can be created with appropriate processing
C. Minimum detectible signal level is reduced
D Automatic conversion of the signal from digital to analog

## Slide 22
G7C10
What is an advantage of using I-Q modulation with software-defined radios (SDRs)?
A. The need for high resolution analog-to-digital converters is eliminated
B. All types of modulation can be created with appropriate processing
C. Minimum detectible signal level is reduced
D Automatic conversion of the signal from digital to analog

## Slide 23
G7C11
Which of these functions is performed by software in a software-defined radio (SDR)?
A. Filtering
B. Detection
C. Modulation
D. All these choices are correct

## Slide 24
G7C11
Which of these functions is performed by software in a software-defined radio (SDR)?
A. Filtering
B. Detection
C. Modulation
D. All these choices are correct

## Slide 25
G7C12
What is the frequency above which a low-pass filter’s output power is less than half the input power?
A. Notch frequency
B. Neper frequency
C. Cutoff frequency
D. Rolloff frequency

## Slide 26
G7C12
What is the frequency above which a low-pass filter’s output power is less than half the input power?
A. Notch frequency
B. Neper frequency
C. Cutoff frequency
D. Rolloff frequency

## Slide 27
G7C13
What term specifies a filter’s maximum ability to reject signals outside its passband?
A. Notch depth
B. Rolloff
C. Insertion loss
D. Ultimate rejection

## Slide 28
G7C13
What term specifies a filter’s maximum ability to reject signals outside its passband?
A. Notch depth
B. Rolloff
C. Insertion loss
D. Ultimate rejection

## Slide 29
G7C14
The bandwidth of a band-pass filter is measured between what two frequencies?
A. Upper and lower half-power
B. Cutoff and rolloff
C. Pole and zero
D. Image and harmonic

## Slide 30
G7C14
The bandwidth of a band-pass filter is measured between what two frequencies?
A. Upper and lower half-power
B. Cutoff and rolloff
C. Pole and zero
D. Image and harmonic