## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G8A
For use with The ARRL General Class License Manual, Tenth Edition
Carriers and modulation: AM, FM, and single sideband; modulation envelope; digital modulation; overmodulation; link budgets and link margins

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G8A01
How is direct binary FSK modulation generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator’s frequency directly with a digital control signal
C. By using a transceiver’s computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator

## Slide 4
G8A01
How is direct binary FSK modulation generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator’s frequency directly with a digital control signal
C. By using a transceiver’s computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator

## Slide 5
G8A02
What is the name of the process that changes the phase angle of an RF signal to convey information?
A. Phase convolution
B. Phase modulation
C. Phase transformation
D. Phase inversion

## Slide 6
G8A02
What is the name of the process that changes the phase angle of an RF signal to convey information?
A. Phase convolution
B. Phase modulation
C. Phase transformation
D. Phase inversion

## Slide 7
G8A03
What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
A. Frequency convolution
B. Frequency transformation
C. Frequency conversion
D. Frequency modulation

## Slide 8
G8A03
What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
A. Frequency convolution
B. Frequency transformation
C. Frequency conversion
D. Frequency modulation

## Slide 9
G8A04
What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
A. Multiplex modulation
B. Phase modulation
C. Amplitude modulation
D. Pulse modulation

## Slide 10
G8A04
What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
A. Multiplex modulation
B. Phase modulation
C. Amplitude modulation
D. Pulse modulation

## Slide 11
G8A05
What type of modulation varies the instantaneous power level of the RF signal?
A. Power modulation
B. Phase modulation
C. Frequency modulation
D. Amplitude modulation

## Slide 12
G8A05
What type of modulation varies the instantaneous power level of the RF signal?
A. Power modulation
B. Phase modulation
C. Frequency modulation
D. Amplitude modulation

## Slide 13
G8A06
Which of the following is characteristic of QPSK31?
A. It is sideband sensitive
B. Its encoding provides error correction
C. Its bandwidth is approximately the same as BPSK31
D. All these choices are correct

## Slide 14
G8A06
Which of the following is characteristic of QPSK31?
A. It is sideband sensitive
B. Its encoding provides error correction
C. Its bandwidth is approximately the same as BPSK31
D. All these choices are correct

## Slide 15
G8A07
Which of the following phone emissions uses the narrowest bandwidth?
A. Single sideband
B. Vestigial sideband
C. Phase modulation
D. Frequency modulation

## Slide 16
G8A07
Which of the following phone emissions uses the narrowest bandwidth?
A. Single sideband
B. Vestigial sideband
C. Phase modulation
D. Frequency modulation

## Slide 17
G8A08
Which of the following is an effect of overmodulation?
A. Insufficient audio
B. Insufficient bandwidth
C. Frequency drift
D. Excessive bandwidth

## Slide 18
G8A08
Which of the following is an effect of overmodulation?
A. Insufficient audio
B. Insufficient bandwidth
C. Frequency drift
D. Excessive bandwidth

## Slide 19
G8A09
What type of modulation is used by FT8?
A. 8-tone frequency shift keying
B. Vestigial sideband
C. Amplitude compressed AM
D. 8-bit direct sequence spread spectrum

## Slide 20
G8A09
What type of modulation is used by FT8?
A. 8-tone frequency shift keying
B. Vestigial sideband
C. Amplitude compressed AM
D. 8-bit direct sequence spread spectrum

## Slide 21
G8A10
What is meant by the term “flat-topping,” when referring to an amplitude-modulated phone signal?
A. Signal distortion caused by insufficient collector current
B. The transmitter’s automatic level control (ALC) is properly adjusted
C. Signal distortion caused by excessive drive or speech levels
D. The transmitter’s carrier is properly suppressed

## Slide 22
G8A10
What is meant by the term “flat-topping,” when referring to an amplitude-modulated phone signal?
A. Signal distortion caused by insufficient collector current
B. The transmitter’s automatic level control (ALC) is properly adjusted
C. Signal distortion caused by excessive drive or speech levels
D. The transmitter’s carrier is properly suppressed

## Slide 23
G8A11
What is the modulation envelope of an AM signal?
A. The waveform created by connecting the peak values of the modulated signal
B. The carrier frequency that contains the signal
C. Spurious signals that envelop nearby frequencies
D. The bandwidth of the modulated signal

## Slide 24
G8A11
What is the modulation envelope of an AM signal?
A. The waveform created by connecting the peak values of the modulated signal
B. The carrier frequency that contains the signal
C. Spurious signals that envelop nearby frequencies
D. The bandwidth of the modulated signal

## Slide 25
G8A12
What is QPSK modulation?
A. Modulation using quasi-parallel to serial conversion to reduce bandwidth
B. Modulation using quadra-pole sideband keying to generate spread spectrum signals
C. Modulation using Fast Fourier Transforms to generate frequencies at the first, second, third, and fourth harmonics of the carrier frequency to improve noise immunity
D. Modulation in which digital data is transmitted using 0-, 90-, 180- and 270-degrees phase shift to represent pairs of bits

## Slide 26
G8A12
What is QPSK modulation?
A. Modulation using quasi-parallel to serial conversion to reduce bandwidth
B. Modulation using quadra-pole sideband keying to generate spread spectrum signals
C. Modulation using Fast Fourier Transforms to generate frequencies at the first, second, third, and fourth harmonics of the carrier frequency to improve noise immunity
D. Modulation in which digital data is transmitted using 0-, 90-, 180- and 270-degrees phase shift to represent pairs of bits

## Slide 27
G8A13
What is a link budget?
A. The financial costs associated with operating a radio link
B. The sum of antenna gains minus system losses
C. The sum of transmit power and antenna gains minus system losses as seen at the receiver
D. The difference between transmit power and receiver sensitivity

## Slide 28
G8A13
What is a link budget?
A. The financial costs associated with operating a radio link
B. The sum of antenna gains minus system losses
C. The sum of transmit power and antenna gains minus system losses as seen at the receiver
D. The difference between transmit power and receiver sensitivity

## Slide 29
G8A14
What is link margin?
A. The opposite of fade margin
B. The difference between received power level and minimum required signal level at the input to the receiver
C. Transmit power minus receiver sensitivity
D. Receiver sensitivity plus 3 dB

## Slide 30
G8A14
What is link margin?
A. The opposite of fade margin
B. The difference between received power level and minimum required signal level at the input to the receiver
C. Transmit power minus receiver sensitivity
D. Receiver sensitivity plus 3 dB