## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G8B
For use with The ARRL General Class License Manual, Tenth Edition
Frequency changing; bandwidths of various modes; deviation; intermodulation

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G8B01
Which mixer input is varied or tuned to convert signals of different frequencies to an intermediate frequency (IF)?
A. Image frequency
B. Local oscillator
C. RF input
D. Beat frequency oscillator

## Slide 4
G8B01
Which mixer input is varied or tuned to convert signals of different frequencies to an intermediate frequency (IF)?
A. Image frequency
B. Local oscillator
C. RF input
D. Beat frequency oscillator

## Slide 5
G8B02
What is the term for interference from a signal at twice the IF frequency from the desired signal?
A. Quadrature response
B. Image response
C. Mixer interference
D. Intermediate interference

## Slide 6
G8B02
What is the term for interference from a signal at twice the IF frequency from the desired signal?
A. Quadrature response
B. Image response
C. Mixer interference
D. Intermediate interference

## Slide 7
G8B03
What is another term for the mixing of two RF signals?
A. Heterodyning
B. Synthesizing
C. Frequency inversion
D. Phase inversion

## Slide 8
G8B03
What is another term for the mixing of two RF signals?
A. Heterodyning
B. Synthesizing
C. Frequency inversion
D. Phase inversion

## Slide 9
G8B04
What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
A. Mixer
B. Reactance modulator
C. Balanced converter
D. Multiplier

## Slide 10
G8B04
What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
A. Mixer
B. Reactance modulator
C. Balanced converter
D. Multiplier

## Slide 11
G8B05
Which intermodulation products are closest to the original signal frequencies?
A. Second harmonics
B. Even-order
C. Odd-order
D. Intercept point

## Slide 12
G8B05
Which intermodulation products are closest to the original signal frequencies?
A. Second harmonics
B. Even-order
C. Odd-order
D. Intercept point

## Slide 13
G8B06
What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
A. 3 kHz
B. 5 kHz
C. 8 kHz
D. 16 kHz

## Slide 14
G8B06
What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
A. 3 kHz
B. 5 kHz
C. 8 kHz
D. 16 kHz

## Slide 15
G8B07
What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
A. 101.75 Hz
B. 416.7 Hz
C. 5 kHz
D. 60 kHz

## Slide 16
G8B07
What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
A. 101.75 Hz
B. 416.7 Hz
C. 5 kHz
D. 60 kHz

## Slide 17
G8B08
Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles that could exceed the transmitter’s average power rating
C. To allow time for the other station to break in during a transmission
D. To prevent overmodulation

## Slide 18
G8B08
Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles that could exceed the transmitter’s average power rating
C. To allow time for the other station to break in during a transmission
D. To prevent overmodulation

## Slide 19
G8B09
Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
A. It is required by FCC rules
B. It minimizes power consumption in the receiver
C. It improves impedance matching of the antenna
D. It results in the best signal-to-noise ratio

## Slide 20
G8B09
Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
A. It is required by FCC rules
B. It minimizes power consumption in the receiver
C. It improves impedance matching of the antenna
D. It results in the best signal-to-noise ratio

## Slide 21
G8B10
What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is half the symbol rate

## Slide 22
G8B10
What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is half the symbol rate

## Slide 23
G8B11
What combination of a mixer’s Local Oscillator (LO) and RF input frequencies is found in the output?
A. The ratio
B. The average
C. The sum and difference
D. The arithmetic product

## Slide 24
G8B11
What combination of a mixer’s Local Oscillator (LO) and RF input frequencies is found in the output?
A. The ratio
B. The average
C. The sum and difference
D. The arithmetic product

## Slide 25
G8B12
What process combines two signals in a non-linear circuit to produce unwanted spurious outputs?
A. Intermodulation
B. Heterodyning
C. Detection
D. Rolloff

## Slide 26
G8B12
What process combines two signals in a non-linear circuit to produce unwanted spurious outputs?
A. Intermodulation
B. Heterodyning
C. Detection
D. Rolloff

## Slide 27
G8B13
Which of the following is an odd-order intermodulation product of frequencies F1 and F2?
A. 5F1-3F2
B. 3F1-F2
C. 2F1-F2
D. All these choices are correct

## Slide 28
G8B13
Which of the following is an odd-order intermodulation product of frequencies F1 and F2?
A. 5F1-3F2
B. 3F1-F2
C. 2F1-F2
D. All these choices are correct