## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G8C
For use with The ARRL General Class License Manual, Tenth Edition
Digital emission modes

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G8C01
On what band do amateurs share channels with the unlicensed Wi-Fi service?
A. 432 MHz
B. 902 MHz
C. 2.4 GHz
D. 10.7 GHz

## Slide 4
G8C01
On what band do amateurs share channels with the unlicensed Wi-Fi service?
A. 432 MHz
B. 902 MHz
C. 2.4 GHz
D. 10.7 GHz

## Slide 5
G8C02
Which digital mode is used as a low-power beacon for assessing HF propagation?
A. WSPR
B. MFSK16
C. PSK31
D. SSB-SC

## Slide 6
G8C02
Which digital mode is used as a low-power beacon for assessing HF propagation?
A. WSPR
B. MFSK16
C. PSK31
D. SSB-SC

## Slide 7
G8C03
What part of a packet radio frame contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Trailer

## Slide 8
G8C03
What part of a packet radio frame contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Trailer

## Slide 9
G8C04
Which of the following describes Baudot code?
A. A 7-bit code with start, stop, and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN

## Slide 10
G8C04
Which of the following describes Baudot code?
A. A 7-bit code with start, stop, and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN

## Slide 11
G8C05
In an ARQ mode, what is meant by a NAK response to a transmitted packet?
A. Request retransmission of the packet
B. Packet was received without error
C. Receiving station connected and ready for transmissions
D. Entire file received correctly

## Slide 12
G8C05
In an ARQ mode, what is meant by a NAK response to a transmitted packet?
A. Request retransmission of the packet
B. Packet was received without error
C. Receiving station connected and ready for transmissions
D. Entire file received correctly

## Slide 13
G8C06
What action results from a failure to exchange information due to excessive transmission attempts when using an ARQ mode?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set

## Slide 14
G8C06
What action results from a failure to exchange information due to excessive transmission attempts when using an ARQ mode?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set

## Slide 15
G8C07
Which of the following narrow-band digital modes can receive signals with very low signal-to-noise ratios?
A. MSK144
B. FT8
C. AMTOR
D. MFSK32

## Slide 16
G8C07
Which of the following narrow-band digital modes can receive signals with very low signal-to-noise ratios?
A. MSK144
B. FT8
C. AMTOR
D. MFSK32

## Slide 17
G8C08
Which of the following statements is true about PSK31?
A. Upper case letters are sent with more power
B. Upper case letters use longer Varicode bit sequences and thus slow down transmission
C. Error correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates

## Slide 18
G8C08
Which of the following statements is true about PSK31?
A. Upper case letters are sent with more power
B. Upper case letters use longer Varicode bit sequences and thus slow down transmission
C. Error correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates

## Slide 19
G8C09
Which is true of mesh network microwave nodes?
A. Having more nodes increases signal strengths
B. If one node fails, a packet may still reach its target station via an alternate node
C. Links between two nodes in a network may have different frequencies and bandwidths
D. More nodes reduce overall microwave out of band interference

## Slide 20
G8C09
Which is true of mesh network microwave nodes?
A. Having more nodes increases signal strengths
B. If one node fails, a packet may still reach its target station via an alternate node
C. Links between two nodes in a network may have different frequencies and bandwidths
D. More nodes reduce overall microwave out of band interference

## Slide 21
G8C10
How does forward error correction (FEC) allow the receiver to correct data errors?
A. By controlling transmitter output power for optimum signal strength
B. By using the Varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character

## Slide 22
G8C10
How does forward error correction (FEC) allow the receiver to correct data errors?
A. By controlling transmitter output power for optimum signal strength
B. By using the Varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character

## Slide 23
G8C11
How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
A. Dot and dash
B. On and off
C. High and low
D. Mark and space

## Slide 24
G8C11
How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
A. Dot and dash
B. On and off
C. High and low
D. Mark and space

## Slide 25
G8C12
Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary

## Slide 26
G8C12
Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary

## Slide 27
G8C13
What is indicated on a waterfall display by one or more vertical lines on either side of a data mode or RTTY signal?
A. Long path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation

## Slide 28
G8C13
What is indicated on a waterfall display by one or more vertical lines on either side of a data mode or RTTY signal?
A. Long path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation

## Slide 29
G8C14
Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity

## Slide 30
G8C14
Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity

## Slide 31
G8C15
What does an FT8 signal report of +3 mean?
A. The signal is 3 times the noise level of an equivalent SSB signal
B. The signal is S3 (weak signals)
C. The signal-to-noise ratio is equivalent to +3dB in a 2.5 kHz bandwidth
D. The signal is 3 dB over S9

## Slide 32
G8C15
What does an FT8 signal report of +3 mean?
A. The signal is 3 times the noise level of an equivalent SSB signal
B. The signal is S3 (weak signals)
C. The signal-to-noise ratio is equivalent to +3dB in a 2.5 kHz bandwidth
D. The signal is 3 dB over S9

## Slide 33
G8C16
Which of the following provide digital voice modes?
A. WSPR, MFSK16, and EasyPAL
B. FT8, FT4, and FST4
C. Winlink, PACTOR II, and PACTOR III
D. DMR, D-STAR, and SystemFusion

## Slide 34
G8C16
Which of the following provide digital voice modes?
A. WSPR, MFSK16, and EasyPAL
B. FT8, FT4, and FST4
C. Winlink, PACTOR II, and PACTOR III
D. DMR, D-STAR, and SystemFusion