## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G9A
For use with The ARRL General Class License Manual, Tenth Edition
Feed lines: characteristic impedance and attenuation; standing wave ratio (SWR) calculation, measurement, and effects; antenna feed point matching

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G9A01
Which of the following factors determine the characteristic impedance of a parallel conductor feed line?
A. The distance between the centers of the conductors and the radius of the conductors
B. The distance between the centers of the conductors and the length of the line
C. The radius of the conductors and the frequency of the signal
D. The frequency of the signal and the length of the line

## Slide 4
G9A01
Which of the following factors determine the characteristic impedance of a parallel conductor feed line?
A. The distance between the centers of the conductors and the radius of the conductors
B. The distance between the centers of the conductors and the length of the line
C. The radius of the conductors and the frequency of the signal
D. The frequency of the signal and the length of the line

## Slide 5
G9A02
What is the relationship between high standing wave ratio (SWR) and transmission line loss?
A. There is no relationship between transmission line loss and SWR
B. High SWR increases loss in a lossy transmission line
C. High SWR makes it difficult to measure transmission line loss
D. High SWR reduces the relative effect of transmission line loss

## Slide 6
G9A02
What is the relationship between high standing wave ratio (SWR) and transmission line loss?
A. There is no relationship between transmission line loss and SWR
B. High SWR increases loss in a lossy transmission line
C. High SWR makes it difficult to measure transmission line loss
D. High SWR reduces the relative effect of transmission line loss

## Slide 7
G9A03
What is the nominal characteristic impedance of “window line” transmission line?
A. 50 ohms
B. 75 ohms
C. 100 ohms
D. 450 ohms

## Slide 8
G9A03
What is the nominal characteristic impedance of “window line” transmission line?
A. 50 ohms
B. 75 ohms
C. 100 ohms
D. 450 ohms

## Slide 9
G9A04
What causes reflected power at an antenna’s feed point?
A. Operating an antenna at its resonant frequency
B. Using more transmitter power than the antenna can handle
C. A difference between feed line impedance and antenna feed point impedance
D. Feeding the antenna with unbalanced feed line

## Slide 10
G9A04
What causes reflected power at an antenna’s feed point?
A. Operating an antenna at its resonant frequency
B. Using more transmitter power than the antenna can handle
C. A difference between feed line impedance and antenna feed point impedance
D. Feeding the antenna with unbalanced feed line

## Slide 11
G9A05
How does the attenuation of coaxial cable change with increasing frequency?
A. Attenuation is independent of frequency
B. Attenuation increases
C. Attenuation decreases
D. Attenuation follows Marconi’s Law of Attenuation

## Slide 12
G9A05
How does the attenuation of coaxial cable change with increasing frequency?
A. Attenuation is independent of frequency
B. Attenuation increases
C. Attenuation decreases
D. Attenuation follows Marconi’s Law of Attenuation

## Slide 13
G9A06
In what units is RF feed line loss usually expressed?
A. Ohms per 1,000 feet
B. Decibels per 1,000 feet
C. Ohms per 100 feet
D. Decibels per 100 feet

## Slide 14
G9A06
In what units is RF feed line loss usually expressed?
A. Ohms per 1,000 feet
B. Decibels per 1,000 feet
C. Ohms per 100 feet
D. Decibels per 100 feet

## Slide 15
G9A07
What must be done to prevent standing waves on a feed line connected to an antenna?
A. The antenna feed point must be at DC ground potential
B. The feed line must be an odd number of electrical quarter wavelengths long
C. The feed line must be an even number of physical half wavelengths long
D. The antenna feed point impedance must be matched to the characteristic impedance of the feed line

## Slide 16
G9A07
What must be done to prevent standing waves on a feed line connected to an antenna?
A. The antenna feed point must be at DC ground potential
B. The feed line must be an odd number of electrical quarter wavelengths long
C. The feed line must be an even number of physical half wavelengths long
D. The antenna feed point impedance must be matched to the characteristic impedance of the feed line

## Slide 17
G9A08
If the SWR on an antenna feed line is 5:1, and a matching network at the transmitter end of the feed line is adjusted to present a 1:1 SWR to the transmitter, what is the resulting SWR on the feed line?
A. 1:1
B. 5:1
C. Between 1:1 and 5:1 depending on the characteristic impedance of the line
D. Between 1:1 and 5:1 depending on the reflected power at the transmitter

## Slide 18
G9A08
If the SWR on an antenna feed line is 5:1, and a matching network at the transmitter end of the feed line is adjusted to present a 1:1 SWR to the transmitter, what is the resulting SWR on the feed line?
A. 1:1
B. 5:1
C. Between 1:1 and 5:1 depending on the characteristic impedance of the line
D. Between 1:1 and 5:1 depending on the reflected power at the transmitter

## Slide 19
G9A09
What standing wave ratio results from connecting a 50-ohm feed line to a 200-ohm resistive load?
A. 4:1
B. 1:4
C. 2:1
D. 1:2

## Slide 20
G9A09
What standing wave ratio results from connecting a 50-ohm feed line to a 200-ohm resistive load?
A. 4:1
B. 1:4
C. 2:1
D. 1:2

## Slide 21
G9A10
What standing wave ratio results from connecting a 50-ohm feed line to a 10-ohm resistive load?
A. 2:1
B. 1:2
C. 1:5
D. 5:1

## Slide 22
G9A10
What standing wave ratio results from connecting a 50-ohm feed line to a 10-ohm resistive load?
A. 2:1
B. 1:2
C. 1:5
D. 5:1

## Slide 23
G9A11
What is the effect of transmission line loss on SWR measured at the input to the line?
A. Higher loss reduces SWR measured at the input to the line
B. Higher loss increases SWR measured at the input to the line
C. Higher loss increases the accuracy of SWR measured at the input to the line
D. Transmission line loss does not affect the SWR measurement

## Slide 24
G9A11
What is the effect of transmission line loss on SWR measured at the input to the line?
A. Higher loss reduces SWR measured at the input to the line
B. Higher loss increases SWR measured at the input to the line
C. Higher loss increases the accuracy of SWR measured at the input to the line
D. Transmission line loss does not affect the SWR measurement