## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G9B
For use with The ARRL General Class License Manual, Tenth Edition
Basic dipole and monopole antennas

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G9B01
What is a characteristic of a random-wire HF antenna connected directly to the transmitter?
A. It must be longer than 1 wavelength
B. Station equipment may carry significant RF current
C. It produces only vertically polarized radiation
D. It is more effective on the lower HF bands than on the higher bands

## Slide 4
G9B01
What is a characteristic of a random-wire HF antenna connected directly to the transmitter?
A. It must be longer than 1 wavelength
B. Station equipment may carry significant RF current
C. It produces only vertically polarized radiation
D. It is more effective on the lower HF bands than on the higher bands

## Slide 5
G9B02
Which of the following is a common way to adjust the feed point impedance of an elevated quarter-wave ground-plane vertical antenna to be approximately 50 ohms?
A. Slope the radials upward
B. Slope the radials downward
C. Lengthen the radials beyond one wavelength
D. Coil the radials

## Slide 6
G9B02
Which of the following is a common way to adjust the feed point impedance of an elevated quarter-wave ground-plane vertical antenna to be approximately 50 ohms?
A. Slope the radials upward
B. Slope the radials downward
C. Lengthen the radials beyond one wavelength
D. Coil the radials

## Slide 7
G9B03
Which of the following best describes the radiation pattern of a quarter-wave ground-plane vertical antenna?
A. Bi-directional in azimuth
B. Isotropic
C. Hemispherical
D. Omnidirectional in azimuth

## Slide 8
G9B03
Which of the following best describes the radiation pattern of a quarter-wave ground-plane vertical antenna?
A. Bi-directional in azimuth
B. Isotropic
C. Hemispherical
D. Omnidirectional in azimuth

## Slide 9
G9B04
What is the radiation pattern of a dipole antenna in free space in a plane containing the conductor?
A. It is a figure-eight at right angles to the antenna
B. It is a figure-eight off both ends of the antenna
C. It is a circle (equal radiation in all directions)
D. It has a pair of lobes on one side of the antenna and a single lobe on the other side

## Slide 10
G9B04
What is the radiation pattern of a dipole antenna in free space in a plane containing the conductor?
A. It is a figure-eight at right angles to the antenna
B. It is a figure-eight off both ends of the antenna
C. It is a circle (equal radiation in all directions)
D. It has a pair of lobes on one side of the antenna and a single lobe on the other side

## Slide 11
G9B05
How does antenna height affect the azimuthal radiation pattern of a horizontal dipole HF antenna?
A. If the antenna is too high, the pattern becomes unpredictable
B. Antenna height has no effect on the pattern
C. If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional
D. If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated

## Slide 12
G9B05
How does antenna height affect the azimuthal radiation pattern of a horizontal dipole HF antenna?
A. If the antenna is too high, the pattern becomes unpredictable
B. Antenna height has no effect on the pattern
C. If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional
D. If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated

## Slide 13
G9B06
Where should the radial wires of a ground-mounted vertical antenna system be placed?
A. As high as possible above the ground
B. Parallel to the antenna element
C. On the surface or buried a few inches below the ground
D. At the center of the antenna

## Slide 14
G9B06
Where should the radial wires of a ground-mounted vertical antenna system be placed?
A. As high as possible above the ground
B. Parallel to the antenna element
C. On the surface or buried a few inches below the ground
D. At the center of the antenna

## Slide 15
G9B07
How does the feed point impedance of a horizontal 1/2 wave dipole antenna change as the antenna height is reduced to 1/10 wavelength above ground?
A. It steadily increases
B. It steadily decreases
C. It peaks at about 1/8 wavelength above ground
D. It is unaffected by the height above ground

## Slide 16
G9B07
How does the feed point impedance of a horizontal 1/2 wave dipole antenna change as the antenna height is reduced to 1/10 wavelength above ground?
A. It steadily increases
B. It steadily decreases
C. It peaks at about 1/8 wavelength above ground
D. It is unaffected by the height above ground

## Slide 17
G9B08
How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends?
A. It steadily increases
B. It steadily decreases
C. It peaks at about 1/8 wavelength from the end
D. It is unaffected by the location of the feed point

## Slide 18
G9B08
How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends?
A. It steadily increases
B. It steadily decreases
C. It peaks at about 1/8 wavelength from the end
D. It is unaffected by the location of the feed point

## Slide 19
G9B09
Which of the following is an advantage of using a horizontally polarized as compared to a vertically polarized HF antenna?
A. Lower ground losses
B. Lower feed point impedance
C. Shorter radials
D. Lower radiation resistance

## Slide 20
G9B09
Which of the following is an advantage of using a horizontally polarized as compared to a vertically polarized HF antenna?
A. Lower ground losses
B. Lower feed point impedance
C. Shorter radials
D. Lower radiation resistance

## Slide 21
G9B10
What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz?
A. 8 feet
B. 16 feet
C. 24 feet
D. 33 feet

## Slide 22
G9B10
What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz?
A. 8 feet
B. 16 feet
C. 24 feet
D. 33 feet

## Slide 23
G9B11
What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz?
A. 42 feet
B. 84 feet
C. 132 feet
D. 263 feet

## Slide 24
G9B11
What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz?
A. 42 feet
B. 84 feet
C. 132 feet
D. 263 feet

## Slide 25
G9B12
What is the approximate length for a 1/4 wave monopole antenna cut for 28.5 MHz?
A. 8 feet
B. 11 feet
C. 16 feet
D. 21 feet

## Slide 26
G9B12
What is the approximate length for a 1/4 wave monopole antenna cut for 28.5 MHz?
A. 8 feet
B. 11 feet
C. 16 feet
D. 21 feet