## Slide 1
The ARRL General Class License Course
All You Need to Pass Your General Class Exam
Level 2: General – G9D
For use with The ARRL General Class License Manual, Tenth Edition
Specialized antenna types and applications

## Slide 2
General Class License Manual and other resources
Level 2: General
http://www.arrl.org/shop/Licensing-Education-and-Training/

## Slide 3
G9D01
Which of the following antenna types will be most effective as a near vertical incidence skywave (NVIS) antenna for short-skip communications on 40 meters during the day?
A. A horizontal dipole placed between 1/10 and 1/4 wavelength above the ground
B. A vertical antenna placed between 1/4 and 1/2 wavelength above the ground
C. horizontal dipole placed at approximately 1/2 wavelength above the ground
D. A vertical dipole placed at approximately 1/2 wavelength above the ground

## Slide 4
G9D01
Which of the following antenna types will be most effective as a near vertical incidence skywave (NVIS) antenna for short-skip communications on 40 meters during the day?
A. A horizontal dipole placed between 1/10 and 1/4 wavelength above the ground
B. A vertical antenna placed between 1/4 and 1/2 wavelength above the ground
C. horizontal dipole placed at approximately 1/2 wavelength above the ground
D. A vertical dipole placed at approximately 1/2 wavelength above the ground

## Slide 5
G9D02
What is the feed point impedance of an end-fed half-wave antenna?
A. Very low
B. Approximately 50 ohms
C. Approximately 300 ohms
D. Very high

## Slide 6
G9D02
What is the feed point impedance of an end-fed half-wave antenna?
A. Very low
B. Approximately 50 ohms
C. Approximately 300 ohms
D. Very high

## Slide 7
G9D03
In which direction is the maximum radiation from a VHF/UHF “halo” antenna?
A. Broadside to the plane of the halo
B. Opposite the feed point
C. Omnidirectional in the plane of the halo
D. On the same side as the feed point

## Slide 8
G9D03
In which direction is the maximum radiation from a VHF/UHF “halo” antenna?
A. Broadside to the plane of the halo
B. Opposite the feed point
C. Omnidirectional in the plane of the halo
D. On the same side as the feed point

## Slide 9
G9D04
What is the primary function of antenna traps?
A. To enable multiband operation
B. To notch spurious frequencies
C. To provide balanced feed point impedance
D. To prevent out-of-band operation

## Slide 10
G9D04
What is the primary function of antenna traps?
A. To enable multiband operation
B. To notch spurious frequencies
C. To provide balanced feed point impedance
D. To prevent out-of-band operation

## Slide 11
G9D05
What is an advantage of vertically stacking horizontally polarized Yagi antennas?
A. It allows quick selection of vertical or horizontal polarization
B. It allows simultaneous vertical and horizontal polarization
C. It narrows the main lobe in azimuth
D. It narrows the main lobe in elevation

## Slide 12
G9D05
What is an advantage of vertically stacking horizontally polarized Yagi antennas?
A. It allows quick selection of vertical or horizontal polarization
B. It allows simultaneous vertical and horizontal polarization
C. It narrows the main lobe in azimuth
D. It narrows the main lobe in elevation

## Slide 13
G9D06
Which of the following is an advantage of a log-periodic antenna?
A. Wide bandwidth
B. Higher gain per element than a Yagi antenna
C. Harmonic suppression
D. Polarization diversity

## Slide 14
G9D06
Which of the following is an advantage of a log-periodic antenna?
A. Wide bandwidth
B. Higher gain per element than a Yagi antenna
C. Harmonic suppression
D. Polarization diversity

## Slide 15
G9D07
Which of the following describes a log-periodic antenna?
A. Element length and spacing vary logarithmically along the boom
B. Impedance varies periodically as a function of frequency
C. Gain varies logarithmically as a function of frequency
D. SWR varies periodically as a function of boom length

## Slide 16
G9D07
Which of the following describes a log-periodic antenna?
A. Element length and spacing vary logarithmically along the boom
B. Impedance varies periodically as a function of frequency
C. Gain varies logarithmically as a function of frequency
D. SWR varies periodically as a function of boom length

## Slide 17
G9D08
How does a “screwdriver” mobile antenna adjust its feed point impedance?
A. By varying its body capacitance
B. By varying the base loading inductance
C. By extending and retracting the whip
D. By deploying a capacitance hat

## Slide 18
G9D08
How does a “screwdriver” mobile antenna adjust its feed point impedance?
A. By varying its body capacitance
B. By varying the base loading inductance
C. By extending and retracting the whip
D. By deploying a capacitance hat

## Slide 19
G9D09
What is the primary use of a Beverage antenna?
A. Directional receiving for low HF bands
B. Directional transmitting for low HF bands
C. Portable direction finding at higher HF frequencies
D. Portable direction finding at lower HF frequencies

## Slide 20
G9D09
What is the primary use of a Beverage antenna?
A. Directional receiving for low HF bands
B. Directional transmitting for low HF bands
C. Portable direction finding at higher HF frequencies
D. Portable direction finding at lower HF frequencies

## Slide 21
G9D10
In which direction or directions does an electrically small loop (less than 1/3 wavelength in circumference) have nulls in its radiation pattern?
A. In the plane of the loop
B. Broadside to the loop
C. Broadside and in the plane of the loop
D. Electrically small loops are omnidirectional

## Slide 22
G9D10
In which direction or directions does an electrically small loop (less than 1/3 wavelength in circumference) have nulls in its radiation pattern?
A. In the plane of the loop
B. Broadside to the loop
C. Broadside and in the plane of the loop
D. Electrically small loops are omnidirectional

## Slide 23
G9D11
Which of the following is a disadvantage of multiband antennas?
A. They present low impedance on all design frequencies
B. They must be used with an antenna tuner
C. They must be fed with open wire line
D. They have poor harmonic rejection

## Slide 24
G9D11
Which of the following is a disadvantage of multiband antennas?
A. They present low impedance on all design frequencies
B. They must be used with an antenna tuner
C. They must be fed with open wire line
D. They have poor harmonic rejection

## Slide 25
G9D12
What is the common name of a dipole with a single central support?
A. Inverted V
B. Inverted L
C. Sloper
D. Lazy H

## Slide 26
G9D12
What is the common name of a dipole with a single central support?
A. Inverted V
B. Inverted L
C. Sloper
D. Lazy H

## Slide 27
G9D13
What is the combined vertically and horizontally polarized radiation pattern of a multi-wavelength, horizontal loop antenna?
A. A figure-eight, similar to a dipole
B. Four major loops with deep nulls
C. Virtually omnidirectional with a lower peak vertical radiation angle than a dipole
D. Radiation maximum is straight up

## Slide 28
G9D13
What is the combined vertically and horizontally polarized radiation pattern of a multi-wavelength, horizontal loop antenna?
A. A figure-eight, similar to a dipole
B. Four major loops with deep nulls
C. Virtually omnidirectional with a lower peak vertical radiation angle than a dipole
D. Radiation maximum is straight up